## Slide 1: WF on IAB-MT ACS,IBB and ACLR in FR1
ZTE
R4-2002490
3GPP TSG-RAN WG4 #94e
24th Feb.2020 – 6th Mar. 2020

## Slide 2: Background
Tentative agreement in discussion #82 of RAN4#94-e to define two classes for IAB-MT, out of which at least one is for macro/planned/high power deployments
Coexistence simulation results have been performed for layout 1 and layout 2 addressing HetNet deployment and homogenous deployment micro/planned
Coexistence results among companies differ between the layouts and there are two options proposed among companies, either to reuse FR1 UE ACLR requirement with lower minimum output power or reuse FR1 BS ACLR requirement with higher minimum output power.

## Slide 3: Agreement
    For IAB MT ACS requirement:
    reuse the BS requirement
    For IAB MT IBB requirment
    reuse the BS requirement
    For IAB-MT ACLR and minimum output power
    Option 1: 30dBc with minimum output power=10dBm
    Option 2: 45dBc with higher minimum output power =FFS
    Other options are not precluded.
    Minimum power requirement means that IAB-MT shall be able to transmit the widest declared channel BW with maximum possible number of RBs allocated for the said channel at the specified or lower power output power.

## Slide 4: References:
  R4-2001873 in-band blocking and ACS of IAB MT, Ericsson
  R4-2000972 simulation results for FR1 IAB coexistence study, ZTE
  R4-2001865 IAB-MT ACLR , Ericsson
  R4-2000977 In-band blocking for FR1 IAB MT, ZTE
  R4-1910838 FR1 IAB co-existence study,CMCC
  R4-1911735 simulation results for FR1 IAB coexistence study,ZTE
  R4-1912009 Coexistence simulation results for FR1 - layout 1,Ericsson
  R4-1912011 Coexistence simulation results for FR1 - layout 2,Ericsson
  R4-1914163 Simulation results for IAB in FR1,Huawei