## Slide 1: Way forward for NR UE URLLC performance requirements
Intel Corporation
3GPP TSG-RAN WG4 Meeting #94-e R4-2002428
Electronic Meeting, 24 Feb. – 6 Mar., 2020

## Slide 2: UE Performance requirements for high reliability (1)
Test parameters for UE FR1 URLLC demodulation requirement with high BLER
Agreements:
  TDD pattern: 7D1S2U, S=6D: 4G: 4U for 30 kHz SCS.
  MCS: MCS 5 in table 3.
  Propagation condition: TDLA30-10
  SCS & CBW:
    FDD: 15 kHz & 10 MHz
    TDD: 30 kHz & 40 MHz
  PDSCH configuration: Mapping type A, symbol length 12, starting symbol 2.
  Antenna configuration: 2x2 and 2x4, ULA low

## Slide 3: UE Performance requirements for high reliability (2)
Open Issues
Issue 1-5-1: Whether to define UE FR2 URLLC requirements for high reliability
  Option 1: Define requirements for FR2 (Ericsson, Intel, DoCoMo)
  Option 2: Do not define requirements for FR2. (Qualcomm, Huawei)
Issue 1-5-2: Target BLER
  Option 1: 1% BLER requirement (Intel, Ericsson, Huawei, QC)
  Option 2: 10% (Ericsson)
  Option 3: 0.1% (Ericsson, Huawei)
Issue 1-5-3: How to calculate the target BLER if HARQ activated
  Option 1: 1st transmission BLER (Ericsson)
  Option 2: BLER after all transmission if HARQ activated (Ericsson, Huawei, Intel, QC)

## Slide 4: UE Performance requirements for high reliability (3)
Open Issues (continued)
Issue 1-5-4: Target confidence level
  Option 1: 99% (Ericsson, Intel, Huawei, QC)
  Option 2: 95% (QC if 10% BLER)
Issue 1-5-5: PDSCH aggregation level
  FDD
    Option 1: 4 (Huawei, Intel)
    Option 2: 8 (NTT DoCoMo)
    Option 3: 2 (QC)
  TDD
    Option 1: 4 (NTT DoCoMo, Huawei, Ericsson, Intel)
    Option 2: 2 (QC)
Issue 1-5-6: Number of HARQ transmission
  Option 1: 1 (Ericsson, Intel)
  Option 2: 4 (Huawei, Qualcomm, Ericsson, DoCoMo, Intel)

## Slide 5: UE Performance requirements for low latency (1)
UE FR1 demodulation requirements for URLLC low latency
Agreements:
Verify PDSCH mapping Type B with PDSCH processing capability 2
  Slots to be scheduled:
    FDD: All DL slots with K1=0
    TDD: S slots with K1=0
  Starting symbol: 2
  Symbol length: 2, FFS on additional symbol length 4, 7
  Slot aggregation level: 1
Pre-emption indication
  Time frequency set: 14x1
  Number of symbols to be pre-emptied: 2, FFS on additional symbol length 4, 7
  Starting symbol to be pre-emptied: 3
  Test applicability for eMBB UE PI requirements: optional with UE capability signalling
  No URLLC PI performance requirements

## Slide 6: UE Performance requirements for low latency (2)
Open Issues for URLLC UE
Issue 2-5: Whether to introduce UE performance requirements in FR2 for URLLC
  Option 1: Introduce (Ericsson, Intel, DoCoMo)
  Option 2: Do not introduce (Huawei, QC)
Issue 2-5-1-1: TDD Pattern (30KHz SCS)
  Option 1: 7D1S2U, S=6D:4G:4U (Ericsson)
  Option 2a: DDDSUUDDDD, S=6D:4G:4U (DoCoMo (1st priority))
  Option 2b: DSUU, S=12D:2G (DoCoMo (2nd priority), Intel (1st priority ))
  Option 3: DDDSU, S=10D+2G+2U (Huawei, Qualcomm, Intel (2nd priority))
  Option 4: SU, S=12D+2G (Intel)
Issue 2-5-1-2: Number of HARQ Processes
  Option 1: 2 (Intel, DoCoMo)
  Option 2: 4 or 8 (DoCoMo)
Issue 2-5-1-3: Maximum number of HARQ transmissions
  Option 1: 1 (Ericsson, Intel, Huawei, QC)
  Option 2: >1
Issue 2-5-1-4: How to verify PDSCH processing capability 2 and type B mapping
  Option 1: Test together (Ericsson, Intel, Huawei, QC)
  Option 2: Test separately
Issue 2-5-1-5: Symbol length (L)
  Option 1: Also include 4os (DoCoMo)
  Option 2: Also include 7os with K1 = 1 (Ericsson)
  Option 3: Only 2os (Huawei, Intel, QC)
Issue 2-5-1-6: Other test parameters

## Slide 7: UE Performance requirements for low latency (3)
Open Issues for Preemption Indication
Issue 2-5-2-1: Pre-emption periodicity
  Option 1: 10% probability with non-fixed scheduling in RAN4 spec (similar to CSI-RS trigger for PMI testing, also 10% probability with fixed scheduling in RAN5 spec) within 1 radio frame (Ericsson, Qualcomm, Intel)
  Option 2: 1 slot (Huawei)
Issue 2-5-2-2: Channel Model
  Option 1: TDLC300-100 (Ericsson)
  Option 2: TDLA30-10 (Qualcomm, Huawei, Intel)
Issue 2-5-2-3: Antenna configuration
  Option 1: 2x2, ULA low (Ericsson)
  Option 2: 2x2 and 2x4, ULA low (Ericsson, Huawei, Intel, QC)
Issue 2-5-2-4: FRC
  Option 1: 16QAM with modified FRC (Ericsson)
  Option 2: QPSK (Qualcomm, Huawei)
  Option 3: New FRC with 64QAM (Intel)
Issue 2-5-2-5: Number of symbols to be pre-empted
  Option 1: Also include 4os
  Option 2: Also include 7os
  Option 3: Only 2os (Intel, Huawei, QC)

## Slide 8: CQI reporting requirements for support of CQI table 3 (1)
Issue 3-5-1-1: Propagation channel for CQI reporting
  Option 1: AWGN (Qualcomm, Huawei)
  Option 2: Fading channel (Intel)
Issue 3-5-1-2: Target BLER
  Option 1: 10^-3 (Huawei, Ericsson)
  Option 2: 10^-2 (Ericsson)
  Option 3: 10^-5 (Qualcomm, Intel (for AWGN))
  Option 4: No BLER metric in fading (Intel)
Issue 3-5-1-3: Test metric
  Option 1: Reuse existing BLER criteria test metrics (Huawei, Ericsson)
  Option 2: Percentage based of the maximum theoretical throughput (per MCS) (Ericsson)
  Option 3: Reuse existing BLER criteria test metrics with a minimum median CQI (Qualcomm)
  Option 4: TP ratio with follow CQI vs median CQI and CQI not in set metric (Intel)
Issue 3-5-1-4: Feasibility to define CQI reporting test case and FMCS case at the same SNR
  Option 1: Consider evaluating the UE performance with and without HARQ. If they are similar, we can have an applicability rule between CQI reporting test and FMCS test under AWGN to reduce the number of tests. (Qualcomm)