## Slide 1: 3GPP TSG-RAN WG4 Meeting #94-e R4-2002429 Electronic Meeting, Feb.24th – Mar.6th 2020
Huawei, HiSilicon
Way forward on NR URLLC BS performance requirements

## Slide 2: BS demodulation requirements for high reliability
BS FR1 URLLC PUSCH demodulation requirement for high reliability with higher BLER and/or confidence level:
  Agreements from the first round:
    Target BLER : 1%
    Target confidence level: 99%
    Calculate the target BLER after all transmission if HARQ activated.
    Number of HARQ transmission: 4
    MCS: MCS 5 in table 3
    Waveform: CP-OFDM
    TDD pattern:
      15kHz SCS: 3D1S1U, S=10D: 2G: 2U
      30kHz SCS: 7D1S2U, S=6D: 4G: 4U
    Symbol length is 14 with starting symbol 0
    DM-RS configuration: Type 1 with single-symbol: 1+1
    Antenna configuration: 1x2, ULA low
    Propagation condition: TDLB100-400
Define the PUCCH performance requirements for high reliability
  Agreements from the first round: Do not define the PUCCH performance requirements for high reliability.

## Slide 3: BS demodulation requirements for high reliability
BS FR1 URLLC PUSCH demodulation requirement for high reliability with higher BLER and/or confidence level:
  Agreements from the second round:
      Mapping Type: Type A and B with test applicability rule defined.
      SCS&BW for FR 1
        10MHz/15kHz
        40MHz/30kHz
        Other sets are not precluded

## Slide 4: BS demodulation requirements for high reliability
BS FR1 URLLC PUSCH demodulation requirement for high reliability with higher BLER and/or confidence level:
  Open issues for the next meeting:
    Issue 1: Whether to define BS FR2 URLLC performance requirements for high reliability
    Proposals
      Option 1: Do not define (Nokia, Samsung, Huawei, Intel?)
      Option 2: Define. (Ericsson, NTT DoCoMo)
    Issue 2: Test applicability rule for FR1 and FR2 performance requirements if both requirements are defined
    Proposals
      Option 1: Based on BS declaration of support FR1 or FR2 (Ericsson, Samsung)
      Option 2: If BS supports both FR1 and FR2, the performance requirements for both FR1 and FR2 should be tested (NTT DoCoMo)
    Recommended WF
      This depends on the discussion on Issue 4-5-1

## Slide 5: BS demodulation requirements for high reliability
BS FR1 URLLC PUSCH demodulation requirement for high reliability with higher BLER and/or confidence level:
  Open issues for the next meeting:
    Issue 3: PUSCH aggregation level
    Proposals
      Option 1: 2 (Samsung, Intel, Huawei)
      Option 2: 4 (Nokia, , Intel, Samsung if HARQ=1)
      Option 3: 2, 4 (Ericsson)
      Option 3: 8 (NTT DoCoMo)

## Slide 6: BS demodulation requirements for high reliability
BS FR1 URLLC PUSCH demodulation requirement for high reliability with higher BLER and/or confidence level:
  Open issues for the next meeting:
    Issue 4: Number of PRBs
    Proposals
      Option 1: 25 (Ericsson, Samsung)
      Option 2: Full bandwidth (NTT DoCoMo, Nokia, Intel)

## Slide 7: BS demodulation requirements for high reliability
BS URLLC PUSCH demodulation requirement for high reliability with higher BLER and/or confidence level:
  Open issues for the next meeting:
    Issue 5: SCS&BW for FR2 if FR2 will be defined
    Proposals for SCS & BW
      FR2:
        60kHz SCS
          Option 1: 50/100MHz (NTT DoCoMo)
          Option 2: No test (Nokia)
          Option 3: 50 MHz (Intel)
        120kHz SCS
          Option 1: 50/100/200MHz (NTT DoCoMo)
          Option 2: No test (Nokia)
          Option 3: 100 MHz (Intel)
      Note: this issue depends on issue 1.

## Slide 8: BS demodulation requirements for high reliability
BS FR1 URLLC PUSCH demodulation requirement for high reliability with higher BLER and/or confidence level:
  Open issues for the next meeting:
    Issue 6: Safety critical aspects:
    Proposals
    Proposal 11: If high reliability will be tested with BLER metric, add the following note to the test specification: “Note that this test procedure will only provide an indication to a certain confidence level that the target reliability requirements are likely to be satisfied, and it is assumed that for critical applications further testing would be done to ensure suitability of the equipment for the intended application.” (Nokia)
      Since the URLLC features of 5G NR will potentially be used in safety critical applications, the ultimately chosen statistical testing methodology for testing of these features must be verified by an independent body of experts/statisticians, before requirements and test can be used as basis for safety critical implementations. All statistical analysis and discussions provided in this meeting are to be taken as a best effort and is not to be taken as due diligence. (Nokia)
    Option 1: Need to be clarified in 3GPP specification. (Nokia)
    Option 2: No need to be clarified in 3GPP specification. (Huawei, Intel)

## Slide 9: BS demodulation requirements for high reliability
BS FR1 URLLC PUSCH demodulation requirement for high reliability with higher BLER and/or confidence level:
  Open issues for the next meeting:
    Issue 7: Whether to introduce DFT-s-OFDM:
      Proposals
        Option 1: No (Ericsson, Huawei, Samsung, Nokia, Intel)
        Option 2: Yes (NTT DoCoMo)
      Recommended WF

## Slide 10: BS demodulation requirements for low latency
BS FR1 URLLC demodulation requirements for PUSCH mapping Type B
  Agreements from the first round:
    Starting symbol: 0
    PUSCH aggregation level is 1.
    TDD pattern:
      15kHz SCS: 3D1S1U, S=10D: 2G: 2U
      30kHz SCS: 7D1S2U, S=6D: 4G: 4U
    Antenna configuration: 1x2.
    Waveform: CP-OFDM
    Channel condition: TDLC300-100 Low for FR1.
    No PUSCH performance requirements for UL transmission with grant free/UL configured grant.
  Agreements from the second round:
    Number of HARQ transmission: 1
    SCS/BW:
      15 kHz/10 MHz and 30 kHz/40 MHz with defined test applicability rule
      Other sets are not precluded

## Slide 11: BS demodulation requirements for low latency
BS URLLC demodulation requirements for PUSCH mapping Type B
  Open issues for the next meeting
    Issue 1: Whether to define requirements for BS FR2 URLLC performance requirements for low latency
    Proposals
      Option 1: Do not define (Samsung, Huawei, Nokia)
      Option 2: Define. (Ericsson, Intel, NTT DoCoMo)

## Slide 12: BS demodulation requirements for low latency
BS FR1 URLLC demodulation requirements for PUSCH mapping Type B
  Open issues for the next meeting
    Issue 2: Symbol length (L)
    Proposals
      Option 1: 4os (Intel, Samsung)
      Option 2: 2os (Huawei)
      Option 4: 7os (Nokia)
      Option 5: 2os and 7os (Ericsson, NTT DoCoMo)
    Issue 3: DM-RS configuration Type 1 with single symbol
    Proposals for symbol lengths of 5os or 7os based on the options in Issue 5-5-2
      Option 1:1+0 (Intel)
      Option 2: 1+1 (Nokia, Ericsson)
    Recommended WF
      The DM-RS configuration is also related to the agreed symbol length. As per TS 38.211 Table 6.4.1.1.3-3, symbol length L<= 4 only DMRS 1+0 is applicable. 4< L <=7, 1+0 and 1+1 are applicable.

## Slide 13: BS demodulation requirements for low latency
BS FR1 URLLC demodulation requirements for PUSCH mapping Type B
  Open issues for the 2nd round:
    Issue 4: MCS
    Proposals
      Option 1: MCS 5 from Table 3 (Samsung, Huawei, NTT DoCoMo, Nokia, Intel)
      Option 2: MCS 21 (658/1024) from Table 2 (Ericsson, DoCoMo?)
    Issue 5: Number of PRB
    Proposals
      Option 1: full bandwidth (Huawei, DoCoMo, Nokia, Samsung, Intel)
      Option 2: A fixed number of RB (Ericsson)

## Slide 14: BS demodulation requirements for low latency
BS FR1 URLLC demodulation requirements for PUSCH mapping Type B
  Open issues for the next meeting:
    Issue 6: Test metrics
    Proposals
      Option 1: 70% throughput (Huawei, DoCoMo, Samsung)
      Option 2: 10% BLER (= 90% throughput) (Ericsson, Nokia, Intel)
    Issue 7: Whether to introduce DFT-s-OFDM:
      Proposals
        Option 1: No (Ericsson, Huawei, Samsung, Nokia, Intel)
        Option 2: Yes (NTT DoCoMo)
      Recommended WF