## Slide 1: [Draft] Way forward on UE FR1 CA power imbalance requirements
NTT DOCOMO
3GPP TSG-RAN WG4 Meeting #94-e
Electronic Meeting, February 24 – March 6, 2020
RAN4#94e_#95_NR_perf_enh_Demod
R4-2002396

## Slide 2: Wayforward
For power imbalance FR1 intra-band contiguous CA test(s), followings are applied:
  Reference testing point: 85% of maximum throughput
  Measurement cell: Weaker power cell only
  CBW
    Option 1: Specify the following CA configurations. FFS necessity of further down selection
      Option 1A: 50+60, 50+80, 50+100, 60+60, 60+80, 60+100, 80+80 and 80+100 MHz
      Other options are not precluded
      Further discuss after Rel-16 core spec is finalized.
    Option 2: Define requirements for 5+5 MHz bandwidth for FDD+FDD CA, 10+10 MHz bandwidth for TDD+TDD CA, with the following test applicability
      The test is done for any one of the supported bandwidth combination, by using performance requirement for 5+5 MHz FDD+FDD CA or 10+10 MHz TDD+TDD CA.
      The tested PRBs shall be placed in the highest part for the CC with lower carrier frequency, and placed in the lowest part for the CC with higher carrier frequency.
    Option 3: Further discuss one of the following options for CBW combinations selection for NR CA requirements with power imbalance
      Option 3A: Choose one or several fixed CBW combination(s)
      Option 3B: Define generic methodology for selection of CBW combination among all CBW combinations in supported CA configurations.
    Option 3: Define generic methodology for selection of CBW combination among all CBW combinations in supported CA configurations
    Other options are not precluded
  PDSCH RB allocation
    Option 1: Full allocation
    Option 2: 25 PRBs for 15kHz FDD, 24 PRBs for 30kHz TDD
      There are 25 PRBs for 5MHz CBW with 15kHz SCS,
      and 24 PRBs for 10MHz CBW with 30kHz SCS
    Other options are not precluded
(For information) CBW Option2

## Slide 3: Wayforward
For power imbalance EN-DC test(s),
  Start the discussion to define the requirements for FR1 intra-band contiguous and non-contiguous EN-DC with power imbalance between LTE and NR carrier from next RAN4 meeting based on the decision in next RAN plenary meeting.
    The objectives in WID will be revised in next RAN plenary meeting.
  The value of power imbalance,
    6dB for contiguous EN-DC
    FFS for non-contiguous EN-DC. Discussion is needed.
Whether to define power imbalance requirement for FR1 intra-band EN-DC
  Option 1: Yes. Power imbalance requirement should be introduced to ensure correct UE implementation in intra-band contiguous and non-contiguous EN-DC scenario in FR1.
    NR carrier has lower power of 6dB than LTE carrier, and only throughput NR carrier is tested.
  Option 2: No
  Option 3: Define requirements for intra-band contiguous EN-DC with 6dB power imbalance between LTE and NR carrier. Whether to define the requirements for intra-band non-contiguous EN-DC can be discussed further.

## Slide 4: Wayforward
For power imbalance test for FR1 intra-band contiguous NR-CA, following parameters are applied:
Parameters | Value
Duplex mode | Case #1: FDD+FDD CA w/ 15kHz SCS Case #2: TDD+TDD CA w/ 30kHz SCS(TDD pattern: Option 1: 7D1S2U(S=6d4s4u); Option 2: DDDSU+DDSUU (S=10d2s2u))
TDD pattern | Option 1: 7D1S2U(S=6d4s4u) Option 2: DDDSU+DDSUU (S=10d2s2u) Option 3: DDDSUUDDDD (S=6d4s4u)
PDSCH configurations | Mapping type: Type A K0: 0 PRB bundling size: Option 1: WB; Option 2: 2 PRBs
PDSCH DMRS configurations | DMRS type: Type 1 Number of additional DMRS: 1 (i.e., 1+1)
Transmission rank | Rank 1
MCS | MCS: 64QAM Code rate: Option 1: MCS19, 64QAM with 0.5 code rate; Option 2: FFS
Max number of HARQ transmission | 1 (RV = {0})
PDCCH allocation | Option 1: Symbol #0; Option 2: Symbol #0 and #1
MIMO configuration | Option 1: 2x2 and 2x4; Option 2: 1x2 and 1x4
Propagation condition | Static propagation condition without external noise
Precoding configuration | SP Type I, Random per slot with PRB bundling granularity

## Slide 5: Wayforward
For power imbalance test for FR1 non-contiguous EN-DC is introduced with following parameters:
Parameters | Value
Duplex mode | LTE+TDD w/ 30kHz SCS (TDD pattern: Option 1: 7D1S2UU (S=6d4s4u); Option 2: DDDSU+DDSUU (S=10d2s2u))
PDSCH configurations | Mapping type: Type A K0: 0 PRB bundling size: Option 1: WB; Option 2: PRBs
PDSCH DMRS configurations | DMRS type: Type 1 Number of additional DMRS: 1 (i.e., 1+1)
Transmission rank | Rank 1
MCS | MCS: 64QAM Code rate: Option 1: MCS19, 64QAM with 0.5 code rate; Option 2: FFS
Max number of HARQ transmission | 1 (RV = {0})
PDCCH allocation | Option 1: Symbol #0; Option 2: Symbol #0 and #1
MIMO configuration | Option 1: 2x2 and 2x4; Option 2: 1x2 and 1x4
Propagation condition | Static propagation condition without external noise
Precoding configuration | SP Type I, Random per slot with PRB bundling granularity