3GPP TSG-RAN WG4 Meeting #94-e		R4-2002392

E-meeting, 24 February – 6 March, 2020

Agenda item:	8.18.1.1

Source:	Intel Corporation

Title:	Simulation assumptions for NR normal CA UE performance requirements

Document for:	Approval

# Introduction

This paper provides detailed simulation assumptions for link level results alignment for the RAN4 #94 meeting, based on agreements from [1], [2], [3] and [4].

# Simulation assumptions

## SCS and Channel bandwidth

Single carrier SCS

- FR1 FDD: 15kHz

- FR1 TDD: 15 kHz and 30kHz

- FR2: 120 kHz

Single carrier channel bandwidth

- FR1 FDD 15 kHz and TDD 15 kHz: 5, 10, 15, 20, 25, 30, 40, 50 MHz

- FR1 TDD 30 kHz: 5, 10, 15, 20, 25, 30, 40, 50, 60, 80, 90, 100 MHz

- FR2: 50, 100, 200, 400 MHz

## Test parameters

TDD UL-DL pattern:

- FR1 SCS 15 kHz: 3D1S1U with S=10:2:2

- FR1 SCS 30 kHz: 7D1S2U with S=6:4:4

- FR2 SCS 120 kHz: 3D1S1U with S=10:2:2

SSB configuration: Periodicity 20 ms, Allocated in first slot within 20ms

PDSCH configuration

- FR1 FDD: Type A, Start symbol 2, Duration 12

- FR1 TDD 15 kHz:

  - Full DL slots: Type A, Start symbol 2, Duration 12

  - Special slots: Type A, Start symbol 2, Duration 8

- FR1 TDD 30 kHz:

  - Full DL slots: Type A, Start symbol 2, Duration 12

  - Special slots: Type A, Start symbol 2, Duration 4

- FR2 120 kHz:

  - Full DL slots: Type A, Start symbol 1, Duration 13

  - Special slots: Type A, Start symbol 1, Duration 9

DMRS configuration for FR1 and FR2

- Type 1, 1 additional DMRS, Single symbol

PTRS configuration for FR2: Frequency density 2, Time density 1

TRS configuration for FR1 and FR2: 20 ms periodicity, 2 slots, Offset 10 ms

HARQ process number:

- FR1 FDD: 4 (baseline for simulation alignment), 6, 8

- FR1 TDD 15 kHz SCS: 8 (baseline for simulation alignment), 6

- FR1 TDD 30 kHz SCS: 8 (baseline for simulation alignment), 10, 12, 16

- FR2 120 kHz SCS: 8

FRC:

- FR1: Rank 2 with MCS 13 (16QAM, CR 1/2) for 2Rx and 4Rx

- FR2:

  - Option 1: Rank 1 with MCS 13 (16QAM, CR 1/2)

  - Option 2: Rank 2 with MCS 10 (16QAM, CR 1/3)

PRB bundling: 2

Precoding model:

- FR1: Random Precoding, per slot, PRB bundling granularity (codebook configuration Single panel Type 1)

- FR2: Random Precoding, per slot, WB granularity (codebook configuration Single panel Type 1)

Receiver type: MMSE-IRC

Propagation condition:

- FR1: TDLA30-10

- FR2: TDLA30-75

Antenna correlation for MMSE-IRC: ULA Low

Throughput test point: 70% of max TP

# FRC

## FR1 FDD 15 kHz

| Parameter | Unit | Value |
| --- | --- | --- |
| Reference channel |  | R.FDD 5 MHz | R.FDD 10 MHz | R.FDD 15 MHz | R.FDD 20 MHz | R.FDD 25 MHz | R.FDD 30 MHz | R.FDD 40 MHz | R.FDD 50 MHz |
| Channel bandwidth | MHz | 5 | 10 | 15 | 20 | 25 | 30 | 40 | 50 |
| Subcarrier spacing | kHz | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 |
| Number of allocated resource blocks | PRBs | 25 | 52 | 79 | 106 | 133 | 160 | 216 | 270 |
| Number of consecutive PDSCH symbols |  | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |
| Allocated slots per 2 frames | Slots | 19 | 19 | 19 | 19 | 19 | 19 | 19 | 19 |
| MCS table |  | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM |
| MCS index |  | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 |
| Modulation |  | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM |
| Target Coding Rate |  | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 |
| Number of MIMO layers |  | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |
| Number of DMRS REs |  | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |
| Overhead for TBS determination |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Information Bit Payload per Slot |  |  |  |  |  |  |  |  |  |
| For Slot i = 0 | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slots i = 1,…, 19 | Bits | 12552 | 26120 | 39936 | 53288 | 67584 | 79896 | 108552 | 135296 |
| Transport block CRC per Slot |  |  |  |  |  |  |  |  |  |
| For Slot i = 0 | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slots i = 1,…, 19 | Bits | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 |
| Number of Code Blocks per Slot |  |  |  |  |  |  |  |  |  |
| For Slot i = 0 | CBs | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slots i = 1,…, 19 | CBs | 2 | 4 | 5 | 7 | 9 | 10 | 13 | 17 |
| Binary Channel Bits Per Slot |  |  |  |  |  |  |  |  |  |
| For Slot i = 0 | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slots i = 10, 11 | Bits | 25200 | 52416 | 79632 | 106848 | 134064 | 161280 | 217728 | 272160 |
| For Slots i = 1,…, 9, 12, …, 19 | Bits | 26400 | 54912 | 83424 | 111936 | 140448 | 168960 | 228096 | 285120 |
| Max. Throughput averaged over 2 frames | Mbps | 11.924 | 24.814 | 37.939 | 50.624 | 64.205 | 75.901 | 103.124 | 128.531 |
| Note 1: SS/PBCH block is transmitted in slot #0 with periodicity 20 ms Note 2: Slot i is slot index per 2 frames |

## FR1 TDD 15 kHz

| Parameter | Unit | Value |
| --- | --- | --- |
| Reference channel |  | R.TDD 5 MHz | R.TDD 10 MHz | R.TDD 15 MHz | R.TDD 20 MHz | R.TDD 25 MHz | R.TDD 30 MHz | R.TDD 40 MHz | R.TDD 50 MHz |
| Channel bandwidth | MHz | 5 | 10 | 15 | 20 | 25 | 30 | 40 | 50 |
| Subcarrier spacing | kHz | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 |
| Number of allocated resource blocks | PRBs | 25 | 52 | 79 | 106 | 133 | 160 | 216 | 270 |
| Number of consecutive PDSCH symbols |  |  |  |  |  |  |  |  |  |
| For Slot i, if mod(i, 5) = 3 for i from {0,…,19} |  | 8 | 8 | 8 | 8 | 8 | 8 | 8 | 8 |
| For Slot i, if mod(i, 5) = {0,1,2} for i from {1,…,19} |  | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |
| Allocated slots per 2 frames | Slots | 15 | 15 | 15 | 15 | 15 | 15 | 15 | 15 |
| MCS table |  | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM |
| MCS index |  | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 |
| Modulation |  | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM |
| Target Coding Rate |  | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 |
| Number of MIMO layers |  | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |
| Number of DMRS REs |  |  |  |  |  |  |  |  |  |
| For Slot i, if mod(i, 5) = 3 for i from {0,…,19} |  | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |
| For Slot i, if mod(i, 5) = {0,1,2} for i from {1,…,19} |  | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |
| Overhead for TBS determination |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Information Bit Payload per Slot |  |  |  |  |  |  |  |  |  |
| For Slot i = 0 | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slot i, if mod(i, 5) = 3 for i from {0,…,19} | Bits | 8064 | 16896 | 25608 | 33816 | 43032 | 51216 | 69672 | 86040 |
| For Slot i, if mod(i, 5) = {0,1,2} for i from {1,…,19} | Bits | 12552 | 26120 | 39936 | 53288 | 67584 | 79896 | 108552 | 135296 |
| Transport block CRC per Slot |  |  |  |  |  |  |  |  |  |
| For Slot i = 0 | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slot i, if mod(i, 5) = 3 for i from {0,…,19} | Bits | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 |
| For Slot i, if mod(i, 5) = {0,1,2} for i from {1,…,19} | Bits | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 |
| Number of Code Blocks per Slot |  |  |  |  |  |  |  |  |  |
| For Slot i = 0 | CBs | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slot i, if mod(i, 5) = 3 for i from {0,…,19} | CBs | 1 | 3 | 4 | 5 | 6 | 7 | 9 | 11 |
| For Slot i, if mod(i, 5) = {0,1,2} for i from {1,…,19} | CBs | 2 | 4 | 5 | 7 | 9 | 10 | 13 | 17 |
| Binary Channel Bits Per Slot |  |  |  |  |  |  |  |  |  |
| For Slot i = 0 | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slots i = 10, 11 | Bits | 25200 | 52416 | 79632 | 106848 | 134064 | 161280 | 217728 | 272160 |
| For Slot i, if mod(i, 5) = 3 for i from {0,…,19} | Bits | 16800 | 34944 | 53088 | 71232 | 89376 | 107520 | 145152 | 181440 |
| For Slot i, if mod(i, 5) = {0,1,2} for i from {1,…,9,12,…,19} | Bits | 26400 | 54912 | 83424 | 111936 | 140448 | 168960 | 228096 | 285120 |
| Max. Throughput averaged over 2 frames | Mbps | 8.516 | 17.745 | 27.086 | 36.072 | 45.778 | 54.186 | 73.638 | 91.621 |
| Note 1: SS/PBCH block is transmitted in slot #0 with periodicity 20 ms Note 2: Slot i is slot index per 2 frames |

## FR1 TDD 30 kHz

| Parameter | Unit | Value |
| --- | --- | --- |
| Reference channel |  | R.TDD 5 MHz | R.TDD 10 MHz | R.TDD 15 MHz | R.TDD 20 MHz | R.TDD 25 MHz | R.TDD 30 MHz | R.TDD 40 MHz | R.TDD 50 MHz | R.TDD 60 MHz | R.TDD 80 MHz | R.TDD 90 MHz | R.TDD 100 MHz |
| Channel bandwidth | MHz | 5 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 60 | 80 | 90 | 100 |
| Subcarrier spacing | kHz | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 | 30 |
| Allocated resource blocks | PRBs | 11 | 24 | 38 | 51 | 65 | 78 | 106 | 133 | 162 | 217 | 245 | 273 |
| Number of consecutive PDSCH symbols |  |  |  |  |  |  |  |  |  |  |  |  |  |
| For Slot i, if mod(i, 10) = 7 for i from {0,…,39} |  | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 | 4 |
| For Slot i, if mod(i, 10) = {0,1,2,3,4,5,6} for i from {1,…,39} |  | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |
| Allocated slots per 2 frames |  | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 31 | 31 |
| MCS table |  | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM |
| MCS index |  | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 |
| Modulation |  | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM |
| Target Coding Rate |  | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 | 0.48 |
| Number of MIMO layers |  | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |
| Number of DMRS REs |  |  |  |  |  |  |  |  |  |  |  |  |  |
| For Slot i, if mod(i, 10) = 7 for i from {0,…,39} |  | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 |
| For Slot i, if mod(i, 10) = {0,1,2,3,4,5,6} for i from {1,…,39} |  | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |
| Overhead for TBS determination |  | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 |
| Information Bit Payload per Slot |  |  |  |  |  |  |  |  |  |  |  |  |  |
| For Slots 0 and Slot i, if mod(i, 10) = {8,9} for i from {0,…,39} | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slot i, if mod(i, 10) = 7 for i from {0,…,39} | Bits | 1800 | 3840 | 6144 | 8192 | 10504 | 12552 | 16896 | 21504 | 26120 | 34816 | 38936 | 44040 |
| For Slot i, if mod(i, 10) = {0,1,2,3,4,5,6} for i from {1,…,39} | Bits | 5504 | 12040 | 18960 | 25608 | 32776 | 38936 | 53288 | 67584 | 81976 | 110632 | 122976 | 139376 |
| Transport block CRC per Slot |  |  |  |  |  |  |  |  |  |  |  |  |  |
| For Slots 0 and Slot i, if mod(i, 10) = {8,9} for i from {0,…,39} | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slot i, if mod(i, 10) = 7 for i from {0,…,39} | Bits | 16 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 |
| For Slot i, if mod(i, 10) = {0,1,2,3,4,5,6}for i from {1,…,39} | Bits | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 |
| Number of Code Blocks per Slot |  |  |  |  |  |  |  |  |  |  |  |  |  |
| For Slots 0 and Slot i, if mod(i, 10) = {8,9} for i from {0,…,39} | CBs | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slot i, if mod(i, 10) = 7 for i from {0,…,39} | CBs | 1 | 1 | 1 | 1 | 2 | 2 | 3 | 3 | 4 | 5 | 5 | 6 |
| For Slot i, if mod(i, 10) = {0,1,2,3,4,5,6} for i from {1,…,39} | CBs | 1 | 2 | 3 | 4 | 4 | 5 | 7 | 9 | 10 | 14 | 15 | 17 |
| Binary Channel Bits Per Slot |  |  |  |  |  |  |  |  |  |  |  |  |  |
| For Slots 0 and Slot i, if mod(i, 10) = {8,9} for i from {0,…,39} | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slots i = 20, 21 | Bits | 11088 | 24192 | 38304 | 51408 | 65520 | 78624 | 106848 | 134064 | 163296 | 218736 | 246960 | 275184 |
| For Slot i, if mod(i, 10) = 7 for i from {0,…,39} | Bits | 3696 | 8064 | 12768 | 17136 | 21840 | 26208 | 35616 | 44688 | 54432 | 72912 | 82320 | 91728 |
| For Slot i, if mod(i, 10) = {0,1,2,3,4,5,6} for i from {1,…,19,22,…,39} | Bits | 11616 | 25344 | 40128 | 53856 | 68640 | 82368 | 111936 | 140448 | 171072 | 229152 | 258720 | 288288 |
| Max. Throughput averaged over 2 frames | Mbps | 7.790 | 17.022 | 26.825 | 36.209 | 46.348 | 55.074 | 75.318 | 95.539 | 115.892 | 156.316 | 173.805 | 196.966 |
| Note 1: SS/PBCH block is transmitted in slot #0 with periodicity 20 ms Note 2: Slot i is slot index per 2 frames |

## FR2 TDD 120 kHz

| Parameter | Unit | Value |
| --- | --- | --- |
| Reference channel |  | R.TDD-1 50 MHz | R.TDD-1 100 MHz | R.TDD-1 200 MHz | R.TDD-1 400 MHz | R.TDD-2 50 MHz | R.TDD-2 100 MHz | R.TDD-2 200 MHz | R.TDD-2 400 MHz |
| Channel bandwidth | MHz | 50 | 100 | 200 | 400 | 50 | 100 | 200 | 400 |
| Subcarrier spacing | kHz | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 |
| Allocated resource blocks | PRBs | 32 | 66 | 132 | 264 | 32 | 66 | 132 | 264 |
| Number of consecutive PDSCH symbols |  |  |  |  |  |  |  |  |  |
| For Slot i, if mod(i, 5) = 3 for i from {0,…, 159} |  | 9 | 9 | 9 | 9 | 9 | 9 | 9 | 9 |
| For Slot i, if mod(i, 5) = {0,1,2} for i from {1,…,159} |  | 13 | 13 | 13 | 13 | 13 | 13 | 13 | 13 |
| Allocated slots per 2 frames |  | 127 | 127 | 127 | 127 | 127 | 127 | 127 | 127 |
| MCS table |  | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM | 64QAM |
| MCS index |  | 13 | 13 | 13 | 13 | 10 | 10 | 10 | 10 |
| Modulation |  | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM | 16QAM |
| Target Coding Rate |  | 0.48 | 0.48 | 0.48 | 0.48 | 0.33 | 0.33 | 0.33 | 0.3 |
| Number of MIMO layers |  | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 |
| Number of DMRS REs |  |  |  |  |  |  |  |  |  |
| For Slot i, if mod(i, 5) = 3 for i from {0,…, 159} |  | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |
| For Slot i, if mod(i, 5) = {0,1,2} for i from {1,…,159} |  | 12 | 12 | 12 | 12 | 12 | 12 | 12 | 12 |
| Overhead for TBS determination |  | 6 | 6 | 6 | 6 | 6 | 6 | 6 | 6 |
| Information Bit Payload per Slot |  |  |  |  |  |  |  |  |  |
| For Slots 0 and Slot i, if mod(i, 5) = 4 for i from {0,…,159} | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slot i, if mod(i, 5) = 3 for i from {0,…, 159} | Bits | 5504 | 11272 | 22536 | 45096 | 7680 | 15880 | 31752 | 63528 |
| For Slot i, if mod(i, 5) = {0,1,}) for i from {1,…,159} | Bits | 8456 | 17424 | 34816 | 69672 | 11784 | 24072 | 48168 | 96264 |
| Transport block CRC per Slot |  |  |  |  |  |  |  |  |  |
| For Slots 0 and Slot i, if mod(i, 5) = 4 for i from {0,…,159} | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slot i, if mod(i, 5) = 3 for i from {0,…, 159} | Bits | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 |
| For Slot i, if mod(i, 5) = {0,1,}) for i from {1,…,159} | Bits | 24 | 24 | 24 | 24 | 24 | 24 | 24 | 24 |
| Number of Code Blocks per Slot |  |  |  |  |  |  |  |  |  |
| For Slots 0 and Slot i, if mod(i, 5) = 4 for i from {0,…,159} | CBs | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slot i, if mod(i, 5) = 3 for i from {0,…, 159} | CBs | 1 | 2 | 3 | 6 | 1 | 2 | 4 | 8 |
| For Slot i, if mod(i, 5) = {0,1,2} for i from {1,…,159} | CBs | 2 | 3 | 5 | 9 | 2 | 3 | 6 | 12 |
| Binary Channel Bits Per Slot |  |  |  |  |  |  |  |  |  |
| For Slots 0 and Slot i, if mod(i, 5) = 4 for i from {0,…,159} | Bits | N/A | N/A | N/A | N/A | N/A | N/A | N/A | N/A |
| For Slots i = 80, 81 | Bits | 16960 | 34980 | 69960 | 139920 | 33920 | 69960 | 139920 | 279840 |
| For Slot i, if mod(i, 5) = 3 for i from {0,…, 159} | Bits | 11840 | 24420 | 48840 | 97680 | 23680 | 48840 | 97680 | 195360 |
| For Slot i, if mod(i, 5) = {0,1,2} for i from {1,…,79,82,…,159} | Bits | 17728 | 36564 | 73128 | 146256 | 35456 | 73128 | 146256 | 292512 |
| Max. Throughput averaged over 2 frames | Mbps | 48.972 | 100.799 | 201.434 | 403.096 | 68.262 | 139.750 | 279.601 | 558.899 |
| Note 1: SS/PBCH block is transmitted in slot #0 with periodicity 20 ms Note 2: Slot i is slot index per 2 frames |

# References

- R4-1910046 “Way forward on PDSCH CA normal demodulation requirements”, Intel, RAN4 #92, August 2019.

- R4-1912832 “Way forward on PDSCH CA normal demodulation requirements”, Intel, RAN4 #92bis, October 2019.

- R4-1915861 “Way forward on PDSCH CA normal demodulation requirements”, Intel, RAN4 #93, November 2019.

- R4-2002391 “Way forward on PDSCH CA normal demodulation requirements”, Intel, RAN4 #94-e, February 2020.