## Slide 1: WF on finalizing FR2 MIMO OTA
CAICT
3GPP TSG-RAN WG4 Meeting #94-e R4-2002471
Electronic Meeting, Feb.24th – Mar.6th 2020
Agenda item: 10.2.1
Document for: Approval

## Slide 2: FR2 MIMO OTA
Feasible SNR ranges for 3D MPAC
  SNR upper bound is not suggested to be added in the TR. For system validation purpose, this value can be further discussed in WI phase.
  Feasible SNR range is encouraged to be discussed.
System for FR2 MIMO OTA
  The group shall focus on finalizing the test method of the agreed FR2 3D-MPAC (using a common probe layout and a total number of 6 probes)
  Implementing the agreed 3D MPAC using IFF probes is not precluded (as long as same probe configuration and same number of probes is used)
  Alternate probe configurations (different locations and different number of probes) regardless of probe implementation (conventional probes or IFF) is FFS and can be further discussed in the WI
  Re-positioning of the NR MIMO probes can be further discussed in the WI to align the probes with NR FR2 RRM probe configurations
FR2 3D-MPAC layout
  The number of probes for FR2 3D-MPAC system is 6.
  CE vendors align on the 6 probes location before next RAN4 e-meeting.

## Slide 3: FR2 MIMO OTA
Performance metrics
  option1: averaging of the [xx] measured sensitivity points, how to select the points is FFS.
  option2: sensitivity value at the [xx] percentile of the CCDF.
  The value of [xx] shall be defined in potential WI phase.
initial phases for channel models
  Study if this will induce large lab misalignment in the WI phase.
FR2 dynamic testing
  A dynamic geometry-based MIMO OTA testing approach has not been thoroughly studied as the second priority in the SI. However, this is not an open issue preventing to close the SI.
  Enhancement of FR2 MIMO OTA test method with dynamic geometry-based RRM and throughput testing is encouraged in a new SI.
  Clarification of the FR2 test method is not for dynamic testing may be added in the TR38.827 test method part. Example text proposal “the test method and procedure in session 6.2.3 is for FR2 static testing, advanced dynamic testing method with new performance metrics is FFS”
FR2 system validation
  Finalize PSP validation procedure and QoQZ procedure next RAN4 e-meeting