3GPP TSG-RAN WG4 Meeting #94-e	R4-2000xxx
Electronic Meeting, 24 Feb. – 6 Mar., 2020

Agenda item:	10.2.1

Source:	Qualcomm Incorporated

Title:	TP to TR 38.827 v1.1.0 on dynamic testing

Document for:	Approval

# 1	Introduction

This text proposal aims to add clarification on dynamic testing in the TR 38.827.

# 2	References

- R4-2000894,TR 38.827 v0.5.0, CAICT

# 3	Text Proposal

The following text changes are proposed.

========================== Start of change ==========================

### 6.2.3	Baseline setup for FR2

<Editor’s note: clause content is FFS>

The test method and procedure in this session is for FR2 static testing. Advanced dynamic testing method with new performance metrics is FFS.

Note: Static test method means DUT is tested under a static test environment in which there is no update on the DUT’s orientation and position during a test iteration. Advanced dynamic testing method may enable, e.g. DUT’s orientation and/or position, etc, during a test iteration, details of which are FFS.

========================== End of change ==========================