# 3GPP TSG-RAN WG4 Meeting #94-e	R4-2000571

# Electronic Meeting, 24th Feb. – 6th Mar. 2020

Source: 	vivo

Title: 	TP on channel bandwidths for NR V2X licensed band n38

Agenda Item:	8.4.3.1

Document for:	Approval

# Introduction

In RAN4#93, [1] capturing licensed band n38 for NR V2X Communication was approved. According to discussion paper [2], channel bandwidths supported by band n38 are revised in Annex.

# Reference

[1]	R4-1916144, TP on general Tx/Rx requirements for NR V2X UE at licensed bands, LGE, RAN4#93.

[2]   R4-2000570，Channel bandwidths for NR V2X licensed bands, vivo, RAN4#94-e

# Annex: TP for channel arrangement in TR38.886

============================ Start of TP ============================

# 7	Operating bands and channel arrangement

## 7.1	Operating bands

### 7.1.1	Operating bands in FR1

NR V2X communication is designed to operate in the operating bands in FR1 defined in Table 7.1.1-1.

Table 7.1.1-1 NR V2X operating bands in FR1

| NR V2X Operating Band | Sidelink (SL) Transmission operating band | Sidelink (SL) Reception operating band | Duplex Mode | Interface |
| --- | --- | --- | --- | --- |
|  | FUL_low – FUL_high | FDL_low – FDL_high |  |  |
| n381 | 2570 MHz | - | 2620 MHz | 2570 MHz | - | 2620 MHz | TDD | PC5 |
| n47 | 5855 MHz | - | 5925 MHz | 5855 MHz | - | 5925 MHz | TDD | PC5 |

<Unchanged sections are omitted>

## 7.2	Channel bandwidth

### 7.2.1	Channel bandwidth in FR1

The NR V2X Communication channel bandwidths and operating bands are shown in Table 7.2.1-1. The same (symmetrical) channel bandwidth is specified for both the TX and RX path.

Table 7.2.1-1 NR V2X Communication channel bandwidth

| NR V2X band / V2X channel bandwidth |
| --- |
| NR V2X Operating Band | SCS kHz | 10 MHz | 20 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz |
| n38 | 15 | Yes | Yes |  | Yes |  |  |  |  |  |
|  | 30 | Yes | Yes |  | Yes |  |  |  |  |  |
|  | 60 | Yes | Yes |  | Yes |  |  |  |  |  |
| n47 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |
|  | 30 | Yes | Yes | Yes | Yes |  |  |  |  |  |
|  | 60 | Yes | Yes | Yes | Yes |  |  |  |  |  |

============================ End of TP ============================