## Slide 1: Summary of issues related to power class ambiguities and tx div
Qualcomm Incorporated
R4-2004821
3GPP TSG-RAN4 #92Bis-e
Online, 20th – 30th April 2020

## Slide 2: Background
RAN1 allowed specification transparent tx diversity 2017
  Intention was not to specify what kind of signal processing techniques UE should use
Some companies interpret that as also spec transparent in RAN4
When CR to enable transparent tx diversity was proposed, TE vendors expressed their concerns on enabling such feature since it requires TE to detect automatically if UE use tx diversity or not
Other issue is that the LTE always assumed that for 2-tx-port device, the power per tx chain is backed of 3 dB from its maximum power thus emissions will always be also 3 dB lower

## Slide 3: Terminology
23+23 dBm device = UE which intends to declare PC2 but does not have 26 dBm PA
Tx diversity = using more than one antenna for tx
Antenna port = Logical port name, originates from RAN1. UL MIMO uses two logical ports
Antenna connector = physical antenna connector in UE. RAN4 term. LTE mapping of logical port = antenna connector
TAV = (Logical) Transmit Antenna Port Virtualization. A scheme what UE uses to map single logical antenna ports to two or more antenna connectors

## Slide 4: Tx diversity / Transmit Antenna Port virtualization
UE is allowed to implement or not implement and transmit with two tx chains even if network configures UE for single logical antenna port
Currently RAN4 specifications and therefore RAN5 test specification assume logical port = antenna connector mapping
To change this, RAN4 needs to change general terminology so that “power and emissions are summed”
  Testing maybe done per port but requirements must apply to sum of transmissions from each port
Controversies
  TE thinks this is major change in ran5 and Rel-15
  Some companies think TAV is part of UL MIMO
There are numerous agreement not to specify tx diversity

## Slide 5: UL MIMO emissions
Because of LTE antenna port to antenna connector mapping, specification said emissions are valid for each connector thus enabling UE to exceed emissions by 3 dB when summed
Regulation is applicable to UE level
Controversy is that NR UL MIMO specification has been like this until today and correcting this would be tightening against previous 3GPP specification
  But UE still has to meet regulatory emissions so it is unclear why this is problem

## Slide 6: UL MIMO power class ambiguity
There was an early agreement that 23 + 23 dBm device is PC2 UL MIMO
Unfortunately fall back to single port operation behavior was not properly discussed
In order for this type of UE to produce 26 dBm when configured to single logical port, UE needs to implement TAV
UE shares power class declaration between single port and UL MIMO
Controversy is that
  Some companies think that this kind of UE is PC2 UE and it is allowed to fall back to PC3 operation when configured to single port
  Other companies think that this is PC3 UE that behaves as PC2 when configured for two logical ports
If principle that PC2 UE has to be able to produce 26 dBm regardless of how many ports it is configured is agreed, and no TAV is specified, this is not an issue anymore

## Slide 7: EN-DC power class ambiguity
When 23+23 dBm UE that implement TAV is configured for EN-DC for intra-band, it re-purposes the other TX chain and PA for LTE
In UE declares PC2 for EN-DC and also PC2 for NR SA, and PC3 for LTE, network will assume UE can do 23 dBm in LTE, 26 dBm in NR up to 26 dBm combined
In practice, since NR 26 dBm was achieved by means of TAV, UE can do only up to 23 dBm in NR
Controversy is that
  some companies think this drop in power class should be allowed by specification
  others think this kind of UE is not PC2 for EN-DC
Additionally, if RAN4 specifications do not acknowledge TAV, this should not be discussed