## Slide 1
3GPP TSG-RAN WG4 Meeting #94-e-Bis R4-2004965
Electronic Meeting, 20 – 30 Apr, 2020
Motivation for new WI on air-to-ground network for NR
CMCC

## Slide 2: Justification
Air-to-ground (ATG) network refers to in-flight connectivity technique, using ground-based cell towers that send signals up to an aircraft’s antenna(s) of onboard ATG terminal. As a plane travels into different sections of airspace, the onboard ATG terminal automatically connects to the cell with strongest received signal power, just as a mobile phone does on the ground
Scenario: to provide broadband access for civil aircrafts
  ATG gNB deployed on the ground, with antennas pointing upward to form an aerial cell
  Aircraft as a special UE
  Aircraft to ATG gNB: 5G air interface
  Aircraft to passengers: WiFi access

## Slide 3: Justification
There are several regional commercial or trial in-flight networks based on hybrid techniques of ATG and satellite communication, such as Gogo’s commercial network in USA, Inmarsat’s commercial network in Europe, and CMCC’s trial network in China. Regarding the hybrid network, satellite link focus on providing every-where connectivity (e.g., when cross the sea), while ATG link focus on providing high-quality data services for all service available areas (e.g., inland and coastline area) considering its advantage of high throughput, low propagation delay, and low cost over satellite’s application
In RAN#86 meeting, the new WID (RP-193234) solutions for NR to support non-terrestrial networks (NTN) was approved. The NTN work item aims to specify the enhancements identified for NR NTN (non-terrestrial networks) especially LEO and GEO with implicit compatibility to support HAPS (high altitude platform station) and ATG (air to ground) scenarios

## Slide 4: Justification
NTN WI with implicit compatibility to support HAPS and ATG scenarios, the expected conclusion seems to be that NTN's technology can support ATG from RAN1/RAN2, and only RAN1/RAN2 work related to ATG scenario is involved in NTT WI. This means that RAN1/RAN2 will begin to define the work related to ATG scenario. We propose that a separate WI led by RAN4 could be considered if the RAN1/RAN2 part is specified in NTN WI to support ATG
Some characteristics could to be considered for ATG network deployment scenarios:
  Extreme large inter-site distance (ISD) and large coverage range:
  Utilizing non-disjoint operators’ proprietary frequency for deploying both ATG and IMT terrestrial networks:
  Much powerful on-board ATG terminal capacity

## Slide 5: Objective
The objective of the work item is to specify the necessary features to support NR deployment for ATG application in 3GPP Release 17
Objective of SI or Core part WI
Specify features to core specifications of RF and RRM requirements for coexistence between ATG and IMT terrestrial network [RAN4]
  Study and specify the framework how ATG core requirements are defined.
  Specify the potential bands to be used as example for ATG((e.g. n79)
  Specify co-existence evaluation for ATG network (e.g. ACLR, ACS)
  Specify new UE/BS type for ATG network if necessary
  Specify RF requirements for ATG UE/BS
  Specify RRM core requirements for ATG UE
Objective of Performance part WI
Specify RRM performance requirements and test cases for ATG UE. [RAN4]
Specify demodulation performance requirements and test cases for ATG UE/BS. [RAN4]

## Slide 6
Thanks!