## Slide 1: WF on Simulation Assumptions for the SI on 6.425-7.125GHz and 10.0-10.5GHz
Nokia, Ericsson, ZTE
3GPP TSG-RAN WG4 Meeting # 94-e-Bis
Electronic Meeting, 20 – 30 April 2020
Agenda Item: 11.1
R4-2005174

## Slide 2: Background
Contributions on simulation assumptions for the SI on 6.425-7.125GHz and 10.0-10.5GHz in RAN4#94-e-Bis:
[1] R4-2003003->R4-2004951, “System level simulation methodology and assumptions for study on IMT parameters for frequency ranges 6.425-7.125GHz and 10.0-10.5GHz”, Nokia, Nokia Shanghai Bell.
[2] R4-2004128, “SI on IMT parameters - simulation assumptions”, Ericsson.
[3] R4-2004539, “IMT technology - 6.425-7.025GHz and 7.025-7.125GHz simulation parameters”, Huawei.
[4] R4-2004540, “IMT technology 10-10.5 GHz simulation parameters”, Huawei.

## Slide 3: Way forward on Simulation Assumptions (Agreed)
Deployment scenario |  | 
Urban macro | Layout | TR 38.803
 | Multi-operators: | Coordinated and uncoordinated
Dense Urban: | Layout | TR 38.803
 | Multi-operators: | coordinated
Indoor | Layout | TR 38.803
 | Multi-operators: | coordinated
Channel Bandwidth |  | 100 MHz
Frequencies |  | 7 GHz, 10 GHz
Propagation model | Path Loss | TR 38.803 with UMa LOS formula from TR 38.901
 | LOS probability | TR 38.803
 | O-to-I penetration loss | TR 38.803
Tx power control |  | TR 38.803 (May be further adjusted to target 15 UL SINR)
Received power model |  | TR 38.803
ACLR and ACS modeling |  | TR 38.803
BS output power | Max | 43 dBm (Urban macro)
UE power | Max | 23 dBm
UE Noise figure |  | 9 dB
Handover margin |  | 3 dB
UE antenna |  | Isotropic (0dBi)
BS Antenna and beam forming |  | See antenna characteristics in R4-2005173

## Slide 4: Way forward on Simulation Assumptions (Agreed)
 |  | Huawei | Nokia | Ericsson | ZTE | Agreement | Remarks
Deployment scenario |  |  |  |  |  |  | 
Urban macro | ISD | 500m | Urban: 450m Suburban : 900m | 200m | 500m | Urban: 450m Suburban : 900m | ITU-R M.2292 (Macro Urban between 3 to 6 GHz)
 | BS antenna height |  | Urban: 20m Suburban: 25m | 25m | 25m | Urban: 20m Suburban: 25m | ITU-R M.2292 (Macro Urban between 3 to 6 GHz)
Dense Urban: | Radius UE dropping |  | <65m Cell radius: 300 | <28.9m | 70m in 36.872 | Down-prioritized | Dense Urban has the least demanding ACIR requirements among the three simulated scenarios in TR 38.803.
 | Radius UE dropping – suburban |  | <130m Cell radius: 600 |  |  | Down-prioritized | Dense Urban has the least demanding ACIR requirements among the three simulated scenarios in TR 38.803.
 | BS antenna height |  | 6m | 10m | 10m | Down-prioritized | Dense Urban has the least demanding ACIR requirements among the three simulated scenarios in TR 38.803.
Indoor | Priority |  |  | Down-prioritized |  | Down-prioritized Dense Urban scenario instead | Indoor scenario has the most demanding ACIR requirements among the three simulated scenarios in TR 38.803.
BS output power | Max |  | Dense urban: 33dBm Indoor: 23 dBm |  |  | 24 dBm (Indoor) | ITU-R M.2292 (between 3 to 6 GHz)
BS Noise figure |  | 5 dB for macro base station | 7dB | 7 dB (Urban macro and dense urban) | 7dB for macro | 5 or 7dB (7GHz), 7dB(10GHz) | 10GHz according to SI TR 38.820 on 7-24GHz
UE power | Min |  | -40dBm | -36 dBm | -33dBm for 100MHz | -33dBm | TS 38.101-1 (100MHz channel bandwidth), not dominant factor
 | Max | Should we also consider 20dBm for the system simulations for 6.425-7.125GHz as proposed by Apple? |  |  |  |  | As optional case, CLx-ile may need to be adjusted