## Slide 1: WF on MR-DC RRM requirements
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN4 Meeting #94e Bis
E-meeting, April 20th – April 30th, 2020
R4-2005324
Document for: Approval

## Slide 2: Background
During the RAN4#94-e-bis E-meeting the dicussion related to Multi-RAT Dual-Connectivity and Carrier Aggregation enhancements [LTE_NR_DC_CA_enh] continued.
Summary of the round 1 discussion is captured in R4-2005244.
Based on this summary and round 2 discussions (R4-2005396) a number of agreements were reached which are captured in this WF
Additionally a number of open issue for further discussion were identified and listed. These are listed in this WF.

## Slide 3: Agreements for NR EMR
Actively measured condition (sub-topic 1-1)
  At least following conditions apply for an actively measured EMR carrier:
    T331 timer is running.
    Serving cell is in the validity area.
    Serving cell support EMR.
    The EMR carrier and the serving cell carrier are among the supported band combination of the UE
  RAN4 will follow RAN2 agreement ‘The fields s-NonIntraSearchP and s-NonIntraSearchQ in SIB2 do not affect the idle/inactive UE measurement procedures’
  UE measures EMR carriers irrespectively of configured search thresholds (aligned with LTE principle)

## Slide 4: Agreements for NR EMR
Definition of overlapping and non-overlapping (sub-topic 1-2)
    An overlapping carrier is a carrier which the UE is actively measuring for EMR and mobility.
    A non-overlapping carrier is a carrier which the UE is actively measuring for EMR.
  Note: overlapping and overlapping carrier relates to a carrier configured for EMR.

## Slide 5: Agreements for NR EMR
Define measurement requirements for NR inter-frequency and LTE inter-RAT EMR carriers (sub-topic 1-3)
  All companies support the following principle with some additional modifications:
    NR inter-frequency EMR measurement requirements on an overlapping NR EMR carrier follow existing NR inter-frequency measurements.
    LTE inter-RAT EMR measurement requirements on an overlapping LTE EMR carrier follow existing LTE inter-RAT measurements.

## Slide 6: Agreements for NR EMR
Defining the number of EMR carriers (sub-topic 1-4)
  if N>14:
    Option 1: no RAN4 requirements defined (UE implementation)
  Agreement:
    Total number of carriers that the UE needs to measure for cell reselection and EMR (overlapping or not overlapping), including NR and LTE carriers, cannot exceed Rel-15 UE capability (as defined in 38.133, section 4.2.2.1)

## Slide 7: Agreements for NR EMR
Conditions when UE is required to perform measurements for EMR (sub-topic 1-7)
  RAN4 at least defines UE EMR requirements for EMR carriers while T331 timer is active
  RAN4 not to define different or additional UE behaviour than what RAN2 has defined related to EMR measurement at cell change

## Slide 8: Agreements for NR EMR
Cell detected status (sub-topic 1-5)
Define cell detected status based on LTE baseline and on:
  The detected cell is on the overlapping or non-overlapping carrier (as indicated by dedicated RRC signalling or SIB), and
  A T331 is provided during connection release, and
  The carrier frequency of the detected cell and the serving cell are among the supported band combination of the UE
Note: last line (removed by Ericsson was already agreed in last meeting R4-2002334).
  Following was already agreed in RAN494e:
    RAN4 follow RAN2 and captures that the UE performs the idle measurement for the frequencies in configured frequency list only when the UE support CA or MR-DC between the frequency and the serving frequency

## Slide 9: WF for NR EMR
Companies are invited to provide input on measurement requirements for NR inter-frequency and LTE inter-RAT EMR carrier:
  Definition on UE measurement capability to support beam-level measurements for EMR.
  Detailed beam level measurement capability requirements:
    option 1: same as the number of beams in the existing inter-frequency requirements for RRC_CONNECTED state
    option 2: other?
  NR inter-frequency EMR measurement requirements on a non-overlapping carrier
      Consider FR1 and FR2 aspects
    LTE inter-RAT EMR measurement requirements on a non-overlapping carrier
  Measurement requirements for non-overlapping carriers.

## Slide 10: WF for NR EMR
Companies are invited to provide input on the number of EMR carriers:
  Total number of overlapping EMR carriers
  Total number of non-overlapping EMR carriers
  Total number of NR inter-frequency carriers
  Total number of LTE inter-RAT carriers

## Slide 11: WF for NR EMR
Companies are invited to provide input on when UE is required to perform measurements for EMR:
  Will RAN4 define UE EMR requirements for EMR carriers when T331 timer has expired?
  Does RAN4 define transition requirements for EMR measurement at cell change?

## Slide 12: WF for NR EMR
Companies are invited to provide input on Cell detected status:
  The detected cell remains detectable in terms of signal quality
  The detected SSBs of a cell remains detectable in terms of signal quality
  T331 status – specifically and “timer is not expired”

## Slide 13: WF for NR EMR
Companies are invited to provide input on Cell edge conditions and EMR.

## Slide 14: Agreements LTE EMR Rel-16
On measurement requirements for LTE inter-RAT EMR carriers:
  RAN4 use existing cell detection, measurement period and accuracy of cell re-selection for NR inter-RAT measurements for EMR measurements for overlapping carriers
Number of LTE EMR carriers:
  The number of LTE EMR inter-frequency carriers remain unchanged compared to Rel-15
Cell detected status:
  Agreement: Define cell detected status based on LTE baseline and on:
  The detected cell is on the overlapping or non-overlapping carrier (as indicated by dedicated RRC signalling or SIB), and
  A T331 is provided during connection release, and
  The carrier frequency of the detected cell and the serving cell are among the supported band combination of the UE
    Note: last line was already agreed in RAN4#94e meeting.

## Slide 15: WF for LTE EMR Rel-16
On Define measurement requirements for NR inter-frequency and LTE inter-RAT EMR carriers:
  Cell detection, measurement period and accuracy of cell re-selection for NR inter-RAT measurements for EMR measurements for non-overlapping carriers
  The UE beam-level measurement capability requirements for EMR:
    option 1: same as the number of beams in the existing inter-frequency requirements for RRC_CONNECTED state.

## Slide 16: WF for LTE EMR Rel-16
Number of NR Inter-RAT carriers:
    Option 1:
      Define number of NR inter-RAT EMR carriers to measure:
        option 1: 8
        option 3: 1
        option 2: 2
    Option 2:
      The number of reported carriers of CRS based and/or SSB based measurement in LTE IDLE/INACTIVE mode (overlapping and non-overlapping carriers) should not extend the measurement capability defined in Rel-15
      In LTE IDLE/INACTIVE mode DC and CA measurement, UE at least shall be able to measure N=3 carriers for EMR when UE is in cell center and UE at least shall be able to measure N=1 carriers for EMR when UE is not in cell center
      Total number of overlapping + non-overlapping EMR carriers N (including LTE inter-frequency+ NR inter-RAT)
        N= 3, when UE is in cell center
        N= 1, when UE is not in cell center
        When Srxlev > SnonIntraSearchP and Squal > SnonIntraSearchQ, UE measure N = X+Y carriers (total number of overlapping + non-overlapping EMR carriers N, including NR inter-frequency+ LTE inter-RAT)
        When Srxlev ≤ SnonIntraSearchP or Squal ≤ SnonIntraSearchQ, UE measure N = X carriers (total number of overlapping + non-overlapping EMR carriers N, including NR inter-frequency+ LTE inter-RAT)
        Where Y>0.
    Others not precluded

## Slide 17: WF for LTE EMR Rel-16
Cell detected status
  discussed further:
    The detected cell remains detectable in terms of signal quality
    The detected SSBs of a cell remains detectable in terms of signal quality
    T331 status – specifically and “timer is not expired”