## Slide 1
3GPP TSG-RAN WG4 Meeting #94-e R4-2005358
Electronic Meeting, 20 – 30 Apr., 2020
Agenda Item: 6.17.1
WF on RRM for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1912781 WF on RRM for NR HST, RAN4#92BIS
  R4-1915887 WF on RRM for NR HST, RAN4#93
  R4-2002253 WF on RRM for NR HST, RAN4#94-e

## Slide 3: Cell re-selection requirements
  For cell re-selection requirements for neighbour cell, when SMTC < =40ms, remove M2, M3, M4; when SMTC >40ms, M2 = 1.5, M3 = M4 = 2
    FFS whether additional note such as Note x: Operation with scaling factor M=1.5, M=2 may not be sufficient in all high speed deployments considered in this release of the specifications should be added in NR high speed specifications
      Option 1 (CATT, QC, CMCC, HW, Apple, Intel, DCM, MTK, vivo): No
      Option 2 (MTK, Nokia, Ericsson): Yes

## Slide 4: Cell re-selection requirements
  FFS whether to align the serving cell measurement requirements with the proposal for intra-frequency neighbour cell measurement
    Option 1 (Nokia, Ericsson): Yes, for the measurement requirements for serving cell, M1=2 if SMTC periodicity (TSMTC) > 40 ms and DRX cycle ≤ 0.64 second
    Option 2 (CATT, MTK, QC, vivo, Intel, HW, apple): No

## Slide 5: Cell identification delay requirements for DRX case in connected mode
Whether to keep the relaxation factor of 1.5 for DRX cycle <= 0.32s
  In connected mode, when SMTC < =40ms, remove 1.5x scaling factor; when SMTC > 40ms, keep the scaling factor.
    FFS whether additional note such as Note x: Operation with scaling factor 1.5 may not be sufficient in all high speed deployments considered in this release of the specifications should be added in NR high speed specifications
      Option 1 (CATT, QC, CMCC, Docomo, vivo, MTK, Nokia, Intel, HW, Apple): No
      Option 2 (Nokia, MTK , Ericsson): Yes

## Slide 6: Measurement delay requirements for DRX case in connected mode
Measurement delay in connected mode:
    For DRX <=160ms
      5 DRX cycles
      when SMTC < =40ms, remove 1.5x scaling factor; when SMTC > 40ms, keep the scaling factor
    For 160ms < DRX<=320ms
      4 DRX cycles
      when SMTC < =40ms, remove 1.5x scaling factor; when SMTC > 40ms, keep the scaling factor
    For DRX > 320ms
      3 DRX cycles when SMTC <= 40ms, 5 DRX cycles when SMTC > 40ms

## Slide 7: Applied DRX cycle in connected mode for HST
For NR HST, enhanced requirements are applied for DRX cycle <= 1.28s
  FFS whether additional note is added to the spec, such as “Requirements with 0.64s and 1.28s DRX cycle may not be sufficient in all high speed deployments considered in this release of the specifications” should be added in NR high speed specifications”
    Option 1 (DoCoMo, vivo, CATT, MTK, QC, Intel, CMCC, HW, Apple): No
    Option 2 (Nokia, Ericsson): Yes

## Slide 8: RLM
For SSB based RLM, keep the 1.5x relaxation factor
For CSI-RS based RLM, keep the 1.5x relaxation factor

## Slide 9: Beam management
For SSB/CSI-RS based BFD with DRX <= 320ms, keep the 1.5x relaxation factor
For SSB based L1-RSRP
  1.5x relaxation factor is removed when TSSB < =40, and 1.5x relaxation factor is kept when TSSB >40
For CSI-RS based L1-RSRP
  1.5x relaxation factor is removed when TCSI-RS < = 40ms, and 1.5x relaxation factor is kept when TCSI-RS > 40ms

## Slide 10: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell re-selection requirements on NR- EUTRA inter-RAT measurement in idle mode
    Option 1 (CMCC, HW, MTK, Nokia)
    Option 2 (QC, vivo):
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 2.56 (8) | 0.32(1) | 0.96(3)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96 (7) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 5.76(18) | 0.64 (2) | 0.96(3)
0.64 | 7.68 (12) | 1.28 (2) | 1.92 (3)
1.28 | 8.96(7) | 1.28 (1) | 3.84 (3)
2.56 Note1 | 58.88 (23) | 2.56 (1) | 7.68 (3)
    Option 3 (QC, CMCC,):
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 5.76(16) | 0.64 (2) | 0.96(3)
0.64 | 7.68 (12) | 1.28 (2) | 1.92 (3)
1.28 | 8.96(7) | 1.28 (1) | 3.84 (3)
2.56 Note1 | 58.88 (23) | 2.56 (1) | 7.68 (3)

## Slide 11: Inter-RAT measurement
NR- EUTRA Inter-RAT measurement
  Cell identification with DRX in connected mode
    Option 1(HW)
    Option 2 (MTK, QC, vivo, CMCC)
DRX cycle length (s) | TIdentify, E-UTRAN TDD (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.3.2 apply | Non-DRX requirements in clause 9.4.3.2 apply
0.16<DRx cycle<0.32 | Note1 (15) | Note1 (15)
0.32<= DRx cycle <= 0.64 | Note1 (10) | Note1 (10)
0.64 < DRx cycle <= 1.28 | Note1 (8) | Note1 (8)
1.28< DRX-cycle ≤10.24 | Note1 (20) | Note1 (20)
NOTE 1: The time depends on the DRX cycle length. |  | 
DRX cycle length (s) | TIdentify, E-UTRAN TDD (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.3.2 apply | Non-DRX requirements in clause 9.4.3.2 apply
0.16<DRx cycle<0.32 | Note1 (15) | Note1 (15)
0.32<= DRx cycle <= 1.28 | Note1 (10) | Note1 (10)
1.28< DRX-cycle ≤10.24 | Note1 (20) | Note1 (20)
NOTE 1: The time depends on the DRX cycle length. |  | 

## Slide 12: Inter-RAT measurement
EUTRA-NR Inter-RAT measurement
  Cell re-selection requirements on EUTRA-NR inter-RAT in idle mode
    Option 1 (CMCC, Nokia):
DRX cycle length [s] | Tdetect,NR [s] (number of DRX cycles) | Tmeasure,NR [s] (number of DRX cycles) | Tevaluate,NR [s] (number of DRX cycles)
0.32 | 2.56 x M2 (8 x M2) | 0.32 x M3 (1 x M3) | 0.96 x M4 (3 x M4)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96(7) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)
Note 1: M2 = M3 = M4 = 1 when SMTC < =40, and M2 = 1.5, M3 = M4 = 2 when SMTC >40 |  |  | 
DRX cycle length [s] | Tdetect,NR [s] (number of DRX cycles) | Tmeasure,NR [s] (number of DRX cycles) | Tevaluate,NR [s] (number of DRX cycles) | 
0.32 | 5.12 x 1.5 (16 x M) | 1.28 x 1.5 (4 x 1.5 ) | 0.96 x 1.5 (3 x 1.5) | 
0.64 | 10.24 (16) | 1.28 (2 ) | 1.92(3) | 
1.28 | 12.8 (10) | 1.28 (1 ) | 6.4(3) | 
2.56 | 58.88 (23) | 2.56 (1) | 7.68(3) | 
Note 1: M = 1.5 if SMTC periodicity of measured intra-frequency cell > 40 ms; otherwise M=1. |  |  |  | 
    Option 2 (QC)

## Slide 13: Inter-RAT measurement
EUTRA-NR Inter-RAT measurement
  Cell re-selection requirements on EUTRA-NR inter-RAT in idle mode
    Option 3 (HW, MTK, CMCC):
DRX cycle length [s] | Tdetect,NR_Intra [s] (number of DRX cycles) | Tmeasure,NR_Intra [s] (number of DRX cycles) | Tevaluate,NR_Intra [s] (number of DRX cycles)
0.32 | [3.52 x M2 (11 x M2)] | [0.32 x M3 (1 x M3)] | [0.96 x M4 (3 x M4)]
0.64 | [7.04 (11)] | [0.64 (1)] | [1.92 (3)]
1.28 | [12.8 (10)] | [1.28 (1)] | [3.84 (3)]
2.56 | [58.88 (23)] | [2.56 (1)] | [7.68 (3)]

## Slide 14: Inter-RAT measurement
EUTRA - NR Inter-RAT measurement
  Cell identification without DRX and cell identification with DRX in connected mode
    Option 1 (CMCC, QC, MTK, Nokia, ):
DRX cycle | TPSS/SSS_sync_intra | T SSB_measurement_period_intra | TSSB_time_index_intra
No DRX | Max(600ms, 8 x max(MGRP, SMTC period))×Nfreq | Max(200ms, 8 x max(MGRP, SMTC period))×Nfreq | Max(120ms, 3 x max(MGRP, SMTC period)) ×Nfreq
DRX cycle < 320ms | Max(600ms, ceil( 8 x M) x max(MGRP, SMTC period, DRX cycle)) ×Nfreq | Max(200ms, ceil(8 x M) x max(MGRP, SMTC period, DRX cycle))×Nfreq | Max(120ms, ceil(3 x M) x max(MGRP, SMTC period, DRX cycle)) ×Nfreq
DRX cycle≥320ms | 4xM x DRX cycle ×Nfreq | 4xM  DRX cycle ×Nfreq | [3] x DRX cycle ×Nfreq
Note 1: M = 1 when SMTC < =40, and M = 1.5 when SMTC >40 |  |  | 
Condition NOTE1,2 | TPSS/SSS_sync_intra | T SSB_measurement_period_intra | TSSB_time_index_intra
No DRX | max[600ms, [8] x max(MGRP, SMTC period)] | Max(200ms, 8  Max(MGRP, SMTC period))  CSSFinter | max[120ms, [3] x max(MGRP, SMTC period)]
DRX cycle ≤ 320ms | max[600ms, ceil([8]Xm) x max(MGRP, SMTC period, DRX cycle)] | Max(200ms, Ceil(8  M)  Max(MGRP, SMTC period, DRX cycle))  CSSFinter | max[120ms, ceil([3] x M) x max(MGRP, SMTC period, DRX cycle)]
DRX cycle > 320ms | 4Xm x DRX cycle | 4Xm  DRX cycle  CSSFinter | [3] x DRX cycle
NOTE 1: DRX or non DRX requirements apply according to the conditions described in clause 3.6.1 NOTE 2: In EN-DC operation, the parameters, timers and scheduling requests referred to in clause 3.6.1 are for the secondary cell group. The DRX cycle is the DRX cycle of the secondary cell group. NOTE 3: When SMTC < =40ms, M=1; when SMTC >40ms, M = 1.5 |  |  | 
    Option 2 (vivo)

## Slide 15: Inter-RAT measurement
Capabilities and configuration for inter-RAT high speed requirements
  Introduce new LTE signalling (UE capability and network flag) on LTE-NR inter-RAT measurement in 36.331 and 36.306.
  The NR-LTE inter-RAT measurement can be covered by the already agreed capabilities and network configuration (R4-1915855)
  Introduce network flag in SIB to indicate whether enhanced inter-RAT measurement requirements are applied for LTE inter-RAT carrier and NR inter-RAT carrier

## Slide 16: SS-SINR
Q1: whether to specify SS-SINR requirement
  Option 1 (CMCC, Ericsson, DoCoMo, Nokia, QC): Specify SS-SINR requirement
  Option 2 (vivo, MTK, Apple, Nokia): SINR accuracy requirement is not applicable to HST scenario
Q2: If the answer to Q1 is Yes (Option 1), how to specify the SS-SINR requirements
  Option 1 (CMCC): Specify SS-SINR accuracy requirement for SNR <= [11] dB
  Option 2 (QC): SINR accuracy requirement is not applicable to HST scenario when SNR > 5 dB
  Option 3 (Nokia): Reusing Rel-15 intra-frequency SS-SINR accuracy requirements as a baseline for HST, where the lower bound SNR = [-3dB] and the upper bound of SNR = minimum of the absolute SNR value for SCS = 15 kHz and 30 kHz based on simulation results

## Slide 17: Inter-frequency measurement
The inter-frequency measurement enhancement for high speed scenario is not considered in Rel-16