## Slide 1: WF on NR Positioning UE measurements and reporting (RAN4#94-e-Bis email thread #115)
Qualcomm Inc
3GPP TSG-RAN WG4 Meeting # 94-e-Bis
Electronic Meeting, April 20-30, 2020
Agenda: 6.8.2.1.1, 6.8.2.1.2, 6.8.2.1.3, 6.8.2.1.5
R4-2005378

## Slide 2: Parameter k in report mapping tables
Agreement from GTW session (April 27th 1-3pm UTC):
  LMF provides a recommended k value (k1). UE selects parameter k (k2) and informs to the LMF. Further discuss the relation between UE selected parameter k2 and network recommended value k1.
Further discuss for RSTD and UE Rx-Tx time difference reporting:
  Relationship between k1 and k2
  Range of k1 and k2 in FR1
Agreements on RSTD and UE Rx-Tx time difference report mapping tables captured in LS to RAN2 (R4-2005415)

## Slide 3: PRS-RSRP differential report mapping
Agreement from GTW session (April 27th 1-3pm UTC):
  [-30,0] dB for DL-AoD and +/- 30 dB for multi-RTT and DL-TDOA
    Note: values are applicable when PRS RSRP measurements are TDM-ed. Further discuss when PRS RSRP measurements are FDM-ed
Further discuss the applicable range of differential PRS-RSRP when PRS-RSRP measurements are FDM-ed
Agreements on PRS-RSRP report mapping tables captured in LS to RAN2 (R4-2005415)

## Slide 4: NTA,Offset for Rx-Tx time difference reporting
Further discuss:
  Need for UE signaling of NTA,Offset
  If needed, details on UE signaling of NTA,Offset

## Slide 5: Definition of intra-frequency and inter-frequency RSTD measurements
Further discuss the definition of intra-frequency and inter-frequency RSTD measurements:
  Option 1. Intra-frequency RSTD measurement is defined as when the neighbor DL PRS resource and the reference DL PRS resource belong to the same positioning frequency layer. Otherwise, the RSTD measurement is inter-frequency.
  Option 2. Intra-frequency RSTD measurement is defined when neighbour DL PRS resource and reference DL PRS resource belong to the same positioning frequency layer, and the BW of the positioning frequency layer is within the BW of UE’s active DL BWP, and SCS and CP of the positioning frequency layer are the same as those of UE’s active DL BWP. Otherwise, the RSTD measurement is inter-frequency.
    Option 2a. Intra-frequency RSTD measurement is defined when the DL PRS resources to be measured, including reference cell and neighbor cell, have the same center frequency, SCS and CP type as serving cell and the BW of these PRS are all within the active BWP. Otherwise, the RSTD measurement is inter-frequency measurement.
  Option 3. Intra-frequency RSTD measurement: the center frequency of PRS BW is the center frequency of a serving cell SSB and has the same SCS as that of the serving cell SSB, otherwise it is inter-frequency. MG may be needed for intra- or inter-frequency, depending on whether or not the PRS BW is within the active BWP (NOTE: for RSTD, the above conditions are met for both reference and the other DL links)
  Option 4. Intra-frequency PRS measurement is defined when the BW of the PRS layer is confined within the UE active BWP. Otherwise, the PRS measurement is inter-frequency.

## Slide 6: Measurement period – Impact of SSB symbols
Further discuss whether PRS-RSTD, PRS-RSRP, and UE Rx-Tx time difference measurement period should be extended to account for dropped PRS occasions being unavailable (e.g., due to overlap with SSB symbols).
  Details FFS.

## Slide 7: Measurement period – Impact Rx beam sweeping
Further discuss whether or how to extend the measurement period to account for Rx beam sweeping in FR2
  Option 1. Similar to SSB-based RRM measurement in R15
  Option 2. Based on Rx beam sweeping within a PRS occasion over slot repetitions of PRS resources. Details FFS.
  Other options are not excluded

## Slide 8: Measurement period – Impact of SRS periodicity
Further discuss whether SRS periodicity impacts UE Rx-Tx time difference measurement period
  Details FFS

## Slide 9: Measurement period – Basic number of PRS occasions per PRS resource
Further discuss the basic number of PRS occasions (X) per PRS resource needed to meet the accuracy requirements accounting for fading channel, AGC settling, and muting pattern.
  Other factors not excluded

## Slide 10: Measurement period – Others
Measurement period due to HO
  To be discussed after measurement period without HO is defined
Measurement period for more than one frequency layer
  To be discussed after measurement period for one frequency layer is defined
Number of PRS resources for the measurement period definition
  To be discussed after conclusion of RAN1 UE capability discussions
Measurement period with more than one PRS periodicity
  To be discussed after measurement period with one PRS periodicity is defined

## Slide 11: Measurement capability
RAN4 to not define the minimum for the number of positioning frequency layers (X1) for positioning requirements
  RAN1 UE capability for X1 allows values of {1,4} to be signaled with other values FFS.
Whether to define the minimum for X2, …, X7 to be discussed after the conclusion of RAN1 UE capability signaling
Applicability of requirements when exceeding UE processing/buffering to be discussed after the conclusion of RAN1 UE capability signaling

## Slide 12: Measurement reporting criteria
Further discuss measurement reporting criteria for PRS-RSTD, PRS-RSRP, and UE Rx-Tx time difference

## Slide 13: Scheduling restriction in FR1
Further discuss scheduling restrictions for PRS symbols in FR1

## Slide 14: Measurement gap for PRS measurement
Further discuss when measurement gap is needed for PRS measurement in FR1 and FR2
Further discuss applicability of R15 measurement gap patterns to NR positioning
  Option 1: at least Rel-15 NR measurement gaps apply for positioning measurements
  Other options are not excluded

## Slide 15: PRS-RSTD Side conditions
PRS-RSTD side conditions for FR2:
  Option 1. -3 dB for reference and -10 dB for neighbor cells
  Option 2. Same as FR1

## Slide 16: PRS-RSRP Side conditions
Serving cell:
  Option 1. -6 dB
  Option 2. For DL-AoD and Multi-RTT, the side condition for FR1 and FR2 is -3 dB for serving TRP
  Option 3. Not needed
Reference cell:
  Option 1. For OTDOA (i.e., when configured with RSTD), PRS-RSRP side condition for reference (which may or may not be serving) TRP to be the same as for reference cell for RSTD
  Option 2. Not needed
  Option 3. Same as that for the reference cell in PRS-RSTD measurement
Neighbor cell:
  Same as neighbour cell PRS-RSTD

## Slide 17: UE Rx-Tx time difference side conditions
Serving cell:
  Option 1. -6 dB
  Option 2. Serving cell side condition for UE Rx-Tx: -3 dB, for FR1 and FR2.
  Option 3. Not needed
Reference cell:
  Not needed.

## Slide 18: Accuracy requirements
Further discuss the number of samples for accuracy requirements for PRS-RSTD and PRS-RSRP
Further discuss the applicability of RSTD accuracy requirements under cell change after conclusion of intra-frequency and inter-frequency definition
Further discuss the applicability of Rx-Tx time difference accuracy requirements under
  Cell change
  TA change

## Slide 19: Proximity of SRS and PRS
Further discuss the need for proximity condition of SRS and PRS resources in time for UE Rx-Tx time difference measurements
  Details FFS.

## Slide 20: Types of accuracy requirements
Relative and absolute RSRP requirements
  Option 1. Define only relative accuracy requirements for PRS-RSRP
  Option 2. Define both absolute and relative accuracy requirements for PRS-RSRP
  Option 3. Define only absolute accuracy requirements for PRS-RSRP
Serving vs. neighbour UE Rx-Tx timing difference
  Option 1. Define requirements for:
    Serving cell
    Neighbor cell
  Option 2. No separate requirement for serving and neighbour cells

## Slide 21: Link-level simulation plan for UE Rx-Tx time difference
Link-level simulations plan:
  RAN4#95 – try to agree on simulation assumptions,
  RAN4#96 – provide first simulation results.

## Slide 22: Link-level simulation results
FFS: The accuracy requirements shall be agnostic to comb pattern (assuming all other configurations are the same)
PRS-RSTD, PRS-RSRP, and UE Rx-Tx time difference accuracy requirements will be separately defined for FR1 and FR2.