## Slide 1: 3GPP TSG-RAN WG4 Meeting #94-e-Bis Electronic Meeting, 20 – 30 Apr., 2020
ZTE, …
WF on co-location scenarios and Tx IMD requirements for IAB
R4-2005491

## Slide 2: Background
For IAB-MT, it is proposed to reuse BS TX IMD requirement in [1]
TX IMD is co-location requirement so whether to have co-location requirement for IAB-MT is discussed under thread #209 and the summary for first round is in [2].

## Slide 3: Agreements --IAB-MT co-location scenarios
  Co-location scenarios for IAB-MT have been separated as 3 scenarios:
    -co-located with another IAB-MT in same band.
    -co-located as IAB-DU and IAB-MT transmit simultaneously in the same band with same TDD pattern.
    -co-located with another IAB-DU/BS in another band.

## Slide 4: Agreements --IAB TX IMD requirements
For IAB-DU in FR1:
It has been agreed to reuse BS TX IMD requirement for IAB-DU in [3].
For IAB-MT:
For FR2, It is agreed that no TX IMD requirement is specified in [2].
For FR1, based on the co-location scenarios as:
-co-located with another IAB-MT in same band
    -co-located as IAB-DU and IAB-MT of one IAB-Node transmit simultaneously in the same band with same TDD pattern as the other co-located BS and/or IAB-Node.
    - In case of two co-located IAB-Nodes, all IAB-MTs and IAB-Dus need to follow same TDD pattern.
    With these two scenarios considered, reusing BS TX IMD requirement for IAB-MT is applicable for :
      WA IAB-MT
      LA IAB-MT with single carrier case as the multiple carrier how to handle is still FFS
    For interference level it should refer to IAB-MT own power
    The transmitter intermodulation level shall not exceed the unwanted emission requirement defined for each IAB-MT class
    -co-located with another IAB-DU/BS in another band
    As in the BS case if the in-band TX IMD is specified it is dominant and this is not necessary This scenario is covered by co-location spurious emission and co-location blocking requirement.

## Slide 5: Reference
[1] R4-2004096 on IAB TX IMD, ZTE
[2] R4-2005438 Email discussion summary for [94e Bis][208] NR_IAB_RF_Part_2, Nokia
[3] R4-2002497 TP for TR _9 IAB OTA transmitter intermodulation, Ericsson