## Slide 1: 3GPP TSG-RAN WG4 Meeting #94bis-e R4-2005528 Electronic Meeting, 20th – 30th Apr., 2020
Huawei, HiSilicon
Way forward on NR URLLC BS performance requirements

## Slide 2: Background
The following WFs were approved:
  R4-1915913: Way forward on NR URLLC demodulation and CSI requirements, RAN4 #93
  R4-2002429: Way forward for NR BS URLLC performance requirements, RAN4 #94

## Slide 3
Agreements:
  PUSCH aggregation factor
    n2 for TDD 30 kHz SCS with TDD pattern 7DS2U.
  Number of PRBs: Full bandwidth.
  SCS/CBW: 15 kHz for 10 MHz, 30 kHz for 40 MHz
  Test applicability for different SCS and channel bandwidth:
    Reuse the test applicability rules defined for NR Rel-15 PUSCH performance requirements
  Not define requirements with DFT-s-OFDM
  Whether to define requirements for FR2
    Keep it open meanwhile prioritize discussion on introducing FR1 requirements in Q2; and interested companies are encouraged to bring more information and analysis for the deployment/usage scenarios in FR2 with ultra-low BLER and/or higher BLER for high reliability and low latency
PUSCH demodulation requirements for high reliability with higher BLER and/or confidence level:

## Slide 4: PUSCH demodulation requirements for high reliability with higher BLER and/or confidence level:
PUSCH aggregation factor
  15 kHz TDD with pattern DDDSU:
    Option 1: n2
    Option 2: n8
SCS/CBW (15 KHz/10 MHz, 30 KHz/40 MHz have been agreed)
  Option 1: 15 KHz for 5/10 MHz, 30 KHz for 10/40 MHz
  Option 2: Only 15 KHz/10 MHz, 30 KHz/40 MHz
Whether to clarify the safety statement
  Option 1: No
  Option 2: Yes
    Since the URLLC features of 5G NR will potentially be used in safety critical applications, the ultimately chosen statistical testing methodology for testing of these features must be verified by an independent body of experts/statisticians, before requirements and test can be used as basis for safety critical implementations. All statistical analysis and discussions provided in this meeting are to be taken as a best effort and is not to be taken as due diligence

## Slide 5: PUSCH demodulation requirements for high reliability with higher BLER and/or confidence level:
Whether to define requirements for FR2
  Option 1: No
  Option 2: Yes
Test applicability rule for FR1 and FR2 (only if FR2 is defined)
  Option 1: If BS supports both FR1 and FR2, the tests shall be done for either FR1 or FR2
  Option 2: If BS supports both FR1 and FR2, the tests shall be done both
  Option 3: Which tests related to FR1 and FR2 be tested shall be based on BS declaration: [FR1], [FR2], [FR1&FR2]
SCS/BW for FR2 (only if FR2 is defined)
  60 KHz:
    Option 1: 50 MHz
    Option 2: 50 MHz and 100 MHz
  120 KHz
    Option 1: 100 MHz
    Option 2: 50 MHz and 100 MHz

## Slide 6: Simulation assumptions for PUSCH demodulation requirements for high reliability with higher BLER and/or confidence level for FR1
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Antenna configuration |  | 1x2, ULA Low
PUSCH configuration | Mapping type | Type A and Type B
 | Starting symbol (S) | 0
 | Length (L) | 14
 | PUSCH aggregation factor | n2 for 30 kHz SCS FFS 15 kHz SCS
PUSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | 1
Propagation condition |  | TDLB100-400
MCS Table |  | Table 3, MCS 5
SCS and BW |  | 15 kHz for 10 MHz 30 kHz for 40 MHz
Frequency domain resource |  | Full Bandwidth
TDD pattern |  | 15 kHz SCS: 3D1S1U, S=10:2:2 30 kHz SCS: 7D1S2U, S=6:4:4
Maximum number of HARQ transmissions |  | 4
Testing metric |  | Target BLER: 10-2 (Calculate the target BLER after all transmission)

## Slide 7: PUSCH demodulation requirements for low latency
BS FR1 URLLC demodulation requirements for PUSCH mapping Type B
Agreements:
  MCS: MCS 5 from Table 3
  Number of PRB: Full bandwidth for MCS5
  Not introduce performance requirements for DFT-s-OFDM
  SCS/CBW: 15 kHz for 10 MHz, 30 kHz for 40 MHz
  Test applicability for different SCS and channel bandwidth:
    Reuse the test applicability rules defined for NR Rel-15 PUSCH performance requirements
  Whether to define requirements for FR2
    Keep it open meanwhile prioritize discussion on introducing FR1 requirements in Q2; and interested companies are encouraged to bring more information and analysis for the deployment/usage scenarios in FR2 with ultra-low BLER and/or higher BLER for high reliability and low latency

## Slide 8: PUSCH demodulation requirements for low latency
BS FR1 URLLC demodulation requirements for PUSCH mapping Type B
  Symbol length
    Option 1: 4os
    Option 2: 7os
  SCS/CBW (15 KHz/10 MHz, 30 KHz/40 MHz have been agreed)
    Option 1: 15 KHz for 5/10 MHz, 30 KHz for 10/40 MHz
    Option 2: Only 15 KHz/10 MHz, 30 KHz/40 MHz
  Test metrics
    Option 1: 70% throughput
    Option 2: 30% BLER
  Note: Discuss whether to word as throughput, BLER, success rate or something similar.

## Slide 9: BS demodulation requirements for low latency
BS URLLC demodulation requirements for PUSCH mapping Type B
  Whether to define requirements for FR2
    Option 1: No
    Option 2: Yes
  Test applicability rule for FR1 and FR2 (only if FR2 is agreed)
    Option 1: Only FR1 or FR2 will be tested based on BS declaration.
    Option 2: Both FR1 and FR2 should be tested for BS that supports both FR1 and FR2.
    Option 3: Which tests related to FR1 and FR2 be tested shall be based on BS declaration: [FR1], [FR2], [FR1&FR2]
  SCS/CBW for FR2 (only if FR2 is agreed)
    60 KHz:
      Option 1: 50 MHz
      Option 2: 50 MHz and 100 MHz
    120 KHz
      Option 1: 100 MHz
      Option 2: 50 MHz and 100 MHz

## Slide 10: Simulation assumptions for PUSCH demodulation requirements for mapping Type B for FR1
Parameter |  | Value
Frequency range |  | FR1
Transform precoding |  | Disabled
Antenna configuration |  | 1x2, ULA Low
PUSCH configuration | PUSCH mapping type | Type B
 | Start symbol | 0
 | Allocation length | 4 or 7
 | PUSCH aggregation factor | 1
PUSCH DMRS configuration | DMRS Type | Type 1
 | DM-RS duration | Single-symbol DM-RS
 | Number of additional DMRS | FFS: 0 for 4os, 1 for 7os
SCS and BW |  | 15 kHz for 10 MHz 30 kHz for 40 MHz
TDD pattern |  | 15 kHz SCS: 3D1S1U, S=10:2:2 30 kHz SCS: 7D1S2U, S=6:4:4
MCS Table |  | Table 3, MCS 5
Propagation condition |  | TDLC300-100 Low
Maximum number of HARQ transmissions |  | 1
Frequency domain resource assignment |  | Full bandwidth For MCS5
Test metric |  | 70% TP or 30% BLER