## Slide 1: Way forward on PMI reporting requirements for Tx ports larger than 8 and up to 32
Ericsson, Samsung
3GPP TSG-RAN4 Meeting #94e-Bis
Electronic Meeting April 20 – April 30 , 2020
Agenda item: 6.18.1.2
R4-2005549
Document for: Approval

## Slide 2: Timeline of previous agreements
#92
  WF: R4-1910017
#92bis
  WF: R4-1912834
  simulation assumptions: R4-1912811
#93
  WF: R4-1915858
  Simulation assumptions: R4-1915859
#94e
  WF: R4-2002393
  Simulation assumptions: R4-2002394

## Slide 3: PMI tests SP Type I page 1
Wideband PMI requirements
  32Tx ports
PMI requirements for 16 Tx ports (decision in RAN4#95-e)
  Option 1: Introduce subband PMI requirements for 16 Tx ports as baseline
  Option 2: Not introduce subband PMI requirements for 16Tx ports and covers 16Tx port requirements with wideband PMI

## Slide 4: 16Tx ports SP Type I page 2
Duplex mode:
  FDD 10MHz/15kHz BW/SCS
  TDD 40MHz/30kHz BW/SCS
Number of Rx antennas:
  2Rx, and 4Rx
Subband size (if applicable)
  FDD: 8
  TDD: 16

## Slide 5: NZP-CSI-RS configuration SP Type I page 3
16Tx ports:
  (k0, k1, k2, k3) = (2, 4, 6, 8), l0 = (5)
32Tx ports:
  (k0, k1, k2, k3) = (2, 4, 6, 8), (l0, l1) = (5, 12)

## Slide 6: Result collection SP Type I page 4
Further alignment needed given current divergency amonst companies’ results.
Set gamma (gain) values based on simulation results in RAN4#95-e
Detailed simulation assumptions found in tdoc R4-2005550

## Slide 7: Type II test setup
Test setup:
  Option 1: Use SU-MIMO test setup as baseline scenario
  Option 2: MU-MIMO based test setup

## Slide 8: Parameters for SU-MIMO Type II page 1
Codebook construction
  Option 1: 16Tx ports (N1,N2) = (4,2), (O1, O2) = (4,4)
  Option 2: 32Tx ports (N1,N2) = (4,4), (O1, O2) = (4,4)
L (numberOfBeams)
  2
Npsk (phaseAlphabetSize)
  Option 1: 4
  Option 2: 8
SubbandAmplitude
  Option 1: False
  Option 2: True
PMI-FormatIndicator
  Option 1: Wideband
  Option 2: Subband
Propagation condition
  TDLA30-5
MIMO correlation
  Option 1: XP High
  Option 2: XP Medium

## Slide 9: Parameters for SU-MIMOType II page 2
MCS and rank
  As baseline, use MCS 20, rank 2
Beam steering model
  Option 1: Reusing beam steering approach with dual-cluster beams as specified in B.2.3B.4A of TS 36.101
  Option 2: Use Equation 1 as beam steering model for Type II codebook performance requirements.
  Option 3: Use option 1 if L = 2, and use option 2 if L > 2
Test metric
  TP ratio between following PMI and rand PMI

## Slide 10: Parameters for MU-MIMO Type II
Parameters for MU-MIMO based setup TBD on simulations
Test metric
  Option 1: TP ratio between following PMI and random PMI
  Option 2: TP ratio between following Type II codebook and following SP Type I codebook
  Other options are not precluded

## Slide 11: For information: MU-MIMO based test setup
TBD regarding co-scheduled UE channel assumptions (H(f,t,p))

## Slide 12: For Information: Beam steering model for L number of beams