## Slide 1: WF on Uplink Full Power Transmission
Samsung
3GPP TSG-RAN WG4#94-e-Bis Meeting R4-2005652
Electronic Meeting, 20th – 30th Apr., 2020

## Slide 2: Way Forward (Agreed on Tuesday GTW session)
Transparent Tx Diversity (TxD) in Rel-16 (TBD its applicability for UEs supporting or not supporting full power transmission)
  Transparent TxD shall be allowed for FR1 in Rel-16:
    Necessary changes to Rel-16 RAN4 specification is needed to allow the UE behavior of transparent TxD in FR1;
    TBD (Accordingly RAN5 will change test cases to allow transparent TxD)
  From Rel-16 and beyond, SA UE declaring PC2 HPUE shall have 26dBm MOP for both 1TX port transmission and 2TX UL-MIMO (if supported)
    For UE with 23dBm+23dBm PA architecture, transparent TxD shall be used to have 26dBm MOP for 1TX port transmission.
    TBD how the requirements will be specified
  Conclusion of Rel-16 discussion will have no impact on Rel-15
  TBD how to capture the requirements for different UEs

## Slide 3: Way Forward (Agreed on Tuesday GTW session)
Clarification on Transparent TxD (1/3)
  Scenario-1:
    NW use DCI format 0_0 to schedule PUSCH for 1layer 1Tx antenna port transmission, or
    NW configured 1 SRS port in one SRS resource and use DCI format 0_1 to schedule codebook-based PUSCH transmission PUSCH with precoder [1] for 1layer 1Tx antenna port transmission.
  Transparent TxD shall be allowed in Scenario-1;
  If transparent TxD is used in Scenario-1:
    Transmission come out from two antenna connectors;
    FFS measurement configuration for transparent TxD transmission, e.g.,
      the way to adjustment of relative phase coherence between TX branches;
      the way to derive verdicts under the condition in which the active antennas are unknown;
      the way to derive EVM measurement results after measuring per antenna connector;
      etc.

## Slide 4: Way Forward (Agreed on Tuesday GTW session)
Clarification on Transparent TxD (2/3)
  Scenario-2:
    UE supports 2 SRS ports;
    NW configured 2 SRS ports in one SRS resource;
    NW use DCI format 0_1 to schedule codebook-based PUSCH transmission with precoder [1 0] or [0 1] in 1layer 2Tx precoder codebook, which corresponding to 2 SRS ports in the SRS resource
  The scheduled precoder [1 0] or [0 1] in Scenario-2 is not regarded as “transparent TxD” for two antenna connector implementation.
  In Scenario-2, can “transparent TxD” be applied to non-zero power 1 TX in precoder [1 0] or [0 1]?
    Option-1 (Samsung, Intel): No.
    Option-2: Yes

## Slide 5: Way Forward (Agreed on Tuesday GTW session)
Clarification on Transparent TxD (3/3)
  Scenario-3:
    UE supports 2 SRS ports;
    NW configured 2 SRS ports in one SRS resource;
    NW use DCI format 0_1 to schedule codebook-based PUSCH transmission with precoder [1 1] in 1layer 2Tx precoder codebook, which corresponding to 2 SRS ports in the SRS resource.
  The scheduled precoder [1 1] in Scenario-3 is not regarded as “transparent TxD”. (Qualcomm, Intel, Samsung)

## Slide 6: Way Forward
New Power Class Capability
  No need to introduce a new power-class capability because power class declaration should be applied to all transmission modes from Rel-16.

## Slide 7: Way Forward
General Scope and Assumption for UL Power Transmission (ULFPTx)
  In Rel-16 eMIMO, FFS how to introduce UE RF requirement for ULFPTx feature in FR2:
    Companies are encouraged to bring CR to introduce UE RF requirement for ULFPTx feature in RAN4 May meeting.
  In which specification clause to capture MOP requirement for ULFPTx:
    MOP requirement for ULFPTx with 2 TX ports configured for FR1 should be specified in Section 6.2D;

## Slide 8: Way Forward
Test Configuration and Requirement Applicability for ULFPTx (1/2)
  For Mode 1 UE ULFPTx feature, the following applicability rule should be followed:
    Mode 1 UE shall support TPMI [1 1] with full power transmission when Rel-16 ULFPTx Mode 1 is configured.
  For Mode 2 UE with 1 port configuration, no new ULFPTx MOP requirement is needed to be introduced in clause 6.2D.
    ULFPTx MOP requirement in this case can be guaranteed by MOP requirement for fallback DCI as captured in general requirement in clause 6.2

## Slide 9: Way Forward
Test Configuration and Requirement Applicability for ULFPTx (2/2)
  For Mode 0 UE (“the other mode”) with 2 ports configuration:
    RAN4 core requirement is defined based on all supported full power TPMIs, and it is up to RAN5 to select test configuration to perform test.
  For Mode 0 UE (“the other mode”) with 1 port configuration, no new ULFPTx MOP requirement is needed to be introduced in clause 6.2D.
    ULFPTx MOP requirement in this case can be guaranteed by MOP requirement for fallback DCI as captured in general requirement in clause 6.2

## Slide 10: Contributions List in RAN4#94-e-Bis
T-doc No. | Title | Company
R4-2003216 | On eMIMO full Tx power transmission | Intel Corporation
R4-2003217 | On Transparent Tx Diversity | Intel Corporation
R4-2003330 | Consideration on introduction of Tx diversity feature in Rel-16 | Anritsu Corp.
R4-2003537 | Further Discussion on Uplink Tx Full Power Transmission | Samsung
R4-2003874 | FP transmission, transparent TxD and additional power-class capability | Ericsson
R4-2003907 | Further on full power transmission in eMIMO | OPPO
R4-2004056 | Further discussion on UE RF requirments for eMIMO UL Full power Tx | vivo
R4-2004474 | TX full power capability | Qualcomm Incorporated
R4-2004738 | On NR eMIMO full power transmission | Huawei, HiSilicon
R4-2004869 | Full power transmission and FR2 | Qualcomm Incorporated
R4-2004977 | Enabling TX diversity for eMIMO | Qualcomm Incorporated

## Slide 11: Reference
[1] R4-2005098, “Email discussion summary for [94e Bis][12] NR_eMIMO_UE_RF”, Samsung