## Slide 1: WF on intra-band UL non-contiguous CA MPR
Skyworks, Huawei, Qualcomm
3GPP TSG-RAN WG4 Meeting #94-bis-e R4-2005661
Electronic Meeting, Apr.20th – Apr.30th 2020

## Slide 2: Background based on [1] and scope
From [1]:
  UL NC CA requested configurations are n41(2A), n77(2A), n78(2A)
  2PA/2LO architecture is assumed to enable support of 580MHz with associated signaling
  Signaling on instantaneous transmit bandwidth classes are in place
Scope:
  Defining evaluation assumptions for MPR evaluation
  Due to reverse IMD aspects only measurement may be valid for evaluation
  Some can be derived from n41 ENDC work but:
    NR UL CA should assume equal PSD instead of equal power used in many ENDC measurements
    Only instantaneous TX BW of 194MHz assessed and one CC being 20MHz LTE
    NR UL CA is PC3 only where ENDC targeted PC2 (PA calibration at 31dB ACLR)
    Only equal back-off applies to CA
  At least specific measurements are needed for two 100MHz CCs and instantaneous TX BW of 580MHz
Instantaneous TX bandwidth: frequency range from the lower bound of lower CC to the upper bound of upper CC.

## Slide 3: Background on waveforms
There is up to 2dB difference in PAPR for DFT-s-OFDM and CP-OFDM between correlated and user data only uncorrelated case
It is essential to use different data input for each CC to avoid correlated peaks in each CCs especially when LCRB is the same in each CC.
For 2PA measurements since two separate waveform generators are used it is enough to use different PRBS sequences (PN9 and PN23 for example) per CC. Cell ID is the same for each CC
Lower correlation can further be obtained by using different DMRS patterns for each CC (RB shift) and may be considered

## Slide 4: WF on two transmit path assumptions
Antenna isolation of 10dB
Other PCB related isolations are assumed negligible
Post PA losses of 4dB (Note that worst case RIMD is for lowest post PA losses)
PA calibrated for 30dB ACLR at 26dBm for 20MHz DFT-s-OFDM QPSK 100RB0 waveform
Appropriate waveform settings is used for PAPR
ACLR, SEM and spurious emission evaluated per agreements in [1] without any LO or image exceptions
IBE and EVM are evaluated with only one active CC thus single CC inner allocation MPR applies accordingly

## Slide 5: WF on cases to be evaluated
Companies are encouraged to provide input for following cases (all or partially)
All modulation orders for CP-OFDM and DFT-s-OFDM
Baseline MPR is aligned on QPSK first
100+100MHz with 380MHz separation
20MHz+20MHz with 120MHz separation
20MHz+20MHz with 20MHz separation
20MHz+100MHz with 20MHz separation
A set of corner case allocations:
  1RB+1RB
  Full allocation + Full allocation
  Asymmetric cases that can create IMDs falling fully within outer ACLR regions

## Slide 6: WF on band 7/38/41 protection
With close to 580MHz instantaneous TX BW from >3.4GHz, bands in the 2.5GHz to 2.7GHz range are subject to IMD5 emissions
Band n78/n77 isolation to band 7/38/41 should be evaluated and reported
Potential UL restrictions should be studied accordingly
Companies are invited to provide their input in next meeting

## Slide 7: Reference
[1] R4-2005660, “WF on intra-band UL non-contiguous CA general requirements”, KDDI, […]
[2] R4-2005100, “Email discussion summary for RAN4#94be_#14_NR_RF_FR1_Part_1”, Huawei
[3] R4-2004467, “FR1 Intra-band Non-contiguous ULCA”, Qualcomm