## Slide 1: WF simplification on EN-DC including FR2
NTT DOCOMO, INC.,
3GPP TSG-RAN WG4 Meeting #94-e-Bis R4-2005169
Online Meeting, 20-30 Apr 2020

## Slide 2: Background(1/3)
Previous agreements on simplification on EN-DC configuration including FR2 was option 2-2 described in [1]:
RAN4#94-e-bis has discussed the detail of procedure how to and when to reflect it in the specification and in basket WI procedure.

## Slide 3: Background(2/3)
The following aspects ware discussed in RAN4#94-bis-e.
  1: Whether or not proponent can submit draft CR directly for inter-band EN-DC including FR2
    NOTE: TPs for inter-band EN-DC including FR2 only capture EN-DC configuration, but does not capture any technical analysis such as UE to UE coexistence and MSD.
  2: Structure of Rel-17 basket WI
    Whether we need new basket WI to handle inter-band EN-DC including FR2 efficiently.
  3: Request sheet format according to modification of EN-DC configuration table
  4: Time schedule to reflect the modification
  5: Clarification of the use of wildcard “@”
  NOTES:
    The detail of discussion was captured in [2].
    The above discussion are for only inter-band EN-DC including FR2, and does not touch anything for other band combinations
    The change is for description methods of EN-DC configuration in TS 38.101-3, and there is no change on signalling aspect

## Slide 4: Background (3/3)
5: Clarification of the use of wildcard “@” as proposed in [1][3]
  It impacts on only how to write EN-DC configuration table and how to introduce new EN-DC configuration in the specification. Other aspects including signalling aspects does not change.
    Example) TS 38.101-2 specify CA_n257G and CA_n257H, and TS 38.101-3 specify DC_1A_n257”@”, which means TS 38.101-3 have DC_1A_n257G and DC_1A_n257H. UE can signal its capability in the same manner before.
  Description method
    NR FR2 band n2XX”@” indicates single carrier, intra-band contiguous CA, and intra-band non-contiguous CA specified in TS 38.101-2.
    n2XX”@”-n2YY”@” should be used for FR2 Inter-band CA.
Concerns raised for the use of wildcard @
  If the change is applied in existing Release, EN-DC configuration which were not requested in past are completed automatically
  How to distinguish FR2 intra-band contiguous and FR2 intra-band non-contiguous CA
  Inconsistency of fallback combinations would occur when @ is applied for FR1 + FR2 NR CA

## Slide 5: Way Forward(1/3)
1: Whether or not a proponent can submit draft CR directly for inter-band EN-DC including FR2
  RAN4#95-e should decide to take either of option 1 or option 2.
    Option 1: Keep current manner (just follow the previous agreements in [4])
    Option 2: No need to submit TP and allow a proponent to directly submit draft CR for EN-DC including FR2 bands (which means that we don’t need to capture EN-DC including FR2 in TR)

## Slide 6: Way Forward(2/3)
4: Time schedule to reflect the modification
  RAN4#95-e should decide to take either of option 1 or 2
  Option 1:
    Modification of EN-DC configuration table should be done by the end of Rel-16
      CR for modification on EN-DC configuration table will be approved in RAN#95-e.
    New simplified procedure to specify inter-band EN-DC including FR2 should be applied from the start of Rel-17
  Option 2:
    Modification of EN-DC configuration table should be done for the first publication of Rel-17 specification.
    New simplified procedure to specify inter-band EN-DC including FR2 should be applied from the FFS.
  Other options for simplification on band combinations are not precluded (e.g. using Excel format).
  From which Release the modification of EN-DC configuration table should be done is FFS.

## Slide 7: Way Forward(3/3)
5 : Clarification of the use of wildcard “@”
  Study problematic cases and solutions for the use of wildcard “@” for each band combination cases
    Case 0: Common for all cases from 1 to 5
    Case 1: LTE + FR2 Single carrier
    Case 2: LTE + FR2 intra-band contiguous CA
    Case 3: LTE + FR2 intra-band non-contiguous CA
    Case 4: LTE + FR2 inter-band CA
    Case 5: LTE + FR1 + FR2 inter-band CA
  The wildcard approach will be introduced to each case independently if the problematic cases and solutions are confirmed.

## Slide 8: References
[1] R4-1910908, “Further discussion on EN-DC configuration including FR2”, NTT DOCOMO, INC.
[2] R4-2005121, “Email discussion summary for [94e Bis][35] BC_simplification”, Moderator (NTT DOCOMO)
[3] R4-2003880, “Further discussion on simplification of EN-DC configuration including”, NTT DOCOMO, INC.
[4] RP‑181126, “WF to reduce further TPs due to band combination in RAN4”, NTT DOCOMO, INC., Nokia, Nokia Shanghai Bell