## Slide 1: WF on supporting new channel bandwidth added to existing operating bands in a manner of release independence from Rel-15
ZTE
3GPP TSG-RAN WG4 Meeting #94-e-Bis
E-meeting, 20th – 30th Apr., 2020
R4-2005197

## Slide 2: Background – TS 38.307
TS 38.307 v15.5.0
TS 38.307 v16.2.0

## Slide 3: Issue - 1
Take n28 as one example:
The band was introduced in Rel-15
A new UE channel bandwidth (30MHz) is introduced to n28 in Rel-16, and claimed to be released independent from Rel-15
  According to TS 38.307 v16.2.0, Requirements to be fulfilled are seen from TS 38.307 of the release in which the band was introduced
    Since the band n28 was introduced in Rel-15, the requirements to be fulfilled should be referred to TS 38.307 v15.2.0 (up-to-date Rel-15 version)
    And in TS 38.307 v15.2.0, it is empty in the fourth column of its Table 5.1-1
No clear how to support new channel bandwidth added to existing operating bands in a manner of release independent from Rel-15.

## Slide 4: Issue – 1 (Cont’d)
Option 1: For TS 38.307 Rel-15, duplicate Annex Table B.4.1-1 and Table B.4.3-1 of TS 38.307 Rel-16, and update the pointers in the fourth column of Table 5.1-1 for FR1, Table 6.1-1 for FR2
Option 2: Change the Fourth column header from “Requirements to be fulfilled (see TS 38.307 of the release in which the band was introduced)” to “Requirements to be fulfilled ”
Option 322: No change on TS 38.307 Rel-15
Other options not precluded

## Slide 5: Issue - 2
In TS 38.307 (Rel-15 or Rel-16), there is no information on whether the release independent items are supported optionally or mandatorily. So there is an issue raised on whether or not to capture optional or mandatory support in TS 38.307:
Option 1: Capture optionality of release independence support in TS 38.307
  Option 1a: add a new column in each table indicating optionality
  Option 1b: add a sentence indicating a default optionality in Section 4, and if there is an exception, add a note in the corresponding table
  Option 1c: other option not precluded
Option 2: Do not capture optionality in TS 38.307