## Slide 1: WF on CSI-RS configuration and intra/inter-frequency measurements definition for CSI-RS based L3 measurement
CATT
3GPP TSG-RAN WG4 Meeting #94ebis R4-2005355
Electronic Meeting, Apr.20th – Apr.30th 2020

## Slide 2: WF on CSI-RS configuration for measurement requirement
Define requirements for CSI-RS configuration with {D=3 with PRBs ≥ 48}. FFS whether to define requirements for {D=1 with PRBs ≥ 96}.
Not define additional CSI-RS based measurement requirement

## Slide 3: WF on MO configuration
MO configuration
  Case 1: all CSI-RS resources in the same MO have the same center frequency, BW, SCS, CP type configured.
  Case 2: all CSI-RS resources in the same MO have the same center frequency, SCS, CP type configured. BW can be different.
Not define RRM requirements for Case 2 in Rel-16.
The CSI-RS configurations in the same MO share the same intra/inter-frequency definition
FFS the SSB and CSI-RS configured in the same MO share the same intra/inter-frequency definition

## Slide 4: WF on CSI-RS based intra-frequency and inter-frequency measurement definition
When CSI-RS resource of serving cell is available
  CSI-RS based intra-frequency measurement: a measurement is defined as a CSI-RS based intra-frequency measurement provided that:
    the SCS of CSI-RS on the serving cell and neighbor cell is the same, and
    the CP type of CSI-RS on serving cell and target cell is the same, and
      It is applied for SCS = 60KHz
    Option 1 (Intel, MTK, Huawei, Apple, OPPO)
      the centre frequency of CSI-RS resources on the target cell configured for measurement is the same as centre frequency of CSI-RS resource on the serving cell indicated in servingCellMO
    Option 2 (ZTE, QC, CATT, NEC, Nokia, DOCOMO)
      the centre frequency of CSI-RS resources on the target cell configured for measurement is the same as centre frequency of CSI-RS resource on the serving cell
      Common understanding: centre frequency of CSI-RS resource on the serving cell is indicated in servingCellMO
  CSI-RS based inter-frequency measurement: a measurement is defined as a CSI-RS based inter-frequency measurement if it is not a CSI-RS based intra-frequency measurement
When CSI-RS resource of serving cell is not available
  Option 1: All MO are inter-frequency (ZTE, vivo, Apple, CATT, NEC, DOCOMO)
  Option 2: No requirement is applied (Apple, Nokia, CATT, Qualcomm, MTK)
  Other options are not precluded

## Slide 5: WF on requirement for scenarios
Define intra-frequency requirements for the scenarios
  all CSI-RS resources in the same MO have the same BW
  the BW of the CSI-RS on the neighbor cell is within the active BWP of the UE
  FFS: No requirement is defined when the BW of intra-MO is different from that of the CSI-RS resources configured for the serving cell in Rel-16
Define inter-frequency requirements for the scenarios
  all CSI-RS resources in the same MO have the same BW
  FFS the BW of the CSI-RS on the neighbor cell is not completely contained or within in the active BWP of the UE

## Slide 6: WF on pre-emption on CSI-RS L3 measurement
RAN4 common understanding: the indication by the DCI format 2_1 is not applicable to receptions of CSI-RS for L3 measurement.

## Slide 7: WF on synchronization assumption for CSI-RS measurement
For CSI-RS measurement without associated SSB, it depends on whether to define the requirement for this case.
For CSI-RS measurement with associated SSB,
  Option 1: study this issue in performance part rather than work on the sync assumption in core part. (QC, MTK)
  Option 2: UE is assumed to use the timing of the detected SSB, and the CSI-RS measurement requirements is not conditioned on network synchronization. (Nokia, CATT, Huawei, CMCC)
  Option 3: the timing error is less than [X]us, where X is 3~4us (DOCOMO)
  Option 4: MRTD value for intra-band CA can be reused
  Option 5: less than CP length (LGE)
  Option 6: less than CP/2 length (Apple)