## Slide 1: WF on Rel-16 NR HSTUL TA BS demodulation requirements
ZTE
3GPP TSG-RAN WG4 Meeting #94-e-Bis
E-meeting, 20th – 30th Apr., 2020
R4-2005536

## Slide 2: Agreements from Round-1 discussion
Organisation of high-speed train requirement sections for UL TA 500kph in specifications.
  All UL timing alignment scenarios captured in the section used for scenario Y.
Relationship between TDD and FDD requirements
  Same requirements applicable for FDD and TDD; only one case simulated for result delivery. Parameter tables show SRS mapping for FDD and TDD separately.
Test metric
  Keep previous agreement. 70%TPUT only.
New scenarios
  Specify the 500kph UL TA scenario “Z”, with the following parameters: Channel model: Stationary UE: AWGN, Moving UE: AWGN. UE speed: 500 km/h. A: 15 kHz: 10 us, 30 kHz: 5 us, delta_omega: 15 kHz: 0.18 s-1, 30 kHz: 0.36 s-1.
l0 with PUSCH mapping type B
  Not required to be captured, as type B always has DM-RS in the first OFDM symbol of the TDRA.

## Slide 3: Issue 1: Organization of HST requirements for UL TA 500kph in specs
Organisation of high-speed train requirement sections for UL TA 500kph in specifications.
  Option 1: Requirements for different scenarios captured in same table.
  Option 2: Requirements for different scenarios captured in separate tables.

## Slide 4: Issue 2: High speed support declaration
High speed support declaration for HST UL TA
  Option 1: If 500kph UL TA scenarios are defined, Declare category of supported maximum speed. This can be either 350 or 500kph (or no HST support). If 500kph is supported and successfully tested, then 350kph does not need to be tested.
  Option 2: If 500kph UL TA scenarios are defined, Declare category of supported maximum speed. This can be either 350 or 500kph (or no HST support). If 500kph is supported, both 350kph and 500kph need to be tested for compliance.
  Option 3: If 500kph UL TA scenarios are defined, Declare category of supported design target speed(s). This can be 350 or 500 or 350&500kph (or no HST support). Only the corresponding requirements are tested.

## Slide 5: Issue 3: High speed support declaration and applicability for 120kph HST UL TA
High speed support declaration and applicability for 120kph HST UL TA (Pending on decision on Scenario X)
  Option 1: If performance requirement for scenario X is defined, the corresponding performance requirements should be tested when BS declares to support scenario X.
  Option 2: BS can declare support for either [no HST/default/no declaration], [350kmp] or [500kmp]. If BS declare [no HST/default/no declaration], scenario X is considered.
  o Option 3: No declaration for scenario X is needed. (Same approach as LTE).

## Slide 6: Issue 4: Re-use of high speed support declaration for HST UL TA
Re-use of high speed support declaration for HST UL TA (Pending on decision on Scenario X)
  Option 1: Introduce a new declared item “Maximum supported speed”, either 350km/h or 500km/h, for HST PUSCH, HST PRACH and UL TA.
  Option 2: If UL TA and PUSCH high speed declaration possibilities match, then they should be shared between PUSCH UL TA and PUSCH HST.

## Slide 7: Issue 5: New scenarios
New scenarios
  Option 1: Additionally, specify scenario “X”, with the following parameters: 15KHz SCS: A= 10us, Δω =0.04 s-1; 30KHz SCS: A= 5us, Δω =0.08 s-1.
  Option 2: Additionally, specify scenario “X”, with the following parameters: 15KHz SCS: A= 10us, Δω =0.04 s-1; 30KHz SCS: A= 5us, Δω =0.08 s-1. with the applicability rule: BS can declare support for either [no HST/default/no declaration], [350kmp] or [500kmp]. If BS declare supporting of 500km/h，only scenario Z is considered. If BS declare supporting of 350km/h，only scenario Y is considered. If BS declare [no HST/default/no declaration], scenario X is considered.
  Option 3: Do not specify scenario “X”.

## Slide 8: Issue 6: Additional SCS/CBW combinations
Additional SCS/CBW combinations
  Option 1: Add simulation assumptions for 5MHz CBW/15KHz SCS and 10Mhz CBW/30KHz SCS to simulation summary for agreed UL timing adjustment scenarios
  Option 2: No additional SCS/CBW combinations are required for UL TA requirements.