## Slide 1: WF on inter-band DL CA
Qualcomm,
R4-2005676
3GPP TSG-RAN WG4 Meeting #94Bis-e
Online, , 20th - 30th April 2020

## Slide 2: Way Forward on capability for beam management
CBM = common beam management between the band pair
IBM = independent beam management between the band pairs
How to distinguish between CBM and IBM band pairs is up for discussion in RAN4#95.
  Choose between two alternatives:
    A) per band pair capability to declare IBM or CBM
    B) IBM / CBM band pairs defined in specification.
Network does not assume CBM UE supports non-co-located deployment
Agreement on single AoA RF testing guarantees that also co-located deployment is supported by both IBM and CBM UEs

## Slide 3: CBM band pair requirements
Spherical coverage requirements method: Option 2 requirement on solid angle described by directions that simultaneously meet spherical coverage for both bands, per agreed WF R4-1916024, common area is 50 %
PSD difference between bands in Refsens i.e. peak EIS: 0 dB
PSD difference between bands in EIS spherical coverage: 0 dB
For LB + HB even with CBM, due to the difference in single band performance requirements, we consider option: Set untested band power level equivalent to EIS spherical coverage criterion. PSD is equal to difference between REFSENS and EIS spherical coverage criterion

## Slide 4: IBM band pair requirements
Spherical coverage requirements method: Option 2 requirement on solid angle described by directions that simultaneously meet spherical coverage for both bands, per agreed WF R4-1916024, common area is 50 %
PSD difference between bands in Refsens i.e. peak EIS:
  Agree PSD difference is within a range[6.5 – 25] dB and RAN4 aims to agree one number in RAN4#95
PSD difference between bands in EIS spherical coverage:
  Agree a range[6.5 – 25] dB and target to argee one number in RAN4#95