## Slide 1: Motivation for a new basket WI to cover adding new channel BW support in existing bands
Ericsson
R4-2007516
3GPP TSG-RAN WG4 Meeting #95-e
Electronic meeting, 25th May – 5th June, 2020
Agenda item: 14.2.1

## Slide 2: Motivation
Many NR FR1 bands were re-farmed from LTE considering only LTE channel bandwidth (up to 20MHz).
Operators have larger allocated spectrum and would expect deploying BS/UEs supporting higher NR channel bandwidth for a more efficient use of their available spectrum.
Many requests to add wider channel bandwidth and SCS
  In Rel-16:
    n1: 25, 30, 40 and 50 MHz
    n7: 25, 30, 40 and 50 MHz
    n25: 25, 30, 35 and MHz
    n28: 30 and 40 MHz
    n38: 25, 30, 40 and 50 MHz
    n41: 30 MHz
    n75: 25, 30, 40 and 50 MHz
    n77-n78: 25, 30 and 70 MHz
    n3: 40MHz
    n5: 25 MHz
    n65: 50MHz
  In Rel-17:
    n41: 70MHz
    n48: 70 MHz
Need to easily manage new request while work is already on-going for the same band:
  E.g. band n38: WID has been agreed to add 40MHz only, but there was a new request to add 25 and 30 MHz: we had separate WIs in parallel while it was the same band.
  Idem for band n1 with 30, 40 and later request of 25 MHz and 50MHz, we ended up with 2 separate WIs.

## Slide 3: Motivation
Specifications impacts are very similar for all cases:
  TS 38.104:
    Update CBW/SCS table
  TS 38.101
    Update CBW/SCS table
    A-MPR / NS signalling
    REFSENS requirement
Introducing a basket WI would highly reduce overhead and CRs management.
This has been discussed in RAN4 and was well received:
  Way Forward R4-1912984 was approved, the proposed basket WI captures related agreements.

## Slide 4: Motivation adding 70MHz CBW in bands n41
The amount of spectrum owned by T-Mobile USA varies throughout the US, with 70MHz contiguous in some places.
60 and 80MHz channel BW are already supported in 38.101-1.
70MHz channel BW is already supported by BS.

## Slide 5: Motivation adding 70MHz CBW in bands n48
70MHz has already been added to bands n77 and n78. It would make sense to add it also for n48 then.
No major issue is expected when adding support for this channel BW.