## Slide 1: WF on rough/fine beam assumption, for RRM Test cases
Anritsu
3GPP TSG-RAN WG4 Meeting #95-e
Online, 25 May – 05 June, 2020
R4-2008538

## Slide 2: Background
The assumption about UE beam type in RRM test cases was provided in R4-1904784 from Huawei at RAN4#90bis, Apr 2019.
  R4-1904784 was approved at RAN4#90bis, and supplemented by chairman’s notes information in the meeting report R4-1905301
  The FR2 UE beam assumption was not recorded in the 38.133 A.x RRM test cases
  An assumption about UE beam type is required to design the test case (and for ongoing updates of FR2 test cases to make them implementable by RAN5)
  RAN5 needs to know the UE beam assumption to analyse the effect of uncertainty and derive the final test limits.
  Draft 38.133 CR for A.7.3, A.7.4, A.7.7 in R4-2005285 which adds UE Beam assumption for selected RRM Test cases, was endorsed at RAN4#94-e-Bis

## Slide 3: Update of TS 38.133 Annex A RRM Test cases
RAN4#95 status:
  R4-2007176 Table 1 endorsed at RAN4#95e, with latest beam assumptions
  R4-2006387 CR for A.5.3, A.5.4, A.5.7 agreed at RAN4#95e (13 TCs, Anritsu)
  R4-2006389 CR for A.7.3, A.7.4, A.7.7 agreed at RAN4#95e (20 TCs, Anritsu, update from RAN4#94e Bis version to align with R4-2007176, and remove FFS)
To be provided at RAN4#96, aligning with slides 4 to 9:
  CR for A.5.5 (29 TCs, Anritsu)
  CR for A.7.5 (25 TCs, Samsung)
  CR for A.5.6 (16 TCs, Huawei)
  CR for A.7.1, A.7.6 (18 TCs, Ericsson)

## Slide 4: Beam assumptions per type of test case, 1 of 6
Test case group number | Test purpose | Rough/fine beam | Note
1 | EN-DC cell search and L1 measurement period | Rough | 
2 | SA cell search and L1 measurement period | Rough | 
3 | EN-DC Timing accuracy and adjustment | Fine | 
4 | SA Timing accuracy and adjustment | Fine | 
5 | EN-DC TA accuracy | Fine | 
6 | SA TA accuracy | Fine | 
7 | EN-DC SSB RLM for PSCell IS and OOS | Rough | 
9 | SA SSB RLM for PCell IS and OOS | Rough | 
10 | Random access | Rough | 
11 | SSB based Intra-frequency RSRP accuracy for FR1 and FR2 | Rough | L3

## Slide 5: Beam assumptions per type of test case, 2 of 6
Test case group number | Test purpose | Rough/fine beam | Note
12 | EN-DC SCell activation/deactivation delay | Rough | 
13A | EN-DC CSI RLM for PSCell | Rough | 
13B | SA CSI RLM for PCell | Rough | 
14A | EN-DC interruptions due to DRX transition | Fine | 
14B | EN-DC interruptions due to deactivated SCell operations | Fine assumption for the interrupted cell | Rough assumption for the target SCell if it is interband with the PSCell
15 | EN-DC SFTD measurement delay | N/A | 
17A | Serving NR PSCell and target E-UTRA inter-frequency measurement with LTE PCell | N/A | 
17B | NR Pcell with target inter-RAT E-UTRA measurement | N/A | 
18A | EN-DC NR inter-frequency measurement | Rough | 
18B | SA NR inter-frequency measurement | Rough | 

## Slide 6: Beam assumptions per type of test case, 3 of 6
Test case group number | Test purpose | Rough/fine beam | Note
19 | SSB Inter-frequency RSRP accuracy for FR1 and FR2 | Rough | 
20A | EN-DC interruptions at UL carrier RRC reconfiguration | N/A | 
20B | EN-DC interruptions due to active BWP switching | Fine | 
20C | EN-DC interruptions due to measurement on deactivated SCell | Fine assumption for the interrupted cell | Rough assumption for the target SCell if it is interband with the PSCell
21A | SA interruptions at SCell addition/release/activation/deactivation | Fine assumption for the interrupted cell | 
21B | SA interruptions at UL carrier RRC reconfiguration | N/A | 
21C | SA interruptions due to Active BWP switching | Fine | 
21D | SA interruptions due to measurement on deactivated SCell | Fine assumption for the interrupted cell | Rough assumption for the target SCell if it is interband with the PSCell
25 | EN-DC/SA SSB RLM scheduling restriction and impact on mobility | Rough | Need ensure that the control channel performance is good enough.
26A | NR-NR Handovers | Rough | 

## Slide 7: Beam assumptions per type of test case, 4 of 6
Test case group number | Test purpose | Rough/fine beam | Note
26B | NR handovers to other RATs | N/A | 
27 | RRC Re-establishment | Rough | 
28 | RRC Release with redirection to NR/E-UTRAN | Rough | 
29A | Beam management: L1-RSRP reporting | Rough | 
29B | Beam management: Beam failure detection and link recovery procedure | Rough | 
30 | EN-DC SFTD measurement accuracy | N/A | 
31 | Intra-freq RSRQ accuracy for FR1 and FR2 | Rough | 
32 | Inter-freq RSRQ accuracy for FR1 and FR2 | Rough | 
34 | BWP switching interruptions on E-UTRA serving cells in EN-DC | N/A | 
35 | BWP switching delay | Fine | 

## Slide 8: Beam assumptions per type of test case, 5 of 6
Test case group number | Test purpose | Rough/fine beam | Note
36 | NR PSCell addition and release in EN-DC | Rough | 
37 | UL carrier RRC reconfiguration delay | N/A | 
38 | SA RRC_Idle/inactive cell reselection NR to NR (FR1) | N/A | 
39 | EN-DC/SA beam failure detection and recovery and scheduling restriction | Rough | Need ensure that the control channel performance is good enough.
40 | SA/EN-DC SS-SINR measurement accuracies | Rough | 
42 | TCI switch delay | Rough | May need fine beam depending on which channel to be switched to.
43A | SA NR inter-RAT E-UTRAN RSRP measurement accuracy test cases | N/A | 
43B | SA NR inter-RAT E-UTRAN RSRQ measurement accuracy test cases | N/A | 
43C | SA NR inter-RAT E-UTRAN SINR measurement accuracy test cases | N/A | 
46 | E-UTRAN cell reselection to NR target cell | FFS | Think further whether FR2 test cases will be introduced or not

## Slide 9: Beam assumptions per type of test case, 6 of 6
Test case group number | Test purpose | Rough/fine beam | Note
48 | E-UTRAN inter-RAT NR handover | Rough | 
49 | E-UTRAN inter-RAT NR measurement accuracy | Rough | 
Red text: changes from R4-1901179 (noted, RAN4#90) to R4-1904784 (approved, RAN4#90bis)
Blue text: merge of chairman’s notes decisions in RAN4#90bis meeting report R4-1905301
Green highlight indicates agreements