## Slide 1: WF on NR-U RRM (Part 3) Agreements and topics discussed in email thread: [95e][206] NR_unlic_RRM_3
Nokia, Nokia Shanghai Bell
3GPP TSG-RAN WG4 Meeting #95-e R4-2008575
Electronic Meeting, May 25 – June 5, 2020
Agenda Items: 6.1.5.11 and 6.1.5.12

## Slide 2
Agreements in RAN4 95e

## Slide 3: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-3-1: Assumption of Q in PBCH reading
Except for initial access, Q can be assumed to be always known at the UE

## Slide 4: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-4-1: To define scheduling restrictions during SS-RSRP, SS-SINR and SS-RSRQ measurement
RAN4 to define scheduling restrictions during SS-RSRP, SS-SINR and SS-RSRQ measurements in NR-U

## Slide 5: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-5-2: L1-RSRP reporting delay for semi-persistent CSI reporting with PUSCH
For semi-persistent CSI (L1-RSRP) reporting, reuse the Rel-15 reporting delay

## Slide 6: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-6-1 Event triggered reporting delay
Issue 2-6-2 Event triggered periodic, and periodic reporting delay
Reuse Rel-15 delay, clarifying that this measurement reporting delay excludes a delay, which is caused by no UL resources being available for UE to send the measurement report on, and all delays due to UL LBT failures until the successful transmission of the report.

## Slide 7: Topic #3: RSSI and CO measurements in NR-U
Issue 3-1-1: Intra-frequency and inter-frequency RSSI definition
An intra-frequency RSSI measurement is defined when:
  RSSI channel BW is contained within the channel/carrier BW of the UE.
Further study whether to include SCS conditions into the definition and how to handle RSSI measurements under assumption of different SCS in RSSI, active BWP, etc.
Options discussed in RAN4 95:
  Option 2a: RMTC configured SCS is the same as the SCS of active BWP
  Option 2b: the SCS of the RSSI measurement is the same as the SCS of an intra-frequency SSB or CSI-RS
  Option 2c: No additional condition is needed.
  Option 2d: the SCS configured for the RSSI measurement is the same as the SCS of a serving cell, where the SCS of a serving cell is FFS.

## Slide 8: Topic #3: RSSI and CO measurements in NR-U
RAN4 requirements will be defined for all RMTC configurations.

## Slide 9: Topic #3: RSSI and CO measurements in NR-U
Issue 3-2-1: CSSF definition
  At least for CSSF within measurement gaps, CSSF needs to be adapted for NR-U to account for RSSI measurements in RMTC in addition to other NR-U measurements in SMTC.
  FFS: whether CSSF needs to be adapted for CSSF outside measurement gaps.

## Slide 10: Topic 1 – SFTD measurements
Issue 1-1 Maximum scaling of inter-RAT SFTD measurements
Candidate options:
  Option 1: k = 3
  Option 2: k = 4

## Slide 11: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-1-2: Value of N
N is not specified explicitly but determined by the existing procedures, e.g., the UE can reattempt the measurements until the earlier agreed 8 seconds limit (during which the undetectable cell can remain known) expires

## Slide 12: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-4-5: Scheduling restriction of UE performing measurements with a different subcarrier spacing than PDSCH/PDCCH.
  In NR-U, the scheduling restriction of UE performing measurements with a different subcarrier spacing than PDSCH/PDCCH (clause 9.2.5.3.2 in TS 38.133) is applicable.
  FFS: scheduling restriction to intra-band and inter-band CA.

## Slide 13: Topic #3: RSSI and CO measurements in NR-U
Issue 3-1-2: Need of measurement Gaps during RSSI measurements
Measurement gaps are needed at least when:
  RSSI BW is not fully within the active BWP of the UE.
o FFS: if another condition is needed.

## Slide 14: Topic #3: RSSI and CO measurements in NR-U
Issue 3-3-1: RSSI Reporting criteria
With Ecat=1, 1 report for RSSI and channel occupancy measurements is capable of 1 RSSI measurement and 1 channel occupancy measurement over a channel [TS 37.213] with CCA.

## Slide 15: Issues that need further discussion

## Slide 16
The intention of this part of the Way forward is to list the options discussed during RAN4 95e. Companies are encouraged to provide input to the topics in this Section.

## Slide 17: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-1-1: UE behaviour in case of successively exceeding the maximum number of DL LBT failure during measurements
After N unsuccessful measurement attempts of an already identified cell due to exceeding the max number of unavailable SMTC occasions, UE shall stop the measurement attempts on this SSB.
  The UE cannot measure this SSB again without first detecting it.
  FFS: whether UE shall restart directly from detection stage again for this SSB or the UE performs the detection procedure like for any other SSB.

## Slide 18: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-2-1: UE behaviour in RRC_CONNECTED mode when the serving cell is unavailable for consecutive SSB bursts
Candidate options:
  Option 1: UE shall initiate measurements on neighbour cells indicated by the serving cell if it is unable to measure the serving cell for consecutive SSB bursts.
  Option 2: After no SSBs of a cell can be received during up to 8 seconds, the cell will not be considered as detectable and the Rel-15 UE behavior will apply. No other UE behavior or requirement on the consecutive SSBs in the serving cell is needed.

## Slide 19: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-4-2: Applicability of the signaling of SMTC2 to NR-U
Candidate Options
  Option 1: The signaling of smtc2 is not applicable in unlicensed band.
  Option 2: Signaling of smtc2 is applicable to unlicensed band.
  Option 3: Send a LS to RAN1/RAN2 about this issue.

## Slide 20: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-4-3: Different scheduling restriction when deriveSSB_IndexFromCell is enabled, or not enabled, during SS-RSRQ measurements.
Issue 2-4-4:Different scheduling restriction when deriveSSB_IndexFromCell is enabled during SS-RSRP and SS-SINR measurements
Candidate Options:
  Option 1: In NR-U, scheduling restriction should depend on the signaling of deriveSSB_IndexFromCell.
  Option 2: No differentiation on the scheduling restriction for when deriveSSB_IndexFromCell is enabled or not.

## Slide 21: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-4-6: Scheduling restriction during RSSI/CO measurements
Candidate Options:
  Option 1: Define scheduling restriction during RSSI/CO measurements and differentiate the cases where deriveSSB_IndexFromCell is enabled or not for the definition of scheduling restrictions during RSSI/CO measurements.
  Option 2: Define scheduling restriction during RSSI/CO measurements and do not define differentiation between the cases in which deriveSSB_IndexFromCell is enabled or not for the definition of scheduling restrictions during RSSI/CO measurements
  Option 3: No need to define scheduling restrictions for RSSI measurements in NR-U.

## Slide 22: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-5-1: UE behavior when receiving the MAC CE deactivation command for semi-persistent CSI reporting, in case of UL LBT failure for sending the ACK
Candidate Options:
  Option 1: Option 1: Detailed UE behavior when receiving the MAC CE deactivation command for semi-persistent CSI reporting, in case of UL LBT failure for sending the ACK
    If UE cannot transmit HARQ-ACK on MAC-CE deactivation due to UL CCA failure, UE continues to be in its previous state, i.e., it should measure and report L1-RSRP until it successfully transmits HARQ-ACK
  Option 2: UE should stop the semi-persistent CSI reporting when UE cannot transmit HARQ-ACK for MAC CE deactivation command.

## Slide 23: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-5-3: L1-RSRP reporting delay for semi-persistent CSI reporting with PUCCH
Candidate Options
• Option 1: For semi-persistent CSI reporting with PUCCH, if UE cannot transmit HARQ-ACK on the MAC CE deactivation due to the UL LBT failures, UE delays the CSI reporting.
  o If UE does not receive the deactivation command during the delay period, UE restarts to transmit the delayed CSI reporting. FFS how to extend the delay.
  o If UE receive the deactivation command and can transmit HARQ-ACK, the UE abandon the stored CSI.
• Option 2: For semi-persistent CSI reporting using PUCCH, the reporting delay reuses Rel15 reporting delay.

## Slide 24: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-5-4 CSI-RS based L1-RSRP measurement
RAN 4 is waiting for the conclusion in RAN1.

## Slide 25: Topic #2: Remaining issues in intra and inter-frequency measurements
Issue 2-7-1 Different requirements for LBE (dynamic channel access) and FBE (semi static channel access)
Issue 2-7-2 Number of candidate SSBs the UE is required to monitor during intra and inter-frequency measurements
Issue 2-7-3 Number of candidate SSBs the UE is required to monitor during intra and inter-frequency cell detection
  The discussions were deprioritized in RAN4 95, since RAN4 did not get any LS from RAN1.

## Slide 26: Topic #3: RSSI and CO measurements in NR-U
Issue 3-2-2: RSSI measurement period
The RSSI and CO measurement period depends at least on:
  max(reportInterval, rmtc-Period) in non-DRX when measurement gaps are not required,
  max(reportInterval, rmtc-Period, DRX) in DRX when measurement gaps are not required, or
  max(reportInterval, rmtc-Period, MGRP and gap sharing) in DRX when measurement gaps are required.
For RSSI measurement within measurement gap, measurement period is scaled with CSSFwithin_gap,i
For RSSI measurement outside measurement gap, measurement period is scaled with CSSFoutside_gap,i
FFS: For UE not capable of wideband operation in NR-U, RSSI measurement period scales with the number of MOs not requiring measurement gap according to CSSFoutside_gap,I, CCA
FFS: Whether the scaling factor of 1.5 shall be used if DRX ≤ 320ms

## Slide 27: Topic #3: RSSI and CO measurements in NR-U
Issue 3-4-1: RSSI measurement bandwidth
Candidate options:
  Option 1: RSSI measurement bandwidth is the LBT bandwidth (which is already decided by RAN1 and specified in TS 38.215).
  Option 2: RAN4 discuss this in the performance requirements.