## Slide 1: 3GPP TSG-RAN WG4 Meeting #95-e Electronic Meeting, 25 May – 5 June, 2020
Huawei, HiSilicon
WF on requirements for RSTD and UE Rx-Tx time difference measurement
R4-2008664

## Slide 2: Definition of intra/inter-frequency measurement
Do not define intra/inter-frequency definition for PRS-RSTD
  Note: Accuracy may be different depending whether the measurements are done on the same positioning frequency layer or not.
Do not define intra/inter-frequency definition for PRS-RSRP
  Note: Classification of accuracy requirements is FFS (e.g. whether to define different accuracy for measurements on different frequencies)
Do not define intra/inter-frequency definition for UE Rx-Tx timing difference
  Note: Classification of accuracy requirements is FFS (e.g. whether to define different accuracy for measurements on different frequencies)

## Slide 3: Scenarios for the requirements
RAN4 requirements are to be defined only for the case where PRS is measured with configured measurement gap
  This applies for RSTD, PRS-RSRP and UE Rx-Tx time difference
For UE Rx-Tx time difference, RAN4 requirements are to be defined at least for the case where the positioning SRS resource is on the same band as PRS frequency layer
  FFS: if requirements are to be defined for the case where the positioning SRS resource is in a different band from PRS frequency layer

## Slide 4: Measurement period for RSTD (1)
PRS occasion definition:
  Option 1: PRS occasion is the time duration spanned by one DL PRS resource after repetition by DL-PRS-ResourceRepetitionFactor ± its corresponding DL-PRS-expectedRSTD-uncertainty.
  Option 2: PRS occasion is one single DL PRS repetition (i.e. repetition factor of 1)
  Option 3: PRS occasion is one comb pattern without being repeated within a slot and without applying a resource repetition factor (Ericsson)
Basic number of PRS occasions
  Option 1. A certain number (X) of PRS occasions, X=4
  Option 2. ceil(NPRS,req / KPRS)
    NPRS,req is the comb pattern realizations that are required for RSTD measurement, derived from simulation results
    KPRS= LPRS/CombSizeN  ResourceRepetitionFactor is the number of comb pattern realizations within a single TPRS,
    LPRS is the number of PRS symbols per slot

## Slide 5: Measurement period for RSTD (2)
FFS: Periodicity of PRS measurement
  Option 1.
  Option 2.
  other options not precluded
    Companies are encouraged to check on all possible values for T, Tprs and MGRP
FFS: Sampling and processing time
  Option 1: T
  Option 2.
  other options not precluded

## Slide 6: Measurement period for RSTD (3)
FFS: Scaling of PRS occasions due to UE processing capability
  Option 1.
  Option 2. Depends on T and Tprs
    , if Tprs <= T
    , of Tprs > T
  Option 3.
  other options not precluded
  FFS: requirements do not apply for resources spanning over two sampling periods of N
  FFS: requirements apply provided that the configured PRS duration K is no larger than N
FFS: Calculation of PRS occasion duration
  Option 1. RAN4 to define RSTD measurement period based on Type 2 PRS duration calculation. RSTD measurement period for Type 1 PRS duration calculation shall be no longer than Type 2.
  Option 2. measurement period requirements are defined based the type (type 1 or type 2) as UE used to report {N,T}
  other options not precluded

## Slide 7: Measurement period for RSTD (4)
For FR1, no impact of UE RX beam sweeping on RSTD measurement period shall be considered
For FR2
  Use Rx beam sweeping factor similar way as in SSB-based RRM (i.e. no intra-PRS-occasion Rx beam sweeping) for the case when the QCL information is not available to the UE
  FFS how to handle the case when the QCL information is available to the UE
    Option 1: Do not perform RX beam sweeping
    Option 2: Perform RX beam sweeping
  Solutions with more advanced RX beam sweeping can be considered in the future releases

## Slide 8: Measurement period for RSTD (5)
FFS Measurement period with multiple PRS periodicities
  Option 1. Use the maximum PRS resource periodicity among all PRS resources
  Option 2. LMF needs not to provide multiple PRS periodicity to UE with a single layer at least
  other options not precluded
FFS Measurement period with multiple PRS frequency layers
  Option 1. Measurement periods adds up for each frequency layer that is configured to be measured
  Option 2. Measurement period is scaled by number of frequency layers
  Option 3. Based on CSSF

## Slide 9: Measurement period for RSTD (6)
Extension of measurement period due to HO
    k is the number of times the handover occurs during
    is the time during which the RSTD measurement may not be possible due to handover.
FFS Whether PRS occasion dropping due to SSB collision should be accounted in measurement period
  Option 1. Yes
  Option 2. No, measurement period will be defined for cases when PRS occasions are not dropped for any reason
FFS Measurement period exceeding responseTime
  Option 1. Extension of positioning measurement period due to HO shall not exceed responseTime. UE behaviour in such case is FFS.
  Option 2. No RAN4 impact
  Option 3. Measurement period requirements on measurement period is independent of responseTime

## Slide 10: Measurement period for UE Rx-Tx time difference (1)
FFS: Whether SRS periodicity should be accounted in Rx-Tx time difference measurement period
FFS: Whether SRS dropping should be accounted in measurement period
FFS: Measurement period with HO
  Option 1. When the UE Rx-Tx time difference measurement period is extended, the extension depends on the number of serving cell changes and on the corresponding interruption time
  Option 2. UE should re-start the Rx-Tx time difference measurement after cell change
FFS: whether UE shall continue the UE Rx-Tx time difference measurement during which timing adjustment for its UL transmissions, autonomous adjustment or based on configured TA, occurred one or more times
  FFS: for UE autonomous adjustment and for network issued TA change
  Consider the issue together with gNB Rx-Tx time difference measurement behavior

## Slide 11: Measurement period for UE Rx-Tx time difference (2)
FFS: Proximity between SRS and PRS
  Option 1. The measurement requirements for UE Rx-Tx timing difference is applicable only if the configured parameters SRS-Slot-offset and SRS-Periodicity for SRS resource for positioning are such that any SRS transmission is within [-25, 25] msec of at least one DL PRS resource of each of the TRPs in the assistance data
  Option 2. Rx-Tx timing difference measurement period requirements apply provided that there is at least one SRS transmission within the measurement period.
  Option 3. The requirements for UE Rx-Tx apply regardless of the time separation between SRS and PRS. If the closest subframes #i and #j are separated by more than ½ subframe, the UE shall compensate for the difference in the received timing of radio frame #i used for TUE-TX estimation and the subframe #j.
  Other options not precluded

## Slide 12: Measurement capability
FFS: RAN4 not define measurement capability requirements for PRS measurement
FFS: Requirements when PRS configuration in assistance data exceeds reported capabilities
FFS: If the time span of a DL PRS resource instance (i.e., the time duration spanned after repetition by DL-PRS-ResourceRepetitionFactor) ± its corresponding DL-PRS-expectedRSTD-uncertainty is greater than , where is the duration of DL PRS symbols in ms that UE is capable of processing, measurement requirements do not apply.

## Slide 13: Reporting criteria
RSTD reporting criteria: Ecat = 1, one report which includes RSTD measurements and PRS-RSRP measurements (if configured with RSTD and supported by UE).
UE Rx-Tx reporting criteria: Ecat = 1, one report which includes UE Rx-Tx time difference measurements and PRS-RSRP measurements (if configured with UE Rx-Tx time difference and supported by UE).

## Slide 14: Side condition
FFS: Side condition for RSTD measurement in FR2
  Option 1. PRS SNR of reference cell to be -3 dB and the side condition for PRS SNR of neighbor cells to be -10 dB.
  Option 2. Side conditions for PRS RSTD measurements in FR2 are defined same as those in FR1, i.e. -13dB for neighbour cell and -6dB for serving cell.

## Slide 15: Measurement accuracy (1)
FFS: Number of samples for RSTD accuracy
FFS: Number of samples for UE Rx-Tx time difference accuracy
FFS: Whether RSTD and UE Rx-Tx accuracy is agnostic to comb
  Companies are encouraged to study the impact of number of symbols within a slot
FFS: Assumption on antenna panel in defining accuracy requirements

## Slide 16: Measurement accuracy (2)
FFS: Serving vs. neighbour for Rx-Tx time difference accuracy
  Option 1. Only one set of accuracy requirements applicable to both serving and neighbor cells to be defined.
  Option 2. Specify UE Rx-Tx time difference accuracy requirements for serving cell and for neighbor cell separately
UE Rx-Tx time difference accuracy requirements do not apply under TA change during the measurement period
UE Rx-Tx time difference accuracy requirements do not apply under NTA_offset change during the measurement period
  FFS: whether/how this needs to be captured in the specification
FFS: UE Rx-Tx time difference accuracy requirements do not apply with HO during the measurement period

## Slide 17: Report mapping (1)
Relation between k1 and k2
  Option 1.
    is the positioning layer frequency layer index of all RSTD measurements of the same TRP pair.
  Option 2. k2 >= k1
  Option 3. RAN4 not to define relationship between k1 and k2
  Option 4. k2 <= k1
  Option 5. UE shall report based on the finest granularity it can achieve
Applicable values for k in FR1
  Option 1. {1,2,3,4,5}
  Option 2. {2,3,4,5}
  Option 3. {0,1,2,3,4,5}
  Option 4. {3,4,5}

## Slide 18: Report mapping (2)
Report mapping for differential RSTD and Rx-Tx time difference
  Option 1. Allow different ranges for different k values
  Option 2. Ensure the same range for all k’s, e.g., by increasing the last reporting interval to 8192 for all k values
Report mapping for additional path
  Option 1. Allow different ranges for different k values
  Option 2. Ensure the same range for all k’s, e.g., by increasing the last reporting interval to +/- 8175 for all k values

## Slide 19: MG and Scheduling restriction
FFS: It is up to UE implementation to request measurement gaps for PRS measurement.
FFS: If UE requested measurement gaps for PRS measurement but the gaps are not configured, UE is not expected to measure PRS
FFS: If UE did not request measurement gaps for PRS measurement, UE is expected to process DL PRS in the same OFDM symbol where other DL signals and channels are transmitted to the UE