## Slide 1: Way forward for NR UE URLLC performance requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #95-e
E-meeting, 25 May – 5 June, 2020
Agenda Item: 6.9.1.2
R4-2008807

## Slide 2: High reliability (1)
      Background (Agreed parameters from #94e and #94e-Bis)
  SCS/CBW: ​
    FDD: 15 kHz/10 MHz​
    TDD: 30 kHz/40 MHz​
  TDD pattern: 7D1S2U, S=6D: 4G: 4U for 30 kHz SCS.​
  PDSCH configuration: Mapping type A, symbol length 12, starting symbol 2.​
  PDSCH Aggregation level: 2 for FDD and TDD
  Max number of HARQ transmissions: 4​
  Antenna configuration: 2x2 and 2x4, ULA low​
  Propagation condition: TDLA30-10​
  Target BLER: 1%​ (BLER is calculated after all transmission​)
  Target Confidence level: 99%​

## Slide 3: High reliability (2)
      Scheduling for PDSCH:
  FDD: No scheduling in slots 0 and 1 (or 19) within 20ms.
  TDD: No scheduling in D slots i, where mod(i, 10) = 0, and S slots
      MCS:
  Option 1: MCS13
  Option 2: MCS16
  Option 3: MCS19
Methodology for MCS selection
  Option 1: Higher or equal to -6 dB for average ideal 4 Rx SNR alignment results.
  Option 2: Higher or equal to -3 dB for average ideal 4 Rx SNR alignment results
  Option 3: Higher or equal to -4 dB for final 4 Rx requirement definition (average ideal SNR alignment result + IM)
      FR2 requirements for High reliability
  FFS whether to define FR2 requirements
  Interested companies are encouraged to bring more information and analysis for the deployment/usage scenarios

## Slide 4: PDSCH mapping Type B and processing capability 2 (1)
Background (Agreed parameters from #94e and 94e-bis)
  SCS/CBW:
    FDD: 15 KHz/10 MHz
    TDD: 30 KHz/ 40 MHz
  TDD pattern (30KHz SCS): DDDSU, S=10:2:2
  Slots to be scheduled:
    FDD: All DL slots with K1=0
    TDD: S slots with K1=0
  Starting symbol: 2
  Symbol length: 2
  Slot aggregation level: 1
  Max number of HARQ transmissions: 1
  Number of HARQ process for FDD: 2
  Channel model: TDLA30-10
  Antenna configuration: 2x2 and 2x4, ULA Low.

## Slide 5: PDSCH mapping Type B and processing capability 2 (2)
      PDSCH symbol length for FDD and TDD: 2os only
      Test metrics: 70% throughput
      Number of HARQ process for TDD:
  Option 1: 2
  Option 2: 4 processes and PDSCH scheduling with HARQ index 3
      MCS:
  Option 1: Only MCS 4
  Option 2: Only MCS 17
  Option 3: MCS 4 and MCS 17
      FR2 requirements for PDSCH mapping Type B
  Introduce test cases for FR2, FFS whether test applicable rules will be introduced.

## Slide 6: Pre-emption indication (1)
Background (Agreed parameters from #94e)
  No URLLC PI performance requirements
  Time frequency set: 14x1
  Number of symbols to be pre-empted: 2
  Starting symbol to be pre-empted: 3
  Test applicability for eMBB UE PI requirements: optional with UE capability signalling
  Antenna Configuration: 2x2 and 2x4, ULA low

## Slide 7: Pre-emption indication (2)
      Pre-emption scheduling: Fixed scheduling
      Pre-emption probability
  Option 1: 10% within 1 radio frame
  Option 2: 20% within 1 radio frame
      eMBB MCS
  Option 1: MCS13 in Table 1
  Option 2: MCS4 in Table 1
      Test metric
  Option 1: 70% of max T-put
  Other options are not precluded
      Companies are encouraged to prepare comparison analysis of UE with and without HARQ buffer flushing of pre-empted bits to decide on options above

## Slide 8: Pre-emption indication (3)
      Use the following parameters for eMBB PDSCH configuration
Parameter |  | Value
Duplex mode |  | FDD, TDD
Active DL BWP index |  | 1
PDSCH configuration | Mapping type | Type A
 | k0 | 0
 | Starting symbol (S) | 2
 | Length (L) | 12
 | PDSCH aggregation factor | 1
 | PRB bundling type | Static
 | PRB bundling size | 2
 | Resource allocation type | Type 0
 | RBG size | Config2
 | VRB-to-PRB mapping type | Non-interleaved
 | VRB-to-PRB mapping interleaver bundle size | N/A
PDSCH DMRS configuration | DMRS Type | Type 1
 | Number of additional DMRS | 1
 | Maximum number of OFDM symbols for DL front loaded DMRS | 1
Number of HARQ Processes |  | FDD: 4 TDD: 8
Maximum HARQ transmission |  | 4
The number of slots between PDSCH and corresponding HARQ-ACK information and TDD pattern |  | FDD: 2 TDD: FR1.30-1
CBW/SCS |  | FDD: 10/15 TDD: 40/30
RB allocation |  | Full bandwidth
MIMO layer |  | Rank 1
Propagation condition |  | TDLA30-10

## Slide 9: CQI reporting requirements (1)
      Propagation channel for CQI reporting
  Option 1: AWGN
  Option 2: Fading channel
      Target BLER in case AWGN conditions will be used
  Option 1: 10^-5
  Option 2: 10^-3
  Option 3: 10^-2
      Companies are encouraged to bring analysis whether static CQI/fading CQI test with non-ultra-BLER can serve test purpose

## Slide 10: CQI reporting requirements (2)
      Test metric in case AWGN conditions will be used
  Option 1: Reuse Rel-15 CQI test metric
  Option 2: Reuse Rel-15 CQI test metric and define a lower bound for median reported CQI in the CQI reporting tests
  Other options are not precluded
      Test metric in case Fading conditions will be used
  Option 1:
    A CQI index not in the set {median CQI -1, median CQI, median CQI +1} shall be reported at least α% of the time
    The ratio of the throughput with follow CQI vs median CQI shall be ≥ γ
  Other options are not precluded
      In case AWGN conditions with target BLER 10^-5 will be used, FFS feasibility to define CQI reporting test case and FMCS case at the same SNR and define an applicability rule between CQI reporting test and FMCS test

## Slide 11: Test applicability
      Test applicability for Rel-15 URLLC UE feature:
  The corresponding test applicability rules for the following features needs to be specified:
    PDSCH repetition (pdsch-RepetitionMultiSlots)
    PDSCH mapping type B (pdsch-MappingTypeB)
    PDSCH processing capability 2 (pdsch-ProcessingType2)
    new 64QAM MCS table for PDSCH (dl-64QAM-MCS-TableAlt)
    CQI table with target BLER of 10^-5 (cqi-TableAlt)
FFS whether UE URLLC requirements for Rel-15 features are release independent from Rel-15
FFS necessity of introduction of RAN4 features and UE applicability for URLLC requirements for Rel-15 features

## Slide 12: Specification layout
      How to capture URLLC features in specifications and structure for test cases capturing:
  Introduce new sections within the existing PDSCH requirements for each separate feature when incorporate URLLC requirements into the specification.
  Structure for test cases capturing: Reuse existing Rel-15 eMBB test case structure to capture new demodulation requirements from URLLC WI.

## Slide 13: CR work split for UE
Specification | Requirements title | Frequency range | CR work | CR Responsibility
UE demodulation and CSI (38.101-4) | Test applicability for all cases | FR1 | Test applicability | Huawei, HiSilicon
 |  | FR2 | FFS | FFS
 | FRC for all cases | FR1 | FRC | [Intel]
 |  | FR2 | FFS | FFS
 | Requirements for PDSCH with ultra-low BLER target (10-5) | FR1 | Requirements | [Ericsson]
 |  | FR2 | FFS | FFS
 | Requirements for PDSCH with aggregation factor configured | FR1 | Requirements | Huawei, HiSilicon
 |  | FR2 | FFS | FFS
 | Requirements for PDSCH for mapping Type B and processing capability 2 | FR1 | Requirements | [Qualcomm]
 | Requirements for PDSCH for pre-emption indication | FR1 | Requirements | [Ericsson]
 |  | FR2 | FFS | FFS
 | CQI reporting test for table 3 | FR1 | Requirements | [Apple]
 |  | FR2 | FFS | FFS