## Slide 1: WF on modifying the ED threshold
Nokia, Nokia Shanghai Bell
R4-2009048
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May 25th – June 5th 2020

## Slide 2: Background (1/4)
During RAN4#95e meeting one of discussed topic was energy detection accuracy for LAA/eLAA in based on submitted Tdoc [1] and corresponding CR [2] to TS 37.107 that includes core and performance requirements for shared spectrum access channel.
Historically all RAN4 requirements for shared spectrum access channel (i.e. LAA and eLAA requirements) were included in BS core specification TS 36.104 and BS conformance test specification TS 36.141. However, from Rel-15 onwards all details for share spectrum access channel were moved to newly introduced specification TS 37.107.
[1] R4-2007475 Discussion on interfering signal for conformance test for ED accuracy for eLAA, Nokia, Nokia Shanghai Bell
[2] R4-2007474, CR to TS 37.107 with correction to interfering signal for conformance test for energy detection accuracy to align with TS 37.213, Nokia, Nokia Shanghai Bell

## Slide 3: Background (2/4)
LAA/eLAA test procedure for energy detection threshold is describe in TS 37.213 v16.0.0 in subclause 4.1.5 with following formula for Xthresh_max :
:

## Slide 4: Background (3/4)
However, in performance part of channel access procedure test, that is described in TS 37.107 in subclause 6.1.4.2 point 6) the interfering signal shall be at the fixed level of (-72 dBm + 4 dB)/20MHz:
However such fixed interfering signal level for all frequency ranges within band 46 will cause conflicts with some regulatory requirements for 5 GHz unlicensed band. For example:
  For band 46b (5250 – 5350 MHz), without TPC (transmit power control), EIRP is limited to 20dBm in some regions and countries, which implies a maximum conducted power level (PTX) of 14dBm assuming a 6dBi antenna. The energy detection level for this power level is -63dBm per TS 37.213, however according tests description in TS 37.107 threshold of (-72dBm + 4dB) is specified.
Thus, the energy detection threshold allowed/mandated by TS 37.213 subclause 4.1.5, is not defined in the conformance test in TS 37.107 subclause 6.1.4.2, as conformance test may requires more stringer requirements to be tested than allowed by regulations.
:

## Slide 5: Background (4/4)
To resolve different regional requirements for maximum power allowed in 5GHz frequency range, future CR to TS 37.107 [2] is needed to adapt to RAN1 description for Xthresh_max instead of fixed value considering:
  3GPP compliance means regulatory compliance.
:

## Slide 6: Way forward
  Companies are encouraged to further check the issue of energy detection threshold accuracy test in conformance specification for shared spectrum access channel for next RAN4#96-e meeting.
  If decided to correct ED threshold accuracy test, to discuss and agree from which release modification should be introduce to specification:
    From Rel-15 onwards, consequently update should be introduce to TS 37.107
    From Rel-13, update should be introduce to TS 36.104 and TS 36.141 (Rel-13 and Rel-14)
: