## Slide 1: 3GPP TSG-RAN WG4 Meeting # 95-e Electronic Meeting, 25 May – 5 June, 2020
ZTE, [NTT DOCOMO]…
WF on simplification on band combinations in specification
R4-2009176

## Slide 2: Background(1/2)
How to handle the increasing number of new EN-DC configurations introduced into 38.101-3 spec has been discussed for several meetings [1,2,3]. Previous agreements on EN-DC simplification including FR2 was option 2-2 described in [1]:
New template proposal, i.e. replacing WORD table format with EXCEL table format, for band combination in basket WI in Rel-17 was agreed in [2] in RAN4 94e-bis meeting, and further refinement on excel format for band combinations can be found in [7].

## Slide 3: Background(2/2)
  In [3] in RAN4#94e-bis, the following problematic cases and solutions for the use of wildcard “@” for each band combination cases were specified.
    Case 0: Common for all cases from 1 to 5
    Case 1: LTE + FR2 Single carrier
    Case 2: LTE + FR2 intra-band contiguous CA
    Case 3: LTE + FR2 intra-band non-contiguous CA
    Case 4: LTE + FR2 inter-band CA
    Case 5: LTE + FR1 + FR2 inter-band CA
In RAN4 #95e, only solutions for EN-DC including FR2 intra-band contiguous and non-contiguous CA (i.e. case 2 and case 3) are given in [4] and discussed, but concerns are still raised by the companies for the use of wildcard according to [5]. In addition, for the other cases except case 2/3, there are no inputs/discussions in this meeting.
Moreover, a new discussion on applying excel format to band combination table in TS 38.101-1/2/3 is raised in [6], where the excel formats are based on [2].

## Slide 4: Wayforward (1/2)
For applying excel format to band combination table in [2] in TS 38.101-1/2/3.
  Option 1: Apply all band combinations table in TS 38.101-1/2/3
    Detail table formats are FFS
  Option 2: Apply part of band combinations table
    It is preferred to provide specific table and spec number.
  Option 3: Do not apply any band combinations table.

## Slide 5: Wayforward (2/2)
For using a wildcard
  Option 1: Use a wildcard to denote any intra-band contiguous and non-contiguous CA configurations for FR2 band if all the CA BW classes within a fallback group specified in TS 38.101-2 have been requested in the EN-DC configurations, as stated in [4].
    For the other cases except case 2/3, how to solve the issues by using a wildcard are FFS.
  Option 2: Use wildcard with further modification.
  Option 3: Do not use a wildcard.

## Slide 6: Reference
[1] R4-1910908, “Further discussion on EN-DC configuration including FR2”, NTT DOCOMO, INC.
[2] R4-2005168, WF on new format for band combinations, Huawei, HiSilicon
[3] R4-2005169 WF simplification on EN-DC including FR2, NTT DOCOMO, INC.,
[4] R4-2006840, Considerations on simplification of EN-DC configuration including FR2, ZTE Corporation
[5] R4-2008329, “Email discussion summary for [95e][139] BC_simplification”, Moderator (NTT DOCOMO)
[6] R4-2006626, Simplification of band combination tables in 38.101, Apple
[7] R4-200xxxx,WF on refinement on excel format for band combinations, Huawei, HiSilicon