## Slide 1: WF on IAB-MT unwanted emissions
Nokia, Nokia Shanghai Bell
R4-2009065
3GPP TSG-RAN WG4 Meeting #95-e
Electronic Meeting, May 25th – June 5th 2020

## Slide 2: Contributions in RAN4#95-e
R4-2006800, Samsung
R4-2007130, Qualcomm Incorporated
R4-2007576, Ericsson
R4-2007909, Huawei
R4-2007403, ZTE corporation
R4-2007120, Nokia, Nokia Shanghai Bell

## Slide 3: Way forward on FR1 IAB-MT relative ACLR
IAB-MT ACLR minimum requirement in FR1
  Wide area IAB-MT: 45 dBc
  FFS for Local area IAB-MT, make decision in Q3 2020:
    Option 1: 45dBc
    Option 2: 30dBc

## Slide 4: Way forward on OBUE and SEM
For FR2:
  Wide area IAB-MT: Wide Area IAB-MT shall meet [wide area] BS OBUE requirements
    We can further discuss how to capture the requirements into TS/TR.
  FFS for local area IAB-MT, make decision in Q3 2020
    Option 1: Using Local area BS OBUE requirements
    Option 2: Using UE specification requirements
For FR1
  Wide Area IAB-MT shall meet [wide area] BS OBUE requirements
    We can further discuss how to capture the requirements into TS/TR.
  FFS for local area IAB-MT
    Option 1: Using Local area BS OBUE requirements
    Option 2: Using UE specification requirements
FR1 and FR2 the boundary between in-band and spurious region
  Wide-area IAB-MT: follow BS requirements
  Local-area IAB-MT: FFS

## Slide 5: Way forward on absolute ACLR
Absolute ACLR to be discussed further in future meetings.

## Slide 6: Way forward on Tx spurious emissions
FR1/FR2 Tx spurious emissions
  Wide-area IAB-MT: The same spurious emissions requirements as base stations (category A and category B)
  Local-area IAB-MT:FFS