3GPP TSG-RAN WG4 Meeting # 97-e 															R4-2016871

Electronic Meeting, 2-13 Nov., 2020

Source: 	CATT

Title: 	TP on V2X_n40A-n47A coexistence study

Agenda item:	10.19.2

Document for:	Approval

## 1	Introduction

This contribution provides the co-existence studies for the band combinations, i.e. V2X _n40A-n47A. Specifically, the harmonics and IMD for V2X_n40A-n47A are primarily analysed to study the interference.

=====================================Start of the TP ====================================

# 6	Con-current operation with one Uu band and one PC5 band

## 6.2	Con-current operation between one NR Uu band and one NR PC5 band

### 6.2.2	V2X_n40A-n47A

#### 6.2.2.1	Operating bands for V2X_n40A-n47A

The operating bands for V2X_n40A-n47A are specified in table 6.2.2.1-1.

Table 6.2.2.1-1: Inter-band con-current V2X operating bands for V2X_n40A-n47A

| V2X con-current configuration | NR OperatingBand | Interface | Uplink (UL) band | Downlink (DL) band | Duplex Mode |
| --- | --- | --- | --- | --- | --- |
|  |  |  | BS receive / UE transmit1 | BS transmit / UE receive |  |
|  |  |  | FUL_low – FUL_high | FDL_low – FDL_high |  |
| V2X_n40A-n47A | n40 | Uu | 2300 MHz | – | 2400 MHz | 2300 MHz | – | 2400 MHz | TDD |
|  | n47 | PC5 | 5855 MHz | – | 5925 MHz | 5855 MHz | – | 5925 MHz | HD |

#### 6.2.2.2	Channel bandwidths per operating band for V2X_n40A-n47A

The channel bandwidths per operating band for V2X_n40A-n47A are specified in table 6.2.2.2-1.

Table 6.2.2.2-1: V2X inter-band con-current configurations and bandwidth combination sets for V2X_n40A-n47A

| V2X inter-band Configuration | NR operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | Maximum aggregated bandwidth [MHz] | Bandwidth combination set |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| V2X_n40A-n47A | n40 | 15 | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  |  | 120 | 0 |
|  |  | 30 |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  |  |
|  |  | 60 |  | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  |  |
|  | n47 | 15 |  | Yes |  | Yes |  | Yes | Yes |  |  |  |  |  |
|  |  | 30 |  | Yes |  | Yes |  | Yes | Yes |  |  |  |  |  |
|  |  | 60 |  | Yes |  | Yes |  | Yes | Yes |  |  |  |  |  |

#### 6.2.2.3	Coexistence studies

The harmonics analysis for V2X_n40A-n47A is specified in table 6.2.2.3-1. Up to the 3rd harmonics of band n40 are provided since the frequency range of the 4th harmonics is higher than 5.9GHz. The harmonics of band n47 are not listed as the harmonics distributed in the frequency range much higher than 5.9GHz have no impact on GNSS and ISM bands. Based on the harmonics analysis, it is observed that the 3rd harmonics of band n40 have no impact on band n47.

Table 6.2.2.3-1: Harmonics analysis for V2X_n40A-n47A

| Operating Band | Band n40 | Band n47 |
| --- | --- | --- |
| UE UL carriers | fx_low | fx_high | fy_low | fy_high |
| UL frequency (MHz) | 2300 | 2400 | 5855 | 5925 |
| 2nd harmonics frequency limits | 2*fx_low | 2*fx_high | No effect |
| 2nd harmonics frequency limits (MHz) | 4600 | 4800 |  |
| 3rd harmonics frequency limits | 3*fx_low | 3*fx_high | No effect |
| 3rd harmonics frequency limits (MHz) | 6900 | 7200 |  |

The IMD analysis for V2X_n40A-n47A is specified in table 6.2.2.3-2. Up to the 5th order IMDs of band n40 and band n47 are provided. Based on the IMD analysis, it is observed that no IMD products fall into the associated bands. So there is no IMD issue caused by the band combinations of V2X_n40A-n47A.

Table 6.2.2.3-2: IMD analysis for V2X_n40A-n47A

| Operating Band | Band n40 | Band n47 |
| --- | --- | --- |
| UE UL carriers | fx_low | fx_high | fy_low | fy_high |
| UL frequency (MHz) | 2300 | 2400 | 5855 | 5925 |
| 2nd harmonics frequency limits | 2*fx_low | 2*fx_high | 2* fy_low | 2* fy_high |
| 2nd harmonics frequency limits (MHz) | 4600 | 4800 | 11710 | 11850 |
| 3rd harmonics frequency limits | 3*fx_low | 3*fx_high | 3* fy_low | 3* fy_high |
| 3rd harmonics frequency limits (MHz) | 6900 | 7200 | 17565 | 17775 |
| Two tone 2nd order IMD products | ¦fy_low – fx_high¦ | ¦fy_high – fx_low¦ | ¦fy_low + fx_low¦ | ¦fy_high + fx_high¦ |
| IMD frequency limits (MHz) | 3455 | 3625 | 8155 | 8325 |
| Two-tone 3rd order IMD products | ¦2*fx_low – fy_high¦ | ¦2*fx_high – fy_low¦ | ¦2*fy_low – fx_high¦ | ¦2*fy_high – fx_low¦ |
| IMD frequency limits (MHz) | 1325 | 1055 | 9310 | 9550 |
| Two-tone 3rd order IMD products | ¦2*fx_low + fy_low¦ | ¦2*fx_high + fy_high¦ | ¦2*fy_low + fx_low¦ | ¦2*fy_high + fx_high¦ |
| IMD frequency limits (MHz) | 10455 | 10725 | 14010 | 14250 |
| Two-tone 4th order IMD products | ¦3*fx_low – fy_high¦ | ¦3*fx_high – fy_low¦ | ¦3*fy_low – fx_high¦ | ¦3*fy_high – fx_low¦ |
| IMD frequency limits (MHz) | 975 | 1345 | 15165 | 15475 |
| Two-tone 4th order IMD products | ¦3*fx_low + fy_low¦ | ¦3*fx_high + fy_high¦ | ¦3*fy_low + fx_low¦ | ¦3*fy_high + fx_high¦ |
| IMD frequency limits (MHz) | 12755 | 13125 | 19865 | 20175 |
| Two-tone 4th order IMD products | ¦2*fx_low – 2*fy_high¦ | ¦2*fx_high – 2*fy_low¦ | ¦2*fx_low + 2*fy_low¦ | ¦2*fx_high + 2*fy_high¦ |
| IMD frequency limits (MHz) | 7250 | 6910 | 16310 | 16650 |
| Two-tone 5th order IMD products | ¦fx_low – 4*fy_high¦ | ¦fx_high – 4*fy_low¦ | ¦fy_low – 4*fx_high¦ | ¦fy_high – 4*fx_low¦ |
| IMD frequency limits (MHz) | 21400 | 21020 | 3745 | 3275 |
| Two-tone 5th order IMD products | ¦fx_low + 4*fy_low¦ | ¦fx_high + 4*fy_high¦ | ¦fy_low + 4*fx_low¦ | ¦fy_high + 4*fx_high¦ |
| IMD frequency limits (MHz) | 25720 | 26100 | 15055 | 15525 |
| Two-tone 5th order IMD products | ¦2*fx_low – 3*fy_high¦ | ¦2*fx_high – 3*fy_low¦ | ¦2*fy_low – 3*fx_high¦ | ¦2*fy_high – 3*fx_low¦ |
| IMD frequency limits (MHz) | 13175 | 12765 | 4810 | 4950 |
| Two-tone 5th order IMD products | ¦2*fx_low + 3*fy_low¦ | ¦2*fx_high + 3*fy_high¦ | ¦2*fy_low + 3*fx_low¦ | ¦2*fy_high + 3*fx_high¦ |
| IMD frequency limits (MHz) | 22165 | 22575 | 18610 | 19050 |

The harmonics and intermodulation products should be evaluated when V2X inter-band con-current operating UE coexists with other systems such as GNSS and ISM. The harmonics and IMD analysis of V2X_n40A-n47A for GNSS and ISM bands is shown in table 6.2.2.3-3. Based on the analysis for GNSS and ISM bands, band n47 have an impact on the ISM band (5GHz).

Table 6.2.2.3-3: Harmonic and IMDs analysis of V2X_n40A-n47A UE for GNSS and ISM bands

| Victim Systems | Frequency range [MHz] | Impact | Regions | Comments |
| --- | --- | --- | --- | --- |
| COMPASS (Beidou) | 1559 | - | 1591 | No |  |  |
| Galileo | 1559 | - | 1591 | No |  |  |
| GLONASS | 1591 | - | 1610 | No |  |  |
| GPS | 1563 | - | 1587 | No |  |  |
| ISM band (2.4GHz) | 2400 | - | 2483.5 | No | US/Europe |  |
|  | 2400 | - | 2494 | No | Asia |  |
| ISM band (5GHz) | 5150 | - | 5925 | Yes | US | Band n47 |
|  | 5150 | - | 5350 | No | Europe |  |
|  | 5470 | - | 5725 | No |  |  |
|  | 5150 | - | 5825 | No | Asia |  |

=====================================End of the TP =====================================