## Slide 1: WF on FR2 FWA RF requirements
SoftBank Corp.
3GPP TSG-RAN WG4 #97-e
2 – 13 November 2020
Electronic meeting
R4-2016874

## Slide 2: Background
Capture the open issues as follows:
  Minimum peak EIRP
  MBR
  MPR
  Beam Correspondence
  REFSENS

## Slide 3: Min. peak EIRP
Agreement in GTW session:
  30.0 dBm for n257, 30.4 dBm for n258
    Intel and MediaTek would like to check and feed back within a day

## Slide 4: MBR
Agreement in GTW session:
  Option 1: 0.7dB

## Slide 5: MPR
Agreement in GTW session:
  Option 2: MPR requirements reuse PC3 values

## Slide 6: Beam Correspondence
Agreement in GTW session:
  Option 3, with the clarification that how the UE BC performance can be ensured.
    Option 3: Follow PC1 approach, i.e. no requirement defined in RAN4. No plan to specify in the future.
      “No requirement defined in RAN4” means there is no assurance for the network that the UE has any beam correspondence ability before network assistance with UL beam sweeping.
FFS
Notes: Qualcomm: It appears that there are strong and immediate concerns shared by many companies regarding agreement made in the online session for beam correspondence (GTW) . We echo multiple companies’ views that option 2 is appropriate (no bit 0 UE will be defined), but this view is also not agreeable. We have therefore replaced with FFS.

## Slide 7: REFSENS
Agreements in GTW session:
  -92.6dBm (n257)
  -92.8dBm (n258)
  Note: the values are under the condition of CBW=50MHz.