3GPP TSG-RAN4 Meeting #97-e	                                                                         R4-2017230

Electronic meeting, Nov. 2-13, 2020

Title:	Updated link-level simulation assumption for CSI-RS based L3 measurement

Source:	CATT

Agenda Item:	7.14.2.1

Document for:	Approval

# Introduction

In RAN4#92 meeting, the simulation assumption for CSI-RS based L3 measurement was agreed in [1]. Based on [1] and the latest conclusions in RAN4 #96e meeting [2], updated simulation assumptions are provided in this contribution including the change of CSI-RS bandwidth, density and timing difference.

Interested companies can provide simulation results based on the updated simulation assumption. For the companies that have provided simulation results in previous meeting based on assumption in [1], the simulation results can still be used if the used parameters are included in this updated simulation assumption.

# Simulation Assumptions

Table 1: General parameters

| Simulation parameters | Comments/values |
| --- | --- |
| Carrier frequency for Cell 1 and Cell 2 | 4 GHz | 30 GHz |
| Prior knowledge of Cell 1 / Cell 2 by the UE | Yes / Yes | Yes / Yes |
| DRX | No | No |
| BS transmit antennas for SS blocks | 1 tx or single layer transmissions | 1 tx or single layer transmissions |
| UE receive antennas | Case A: 2 rx (uncorrelated with equal gain, no rx beamforming); Case B: 2 rx with rx beamforming Note1 | Case A: 2 rx (uncorrelated with equal gain, no rx beamforming); Case B: 2 rx with rx beamforming Note1 |
| Measurement period (in number of samlpes) | 1, 3, 5, 10; other number of samples may also be studied upon a need | 1, 3, 5, 10; other numbers of samples may also be studied upon a need |
| NOTE1: For Case B, companies are encouraged to state their assumptions on beamforming and rx antenna configuration together with the provided simulation results |

Table 2: Cell-specific parameters

| Parameter | Unit | Cell 1 | Cell 2 |
| --- | --- | --- | --- |
| E-UTRA RF Channel number | - | Channel 1 | Channel 1 |
| PBCH and DMRS power offset with respect to NR-PSS and NR-SSS | dB | 0 | 0 |
| Data and control PSD relative to NR-PSS and NR-SSS | dB | 0 | 0 |
| RB Utilization | % | 100 | 100 |
| Data Modulation | - | QPSK | QPSK |
| Slot length | - | 14 symbols | 14 symbols |
| CP Length | - | Normal | Normal |
| Frequency Offset relative to UE frequency reference | Hz | 0 | 0 |
| Relative Delay of 1st Path (synchronous) | µs | 0 | 0, CP, 2CP, 3us |
| SNR (in Case B, SNR includes beamforming gain) | dB | 6 dB | 1 dB |
| Es/IoT (calculated from SNRs) | dB | 2.46 dB | -5.97 dB |
| Propagation conditions | - | For 4 GHz: AWGN, EPA5, ETU30 (for 15 kHz SCS), ETU70 (for 15 kHz SCS); For 30 GHz:, optional TDL-A/ /C Note (delay spread: 30 ns; UE speed: 3 km/h and 30 km/h) |
| NOTE: the companies are encouraged to state channel model parameters together with the results, the parameters are to be further discussed and aligned |

Table 3: CSI-RS configuration parameters

| Parameter | 4 GHz | 30 GHz |
| --- | --- | --- |
| CSI-RS bandwidth | 48 PRBs; | 48 PRBs; |
| CSI-RS SCS | 15 kHz, 30 kHz, 60 kHz | 60 kHz; 120 kHz |
| Periodicity | 5 ms (optional); 40 ms | 5 ms (optional); 40 ms |
| CSI-RS configuration: <X,D,N,(Y,Z),CDM>, where: X=number of CSI-RS ports, D=density [RE/RB/port], N=number of OFDM symbols in the same slot, Y=adjacent in frequency REs in PRB, Z=adjacent in time REs in PRB | <1,3,1,N/A,noCDM> | <1,3,1,N/A,noCDM> |

# On CSI-RS Bandwidth

The CSI-RS bandwidth is configurable and can be one of: {24, 48, 96, 192, 264} PRBs in CSI-RS numerology. The bandwidth is, clearly, also limited by the channel bandwidth and depends on the CSI-RS numerology. The following channel bandwidths have been agreed for FR1 and FR2:

# Table 5.3.2-1: Maximum transmission bandwidth configuration NRB for FR1 [TS 38.104]

| SCS [kHz] | 5 MHz | 10 MHz | 15 MHz | 30 MHz | 20 MHz | 25 MHz | 40 MHz | 50 MHz | 60 MHz | 70 MHz | 80 MHz | 90 MHz | 100 MHz |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB | NRB |
| 15 | 25 | 52 | 79 | [160] | 106 | 133 | 216 | 270 | N.A | N.A | N.A | N.A | N.A |
| 30 | 11 | 24 | 38 | [78] | 51 | 65 | 106 | 133 | 162 | [189] | 217 | [245] | 273 |
| 60 | N.A | 11 | 18 | [38] | 24 | 31 | 51 | 65 | 79 | [93] | 107 | [121] | 135 |

# Table 5.3.2-2: Maximum transmission bandwidth configuration NRB for FR2 [TS 38.104]

| SCS [kHz] | 50MHz | 100MHz | 200MHz | 400 MHz |
| --- | --- | --- | --- | --- |
|  | NRB | NRB | NRB | NRB |
| 60 | 66 | 132 | 264 | N.A |
| 120 | 32 | 66 | 132 | 264 |

The minimum configurable number of PRBs is 24 for any SCS. The maximum configurable number of PRBs depends on SCS and the channel bandwidth:

- In FR1:

  - For 15 kHz: 264 PRBs

  - For 30 kHz: 264 PRBs

  - For 60 kHz: 96 PRBs

- In FR2:

  - For 60 kHz: 264 PRBs

  - For 120 kHz: 264 PRBs

# Performance Metrics

The simulations are to be provided for CSI-RSRP, CSI-RSRQ, and CSI-SINR.

For different estimation time periods, the CDF curves and 5th, 50th, 90th, and 95th %-iles are to be provided for (without RF impairment margin):

- Delta measurement   = (estimated measurement – ideal measurement) 	[dB],

where the ideal measurement is based on the perfect channel estimation.

# Reference

[1] R4-1910949,	“Link-level simulation assumptions for CSI-RS based measurements”,		CATT

[2] RAN4_96e_RRM_chairman_report_12_EOM