## Slide 1: Way forward on PDSCH CA normal demodulation requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #97-e
E-meeting, 2 – 13 November 2020
Agenda Item: 7.16.1.1
R4-2017561

## Slide 2: Test applicability rule
      Test of different CA capabilities
  Intra-band CA: test intra-band contiguous CA, and intra-band non-contiguous CA
  Inter-band CA: One or two inter-band configurations will be tested, which will be selected during CA configuration(s) and CBW combination selection procedure.
      Test coverage for different number of component carriers
  Include this section in the TS 38.101-4
  Further discuss the content of this section
      Antenna connection for CA tests with 4 RX
  Option 1:
    If any of the PCell and/or the SCells is a 4 RX supported RF band, all 4 RX should be connected with data source from system simulator.
    If any of the PCell and/or the SCells is a 2 RX supported RF band, 2 out of the 4 RX should be connected with data source from system simulator, and the other 2 RX are connected with zero input.
  Other options are not precluded

## Slide 3: Test applicability rule
      Selection of CA configuration(s) and CBW combination for FR1
  Step 1: Select the CA configuration(s) satisfying the following conditions:
    For each CC, the supported maximum number of MIMO layers is not lower than 2.
    [For each band/CBW combinations, the supported max data rate (calculated according to 4.1.2 of TS 38.306) is not lower than the date rate corresponding to using 2-layer and MCS 13 on the largest (aggregated) channel bandwidth on the band.]
  Step 2: Select any one of the CA configuration(s) with the largest aggregated CA bandwidth among the selected the CA configuration(s) based on step 1.
  [Step 3 (only for inter-band): If selected CA configuration in Step 2 corresponds to inter-band scenario with the largest number of bands then stop selection procedure and use only this CA configuration for testing. Otherwise, go to Step 4 to select the second CA configuration for testing.]
  [Step 4 (only for inter-band): Select CA configuration(s) corresponds to inter-band scenario with the largest number of bands and repeat Steps 1 and 2]

## Slide 4: Test applicability rule
      Selection of CA configuration(s) and CBW combination for FR2
  Step 1: Select CA configuration(s), which contain [all] CBW combination(s) with SNRTEmax higher or equal to SNRreq, among all supported CA configurations.
  Step 2: Among the selected CA configuration(s) in step 0, select the CA configuration(s) satisfying the following conditions:
    For each CC, the supported maximum number of MIMO layers is not lower than 2
    [For each band /CBW combinations, the supported max data rate (calculated according to 4.1.2 of TS 38.306) is not lower than the date rate corresponding to using 2-layer and MCS 10 on the largest (aggregated) channel bandwidth on the band.]
  Step 3: Select any one of the CA configuration(s) with the largest aggregated CA bandwidth among the selected the CA configuration(s) based on step 1.
  [Step 4 (only for inter-band): If selected CA configuration in Step 3 corresponds to inter-band scenario with the largest number of bands then stop selection procedure and use only this CA configuration for testing. Otherwise, go to Step 5 to select the second CA configuration for testing.]
  [Step 5 (only for inter-band): Select CA configuration(s) corresponds to inter-band scenario with the largest number of bands and repeat Steps 1, 2 and 3.]