## Slide 1: WF on Beam Correspondence
Apple Inc.
R4-2016820
3GPP TSG-RAN WG4 Meeting #97-e
Online Meeting, November 2020
Agenda: 7.12.1.1

## Slide 2
As summarized in [11], there are three open issues with Rel-16 beam correspondence under discussion:
  Issue 1-1: SSB’s PSD is backed-off by X dB compared to CSI-RS in CSI-RS based eBC requirements
  Issue 1-2: Additional applicability rules
  Issue 1-3: Testing aspects
A GTW session was organized by the RAN4 Chairman and collected several agreements on the open issues in [10]
  Issues 1-2 and 1-3 were discussed together, and Option 6 reflects this
Background
Notes: Ericsson: added text in blue

## Slide 3
Candidate options:
  Option 1: 3 dB
  Option 2: 6 dB
  Option 3: > 6 dB
  Option 4: 5 dB
Agreements:
  Option 4 is selected as a compromise
WF1: SSB’s PSD is backed-off by X dB compared to CSI-RS
Notes: Ericsson: added text in blue

## Slide 4
Agreement on core requirement applicability:
  For UEs which support both eBC based on SSB and eBC based on CSI-RS, the UE RF core requirements for both side conditions shall apply
Candidate options for test case applicability in case the UE declares it supports both SSB based eBC and CSI-RS based eBC:
  Option 2: Replace TBD with if a UE meets beam correspondence requirements based on SSB, it is considered to have met the beam correspondence requirements based on CSI-RS
  Option 4: “Replace TBD with if UE meet the CSI-RS based beam correspondence, it is considered to have met the beam correspondence requirements based on SSB.”
  Option 5: either option 2 or 4 is up to UE declaration.
  Option 6: All RF requirements in R16 specification are verified using the SSB side condition, and one representative test for the CSI-RS side condition is introduced (where the number of test points is up to RAN5)
Agreement on test case applicability:
  Option 6
WF2: Additional applicability rules
Notes: Ericsson: added text in blue

## Slide 5
Candidate options:
  Option 1: Verify N EIRP points with EIRP ≥ 50%-tile minimum spherical coverage requirement using the CSI-RS side condition; N is up to RAN5
  Option 2: Verify peak EIRP using the CSI-RS side condition, where the link direction is determined in the SSB based test
  Option 3: Leave all parameters for the test up to RAN5
  Option 4: RAN4 to discuss the above options and decide by the next meeting
Agreement on the representative test:
  Option 2
WF3: Representative test for the CSI-RS side condition
Notes: Ericsson: added text in blue

## Slide 6
References
[1] | R4-2014320 | LG Electronics | Enhanced beam correspondence test applicability rules in rel-16
[2] | R4-2014512 | Nokia, Nokia Shanghai Bell | REL16 eBC capability alingment with 38.306
[3] | R4-2014584 | Intel Corporation | On CSI-RS based beam correspondence
[4] | R4-2014722 | Samsung | Discussion on Rel-16 beam correspondence remaining issues
[5] | R4-2014923 | Apple Inc. | Remaining issues with beam correspondence enhancements
[6] | R4-2014924 | Apple Inc. | CR to TR 38.831 on beam correspondence corrections
[7] | R4-2015344 | OPPO | Discussion on Rel-16 BC
[8] | R4-2015808 | Sony, Ericsson | Remaining issues in beam correspondence
[9] | R4-2016518 | Huawei, HiSilicon | CR on beam correspondence side condition
[10] | RAN4#97e GTW [97e][113] NR_RF_FR2_req_enh_Part_4 v2 - GTW.pptx | RAN4 Chairman | RAN4#97e GTW session; [97e][113] NR_RF_FR2_req_enh_Part_4
[11] | R4-2016615 | Moderator (Nokia) | Draft Email discussion summary for [97e][113] NR_RF_FR2_req_enh_Part_4
Notes: Ericsson: added text in blue