## Slide 1: WF on DC_20_n38 RF architecture
LG Electronics, [Huawei]...
3GPP TSG-RAN WG4#97-e Meeting R4-2016840
Electronic Meeting, 2nd – 13th November, 2020

## Slide 2: Background [1]
In previous meeting, RAN4 discussed several parameters to decide MSD and additional ILs for NR V2X UE_20A_n38A.
At last RAN4 meeting, RAN4 agreed to consider harmonic trap filter (HTF) to reduce MSD level due to 3rd harmonic product by Band 20 transmission.
RAN4 recognized that it is quite beneficial to consider the same RF architecture between DC_20_n38 and V2X_20_n38.
However, RAN4 did not consider HTF in DC_20_n38 UE since 0.3dB IL was specified in TS38.101-3 which level was derived only diplexer.
  RAN4 generally decide the additional ILs compare to single carrier supporting UE. For DC UE, the delta term is derived by Diplexer filter performance using shared pain approach.
  Even though DC_20_n38 UE did not consider HTF, the required MSD levels by 3rd harmonic problems is specified as low MSD values compared in [2]

## Slide 3: Issues for DC_20_n38
Based on these background, RAN4 need to decide for MSD level and additional ILs according to RF architecture.
  Issue #1: RF architecture between DC_20_n38 and V2X_20_n38
    Option 1: Consider same RF architecture without HTF
    Option 2: Consider same RF architecture with HTF
    Option 3: Consider different RF architecture
  Issue #2: MSD level for DC_20_n38
    Option 1: keep the current MSD (10.3dB) level for DC_20_n38
    Option 2: change MSD by average manner (10.7dB).
  Issue #3: Additional ILs for DC_20_38
    Option 1: keep the current additional IL level (0.3dB/0 dB) for DC_20_n38.
    Option 2: add 0.2dB by HTF for additional IL level (0.5dB/0.2dB) for DC_20_n38.

## Slide 4: Issue #1: RF architecture for DC_20_n38
3rd harmonic from Band 20 will be impact in n38 reception.
  The impact by 3rd harmonic in Rx sensitivity level can be reduced using HTF.
Candidate options for DC_20_n38 and V2X_20_n38
    Option 1: Consider same RF architecture without HTF
    Option 2: Consider same RF architecture with HTF
    Option 3: Consider different RF architecture
Proposal for WF
  Option 2 is chosen, the RF architecture only consider to derive MSD and additional ILs.

## Slide 5: Issue #2: MSD level for DC_20_n38
RAN4 need to decide whether or not define same MSD level between DC_20_n38 and V2X_20_n38.
Candidate options
    Option 1: Keep the current MSD (10.3dB @ CBW=10MHz) level for DC_20_n38
    Option 2: Change MSD by average manner (10.7dB @ CBW=10MHz).
Proposal for WF
  Option 1 is chosen, RAN4 only consider the architecture to decide additional ILs and MSD level. It should be implemented to achieve this performance.

## Slide 6: Issue #3: Additional ILs for DC_20_n38
RAN4 need to decide whether or not change the current additional ILs for DC_20_n38.
Candidate options
    Option 1: Keep the current additional IL level (0.3dB/0 dB) for DC_20_n38.
    Option 2: Add 0.2dB by HTF for additional IL level (0.5dB/0.2dB) for DC_20_n38.
Proposal for WF
  Option 2 is chosen, RAN4 only consider the architecture to decide additional ILs and MSD level. It should be implemented to achieve this performance.

## Slide 7: WF : MSD for DC_20_n38
MSD for DC_20_n38 in TS38.101-3
  Keep the current MSD levels for DC_20_n38
Table 7.3B.2.3.1-1: Reference sensitivity exceptions (MSD) due to UL harmonic for EN-DC in NR FR1
E-UTRA or NR Band / Channel bandwidth of the affected DL band / MSD |  |  |  |  |  |  |  |  |  |  |  |  | 
UL band | DL band | 5 MHz (dB) | 10 MHz (dB) | 15 MHz (dB) | 20 MHz (dB) | 25 MHz (dB) | 30 MHz (dB) | 40 MHz (dB) | 50 MHz (dB) | 60 MHz (dB) | 80 MHz (dB) | 90 MHz (dB) | 100 MHz (dB)
1, 3 | n772,13 |  | 23.9 | 22.1 | 20.9 |  |  | 17.9 | 16.8 | 16.0 | 14.8 | 14.3 | 13.8
 | n773 |  | 1.1 | 0.8 | 0.3 |  |  |  |  |  |  |  | 
2 | n482,13 | 27.3 | 24.4 | 22.4 | 21.2 |  |  | 18 | 17.1 | 16.3 | 15 | 14.5 | 14
 | n483 | 1.9 | 1.4 | 0.9 | 0.4 |  |  | 0 | 0 | 0 | 0 | 0 | 0
… | … | … | … | … | … |  |  | … | … | … |  |  | 
20 | n388,9 | 12.9 | 10.3 | 8.4 | 7.4 |  |  |  |  |  |  |  | 

## Slide 8: WF : Additional ILs for DC_20_n38
Inter-band EN-DC configuration | E-UTRA or NR Band | ΔTIB,c (dB)
DC_20_n38 | 20 | 0.53
 | n38 | 0.3
… | … | …
DC_1-20_n38 | 1 | 0.5
 | 20 | 0.53
 | n38 | 0.5
… | … | …
DC_3-20_n38 | 3 | 0.5
 | 20 | 0.53
 | n38 | 0.5
… | … | …
DC_3-20-38_n78 DC_3-20_n38-n78 | 3 | 0.6
 | 20 | 0.6
 | 38 or n38 | 0.5
 | n78 | 0.8
… | … | …
DC_1-3-20_n38 | 1 | 0.5
 | 3 | 0.5
 | 20 | 0.53
 | n38 | 0.5
Table 6.2B.4.2.3.1-1: ΔTIB,c due to EN-DC(two bands)
Additional ILs for DC_20_n38 in TS38.101-3
Inter-band EN-DC configuration | E-UTRA or NR Band | ΔRIB,c (dB)
… | … | …
DC_20_n38 | 20 | 0.2
 | n38 | 0.0
… | … | …
DC_1-20_n38 | 20 | 0.2
… | … | …
DC_3-20_n38 | 20 | 0.2
… | … | …
DC_3-20-38_n78 DC_3-20_n38-n78 | 3 | 0.2
 | 20 | 0.2
 | 38 or n38 | 0.4
 | n78 | 0.5
… | … | …
DC_1-3-20-38_n78 DC_1-3-20_n38-n78 | 3 | 0.2
 | 20 | 0.2
 | 38 or n38 | 0.4
 | n78 | 0.5
Table 7.3B.3.3.1-1: ΔRIB,c due to EN-DC(two bands)

## Slide 9: References
# of Tdoc | TDoc | Title | Source | Type
1 | R4-2014317 | Consideration on additional ILs and MSD levels for DC_20_n38 UE and/or V2X_20_n38 UE based on RF architecture | LG Electronics Inc. | Approval
2 | R4-2014318 | Correction on additional ILs and MSD levels for DC_20_n38 UE | LG Electronics, Huawei | CR
3 | R4-2016618 | Email discussion summary for [97e][116] NR_R16_Maintenance | Moderator (OPPO) | Information
4 | R4-2016611 | Email discussion summary for [97e][109] 5G_V2X_NRSL_UE_Concurrent | Moderator (Huawei) | Information
5 | R4-2014322 | MSD Analysis results and harmonic reduction filter for V2X_20A_n38A | LG Electronics France | Approval
6 | R4-2014324 | Correction on NR V2X inter-band con-current UE RF requirements in TS38.101-3 | LG Electronics France | CR