## Slide 1: WF on BS and UE parameters for 6.425-7.125 and 10.0-10.5 GHz
Nokia, CATT, Ericsson, ZTE, Huawei, Qualcomm
3GPP TSG-RAN WG4 Meeting # 97-e
Electronic Meeting, 2 – 13 Novmeber 2020
Agenda Item: 11.1
R4-2016905

## Slide 2: Background
Contributions on BS and UE parameters for the SI on 6.425-7.125GHz and 10.0-10.5GHz in RAN4#97-e have a variety of proposals:
[1] R4-2014457 BS parameters for the frequency range 6.425-7.125GHz, 7.025-7.125GHz and 10.0-10.5GHz CATT
[2] R4-2014474 Proposals of BS Parameters for Frequency Ranges 6.425-7.125GHz and 10.0-10.5GHz Nokia, Nokia Shanghai Bell
[3] R4-2014738 Discussion on remaining issues for 6425-7125 BS parameter CMCC
[4] R4-2014749 Discussion on remaining issues for 6425-7125 BS parameter CMCC
[5] R4-2015677 TP on BS remaining parameters Huawei, HiSilicon
[6] R4-2015899 SI on IMT parameters - Remaining BS parameters Ericsson
[7] R4-2016133 TP to TR38.921 : BS spurious emission ZTE Corporation
[8] R4-2016369 Draft LS to ECC SE21 on Spurious emission limits for AAS BS in 6.425 – 7.125 GHz and 10-10.5 GHz Ericsson
[9] R4-2014456 UE parameters for the frequency range 6.425-7.125GHz, 7.025-7.125GHz and 10.0-10.5GHz CATT
[10] R4-2014473 Proposals of UE Parameters for Frequency Ranges 6.425-7.125GHz and 10.0-10.5GHz Nokia, Nokia Shanghai Bell
[11] R4-2015676 TP on UE IMT technology related parameters Huawei, HiSilicon
[12] R4-2015900 SI on IMT parameters - Remaining UE parameters Ericsson
The Way Forward from the discussion of the contributions are summarized in the following slides.

## Slide 3: Way forward on BS and UE - ACLR and ACS
Agreements:
  Between 6.425-7.125 GHz (31.0dB DL ACIR and 25.9dB UL ACIR)
  Between 10-10.5 GHz (30.0dB DL ACIR and 23.9dB UL ACIR)
  Note: The values apply to the Rural/Macro suburban/Macro urban/Small cell outdoor/Micro urban scenarios, whether they apply to the Small cell indoor/Indoor urban scenario is FFS.
(dB) | ACLR | ACS
BS | 38 | 42
UE | 26 | 32
(dB) | ACLR | ACS
BS | 37 | 40
UE | 24 | 31

## Slide 4: Way forward on BS Spectral mask
Agreements:
  Basic limits for bands above 1 GHz in clauses 6.6.4.2 and 9.7.4.2 of TS 38.104 with Frequency offset step size of [5..50] MHz for 6.425-7.125 GHz and 10.0-10.5 GHz

## Slide 5: Way forward on BS (general) in-band blocking
Agreements:
  Lower interfering signal mean power compared to those in clauses 7.4.2.2 and 10.5.2.2 of TS 38.104: [TBD]dB for 6.425-7.125 GHz and [TBD]dB for 10.0-10.5 GHz

## Slide 6: Way forward on BS out of band blocking
Agreements:
  [-15] dBm CW interferer applies from 1MHz to FUL,low – [60..200]MHz and from FUL,high + [60..200]MHz up to 26000 MHz

## Slide 7: Way forward on BS spurious between 6.425-7.125 GHz
Agreements:
  Conducted:
  OTA – basic limits:
Spurious frequency range | Basic limit | Measurement bandwidth
9 kHz – 150 kHz | -36 dBm | 1 kHz
150 kHz – 30 MHz | -36 dBm | 10 kHz
30 MHz – 1 GHz | -36 dBm | 100 kHz
1 GHz – 26 GHz | -30 dBm | 1 MHz
Spurious frequency range | Basic limit | Measurement bandwidth
30 MHz – 1 GHz | -36 dBm | 100 kHz
1 GHz – 26 GHz | -30 dBm | 1 MHz

## Slide 8: Way forward on BS spurious between 10-10.5 GHz
Agreements (conducted and OTA – basic limits):
Spurious frequency range | Basic limit | Measurement bandwidth
30 MHz – 1 GHz | -36 dBm | 100 kHz
1 GHz – 18 GHz | -30 dBm | 1 MHz
18 GHz – 26 GHz | -20 dBm | 10 MHz

## Slide 9: Way forward on BS ΔfOBUE
Agreements:
  [40-100] MHz for 6.425-7.125GHz and 10-10.5GHz
  Operating band characteristics should be considered

## Slide 10: Way forward on UE Spectral mask
Agreements:
  Out of band emission is FFS

## Slide 11: Way forward on UE blocking
Agreements:
  For 6.425-7.125 GHz and 10.0-10.5 GHz, same limits as defined for the frequency larger than 3300MHz in clause 7.6 in 38.101-1