## Slide 1: WF on RF requirements for PC2 TDD intra-band contiguous UL CA
Huawei, HiSilicon, LGE
R4-2016911
3GPP TSG-RAN WG4 #97-e
Nov 2nd – 13th, 2020
Electronic meeting

## Slide 2: RF architecture
3 options are discussed during RAN4 #97-e meeting:
  Option 1: PC2 UL CA with one 26dBm PA 200MHz 1LO
    UL MIMO can be supported on top of UL CA with an additional path
  Option 2: PC2 UL CA with two 26dBm PA 100MHz 2LO
    UL MIMO is not supported on top of UL CA
  Option 3: PC2 UL CA with two 23dBm PA 200MHz 1LO
    UL MIMO can be supported on top of UL CA
RAN4 further discuss on following issue:
  If more than 1 RF architectures are selected, whether 2 set of RF requirement are needed
    For 2PA architecture, the emission requirement is defined as the sum from both UE transmit antenna connectors.
  Whether MPR required for different architectures can be covered by one baseline option
RAN4 made decision on RF architecture based on above issue conclusion
  If only 1 set of RF requirement is defined, select one RF architecture as baseline
  If 2 set of RF requirements are defined, there is no baseline RF architecture
    Down select RF architecture among options if possible

## Slide 3: RF requirements for PC2 contiguous UL CA
Following agreements are reached:
  Define tolerance for power class 2 ：26dBm +2/-3dB, regardless of RF architecture
  ACLR requirement: 31dB
  Emission requirement: reuse SEM, general spurious, ASEM, ASE and UE-to-UE coexistence requirements defined for PC3
  UL/DL configuration: adopt the same UL/DL configuration between CCs
  Pcmax: Use the same power class fallback mechanism as for single carrier
  Capability of MaxUplinkDutyCycle: Reuse the capability for single carrier case