## Slide 1: MSD test point specification methodology for LTE CA REL-17
Skyworks, Nokia, Huawei, …
3GPP TSG-RAN WG4 Meeting #97-e R4-2016940
Electronic Meeting, 2-13 Nov., 2020

## Slide 2: Background: Current LTE-CA Way of Working (1/3)
The current Way of Working (WoW) for LTE-CA REFSENS MSD Test Points (TP) is that, contrary to NR/EN-DC, LTE-CA higher order combinations cannot be exempted from specifying MSD TP even if constituent lower order (eg. 2DL or 3DL CAs) MSD test points have been previously agreed.
This results in specifying multiple redundant MSD TP.
For example REL-16.7.0 Table 7.3.1A-0bC “Reference sensitivity for carrier aggregation QPSK PREFSENS, CA (exceptions for three bands due to close proximity of UL to DL channel)” contains 88 MSD TP, out of which 82 are TP for Band 3 MSD due to close proximity of Band 1.
Adopting NR WoW could not only reduce significantly the complexity of MSD tables, it may also result in significant conformance test time/cost reduction.

## Slide 3: Background: Adopting NR WoW for new REL-17 LTE-CA Combos (2/3)
To prevent further expansion of the LTE MSD CA tables in future Releases, it has been proposed to adopt the NR / EN-DC MSD TP specification methodology for new Release 17 LTE-CA combinations [1]:
    2DL/1UL MSD test points cover cases of REFSENS:
      Exceptions due to harmonic issue,
      Exceptions due to for two bands due to close proximity of UL to DL channel,
      Exceptions due to cross band isolation issues of TDD and FDD bands,
      CA with SDL band,
    2DL/2UL MSD test points cover cases of REFSENS:
      Exceptions for intermodulation interference due to dual uplink operation,
      Exceptions for intra-band CA,
    3DL/2UL MSD test points cover cases of REFSENS:
      Exceptions for intermodulation interference into third band due to dual uplink operation,
      No additional MSD test point is needed for higher-order combinations.
1St round comments indicate consensus could be reached as all companies which commented are in favour of this approach.

## Slide 4: Background: Handling of Legacy LTE-CA MSD TP (3/3)
In principle, the concept could be ported to legacy MSD tables [1] .
1st round comments indicate two different views on this aspect:
  5 companies are not in favour of applying the NR methodology to legacy MSD test points due to 1) huge work involved, 2) huge impact on RAN5, and 3) possible confusion across the industry for early LTE release devices.
  1 company is in favour of applying the concept to legacy combos, arguing that two separate sets of tables may result in more complicated technical specifications.
One company suggested that it would be preferable to prepare an LS to inform RAN5 about RAN4 change of methodology and that RAN5 may choose the suitable test method to simplify the test procedure.

## Slide 5: Proposed Way Forward for REL-17 Technical Specifications (1/2)
Proposal 1: For new REL-17 combinations,
  Adopt NR/EN-DC MSD test point specification methodology for new LTE CA combinations:
    2DL/1UL MSD test points cover cases of REFSENS:
      Exceptions due to harmonic issue,
      Exceptions due to for two bands due to close proximity of UL to DL channel,
      Exceptions due to cross band isolation issues of TDD and FDD bands,
      CA with SDL band,
    2DL/2UL MSD test points cover cases of REFSENS:
      Exceptions for intermodulation interference due to dual uplink operation,
      Exceptions for intra-band CA,
    3DL/2UL MSD test points cover cases of REFSENS:
      Exceptions for intermodulation interference into third band due to dual uplink operation,
      No additional MSD test point is needed for higher-order combinations.
Proposal 2: Skyworks to work in collaboration with Basket WI Rapporteurs and to bring bigCR at December 2020 plenary to ensure this methodology is implemented in first Release-17 TS 36.101.
Proposal 3: As a first step, priority is to streamline REL-17 specifications to prevent further un-necessary MSD table expansion. Therefore, for legacy combinations, do not change MSD TP tables.
Proposal 4: Once bigCR is effective, inform RAN5 via an LS about RAN4 change of methodology for new LTE-CA REL-17 combinations and suggest conformance test case reduction opportunity for legacy MSD TP.

## Slide 6: Proposed Way Forward for REL-17 LTE Basket Work Item (2/2)
Proposal 5: Rapporteurs to ensure simplifications resulting from new methodology are effective in the Basket WI process:
  Higher-order LTE CA Text Proposals can not be agreed if lower order fall back specifications are missing,
  Higher-order MSD test points are no longer needed if constituent lower-order fall-back MSD are agreed and specified. For example, it is expected that for most combinations with >3 bands, MSD test points are not needed, and considerable simplification is expected for >2 band combinations.
  Corresponding TRs must follow Proposal 1, i.e.:
    2DL/1UL MSD test points cover cases of REFSENS:
      Exceptions due to harmonic issue,
      Exceptions due to for two bands due to close proximity of UL to DL channel,
      Exceptions due to cross band isolation issues of TDD and FDD bands,
      CA with SDL band,
    2DL/2UL MSD test points cover cases of REFSENS:
      Exceptions for intermodulation interference due to dual uplink operation,
      Exceptions for intra-band CA,
    3DL/2UL MSD test points cover cases of REFSENS:
      Exceptions for intermodulation interference into third band due to dual uplink operation,
      No additional MSD test point is needed for higher-order combinations

## Slide 7: References
  [1] R4-2016007 LTE Rel'17 MSD table simplification, Skyworks, Nokia.