## Slide 1: WF on NR SCC UL power drop behavior in FR2
Ericsson
3GPP TSG-RAN WG4 Meeting #97-e
Electronic meeting, 17 – 28 August 2020
R4-2016994
Agenda item: 4.2.2
Document for: Approval

## Slide 2: Background
The 1st round of discussions on the present topic at RAN4#96-e concluded
  “There is a conflicting situation that the minimum requirement were derived based on the assumption of equal PSD as the worst case condition while the actual UE behavior is allowed to scale down the power of SCC during the maximum output power condition.”
According to the WF [1] agreed at RAN4#96-e
  - Companies are encouraged to bring views regarding conditions which should be suggested to RAN5 to measure each CA test case.
  Option 1: Equal PSD between CCs.
  Option 2: Measure the UE as is even SCC output may be scaled down under CA mode.
  Other options are not precluded.
  Study of the methodologies to reproduce the conditions above is RAN5 work.

## Slide 3: RAN4 understanding
The UE prioritizes power on the Pcell and reduces the power on the Scell(s) for transmissions of a given priority when the UE is power limited (38.213)
The RAN4 requirements on PCMAX for CA do not mandate the UE transmit with equal PSD across CCs at maximum output power
Equal PSD was assumed for the development of MPR requirements, but the MPR thus specified for the total CA power is applicable to all transmit conditions (priorities)

## Slide 4: Way forward
Changes to 38.101-2, if any, capturing the RAN4 understanding are FFS
Companies are encouraged to bring views regarding conditions which should be suggested to RAN5 to measure each CA test case (carried over from [1])
Then send LS to RAN5

## Slide 5: References
R4-2011695, ” WF on NR SCC UL power drop behavior in FR2”, Anritsu
R4-2014711, ”PCC SCC prioritization issue solution” Qualcomm Inc.
R4-2015334, ”Discussion on FR2 equal PSD in CA and draft LS”, OPPO
R4-2015335, “CR on FR2 equal PSD in UL CA”, OPPO
R4-2015336, “CR on FR2 equal PSD in UL CA”, OPPO
R4-2015978, “Modification of FR2 MOP verification with account of the 38.213 scaling rule”, Ericsson
R5-2015979, “Correction to Pcmax: account of power prioritization rules for secondary cells”, Ericsson