## Slide 1: WF on NR Mobility Enhancements RRM
Apple
3GPP TSG-RAN WG4 Meeting #97-e R4-2017093
Electronic Meeting, 2nd – 13th November 2020

## Slide 2: Background
Agreements in this way forward are based on email discussion in R4-2017277 Email discussion summary for [97e][207] NR_Mob_enh_RRM
Agreements in the last RAN4#96-e meeting can be found in:
  R4-2012209 Email discussion summary for [96e][209] NR_Mob_enh_RRM
  R4-2012270 WF on MR Mobility Enhancements

## Slide 3: Agreement for core requirement maintenance
Issue 1-1: demodulation performance degradation for async intra-frequency DAPS handover and async intra-band inter-frequency DAPS handover
Agreement: For asynchronous DAPS handover, if the receive time difference exceeds the cyclic prefix length of that SCS, interruptions may occur depending on UE implementation. The duration and frequency of occurrence of such interruptions is not specified.

## Slide 4: Agreement for core requirement maintenance (Cont.)
Issue 1-4: Tprocessing in conditional PSCell change
Agreement: RAN4 is to specify Tprocessing as follows: Tprocessing = 20 ms when source and target cells are in the same FR, and Tprocessing = 40 ms when source and target cells are in different FRs.

## Slide 5: Agreement for core requirement maintenance (Cont.)
Issue 1-3: further clarification on DL-to-UL and UL-to-DL switching time
  Option 1: clarify that 13us switching time is allowed between source cell and target cell:
    Note 2: For DAPS handover on a TDD band, a UE is not expected to transmit in the uplink to source or target cell earlier than NRX-TX after the end of the last received downlink symbol from source or target cell in the same TDD band where NRX-TX=25600Tc.
    Note 3: For DAPS handover on a TDD band, a UE is not expected to receive in the downlink from source or target cell earlier than NTX-RX after the end of the last transmitted uplink symbol toward source or target cell in the same TDD band where NTX-RX=25600Tc.
  Option 2: Retain the existing specification that DL-to-UL and UL-to-DL switching time applies within the same cell
    Note 2: For DAPS handover on a TDD band, a UE is not expected to transmit in the uplink earlier than NRX-TX after the end of the last received downlink symbol in the same cell where NRX-TX=25600Tc.
    Note 3: For DAPS handover on a TDD band, a UE is not expected to receive in the downlink earlier than NTX-RX after the end of the last transmitted uplink symbol in the same cell where NTX-RX=25600Tc.
  Option 3: clarify that 10us switching time is allowed between source cell and target cell
    Note 2: For DAPS handover on a TDD band, a UE is not expected to transmit in the uplink to source or target cell earlier than NRX-TX after the end of the last received downlink symbol from source or target cell in the same TDD band where NRX-TX=19712Tc.
    Note 3: For DAPS handover on a TDD band, a UE is not expected to receive in the downlink from source or target cell earlier than NTX-RX after the end of the last transmitted uplink symbol toward source or target cell in the same TDD band where NTX-RX=19712Tc.
  Other options

## Slide 6: Agreement for DAPS HO test applicability
RAN4 to further split test applicability for DAPS handover to cover intra-frequency, intra-band inter-frequency and inter-band inter-frequency respectively
  To verify intra-frequency DAPS handover requirements
    The UE capable of intra-frequency asynchronous DAPS handover on any band needs to be tested only in asynchronous scenario.
    The UE not capable of intra-frequency asynchronous DAPS handover on any band but capable of synchronous DAPS handover on some band needs to be tested only in synchronous scenario.
  To verify intra-band inter-frequency DAPS handover requirements
    The UE capable of intra-band inter-frequency asynchronous DAPS handover on any band needs to be tested only in asynchronous scenario.
    The UE not capable of intra-band inter-frequency asynchronous DAPS handover on any band but capable of intra-band inter-frequency synchronous DAPS handover on some band needs to be tested only in synchronous scenario.
  To verify inter-band inter-frequency DAPS handover requirements
    The UE capable of inter-band inter-frequency asynchronous DAPS handover on any band combination needs to be tested only in asynchronous scenario.
    The UE not capable of inter-band inter-frequency asynchronous DAPS handover on any band combination but capable of inter-band inter-frequency synchronous DAPS handover on some band combination needs to be tested only in synchronous scenario.