## Slide 1: WF on R16 RRM enhancement part 3 - Inter-frequency measurement without MG
CMCC
3GPP TSG-RAN4 Meeting #97-e R4-2017203
Electronic Meeting, 2 – 13 Nov., 2020

## Slide 2: Background
R4-2008995 WF on inter-frequency without MG was agreed in RAN4#95e meeting
R4-2005348 WF on inter-frequency without MG was agreed in RAN4#94e bis meeting
R4-2002250 WF on inter-frequency without MG was agreed in RAN4#94e meeting
R4-1915853 WF on inter-frequency without MG was agreed in RAN4#93meeting.

## Slide 3: Issue 3-1: Power imbalance condition for inter-frequency without MG
Option 1 (Huawei, QC): The power imbalance between serving frequency layer and inter-frequency layer on which UE performs without gap shall be within [6]dB
Option 2 (MTK, Intel): In the test case of inter-frequency measurement without MG, the power imbalance between serving frequency layer and inter-frequency layer on which UE performs without gap shall be within [6]dB.
Option 3 (Ericsson, Apple, ZTE): such power imbalance limitation in option 1 is not needed

## Slide 4: Issue 6-1: TC list for inter-frequency measurement requirement without MG
TC | Company
TC1: SA event triggered reporting tests for FR1 without gap when DRX is not used (A.6.6.2.X) | CMCC
TC2: SA event triggered reporting tests for FR1 when DRX is used (A.6.6.2.X) | Apple
TC3: SA event triggered reporting tests for FR2 without gap when DRX is not used (A.7.6.2.X) | Huawei
TC4: SA event triggered reporting tests for FR2 without gap when DRX is used (A.7.6.2.X) | Mediatek

## Slide 5: Issue 6-2-2: SSB time index detection in TCs
TC1 FDD is without SSB time index detection
TC2 FDD is with SSB time index detection
TDD tests are defined without SSB time index detection

## Slide 6: Issue 6-2-1: MG configuration in TCs
Do not configure gap in inter-frequency measurement without MG tests.

## Slide 7: Issue 6-2-3: DRX cycle setup in TCs
TC2 tests one DRX cycle only and TC4 tests one DRX cycle only.
The DRX cycle in TC2 and TC4 can be different.