## Slide 1: WF on URLLC UE performance requirements with higher BLER
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #97-e
E-meeting, 2 – 13 November 2020
Agenda Item: 7.8.1.2
R4-2017509

## Slide 2: FR1 High reliability (1)
      Background (Agreed parameters from #94e, #94e-Bis, #95e and #96e)
  SCS/CBW: ​
    FDD: 15 kHz/10 MHz​
    TDD: 30 kHz/40 MHz​
  TDD pattern: 7D1S2U, S=6D: 4G: 4U for 30 kHz SCS.​
  PDSCH configuration:
    Mapping type A, symbol length 12, starting symbol 2.​
    Aggregation level: 2 for FDD and TDD
    Max number of HARQ transmissions: 4​
    FDD: No scheduling in slots 0 and 1 (or 19) within 20ms.
    TDD: No scheduling in D slots i, where mod(i, 10) = 0, and S slots
  Antenna configuration: 2x2 and 2x4, ULA low​
  Propagation condition: TDLA30-10​
  Target BLER: 1%​ (BLER is calculated after all transmission​)
  BLER calculation method
    BLER = NpacketFail/NpacketTx, where NpacketFail is the number of packets with CRC fail after all transmissions (initial and retransmissions), NpacketTx is the total number of packets transmitted during the test.
  Target Confidence level: 99%​

## Slide 3: FR1 High reliability (2)
HARQ process number: 4 for FDD and TDD
The number of slots between PDSCH and corresponding HARQ-ACK information for FDD
  Option 1: 4
  Option 2: 3 for initial transmission and 2 for repetition
  Option 3: The number of slots between final repetition PDSCH and corresponding HARQ-ACK information for FDD: 2
  Option 4: The number of slots between initial transmission PDSCH and corresponding HARQ-ACK information for FDD: 3
MCS 19

## Slide 4: FR2 High reliability (1)
SCS/BW: 120 kHz / 100 MHz
TDD pattern: DDSU, S=11:3:0
PDSCH configuration
  Frequency domain resource allocation: Full bandwidth
  Mapping Type A, Start symbol 1, Length 13
  PDSCH aggregation factor: n2
  Scheduling: No scheduling in D slot i, where mod(i,160) = 0 and mod(i, 160) = 1, and S slots
MCS
  Option 1: MCS19 from Table 3
  Option 2: MCS16 from Table 3
  Option 3: MCS13 from Table 3
  Higher or equal to -4 dB for final 2 Rx requirement definition (average ideal SNR alignment result + IM)

## Slide 5: FR2 High reliability (2)
DM-RS configuration: Type 1, Single-symbol DM-RS, 1 additional DM-RS
PT-RS configuration: Frequency density 2, Time density 1, RE offset 2
Overhead for TBS determination: 6
HARQ process: 2
Maximum number of HARQ re-transmission: 4
Channel model: TDLA30-75
Antenna configuration: 2x2, ULA low
Test metric: 1% BLER

## Slide 6: FR2 PDSCH mapping Type B (1)
Background (Agreed parameters from #96e)
  SCS/CBW: 120 kHz/100 MHz
  TDD pattern: DDDSU with S = 10D:2G:2U
  PDSCH Configuration
    Scheduling: No PDSCH in slot 0 within 20 ms
    MCS: [MCS4] from table 1.
    Start symbol: 1
    Symbol length: 2
  Antenna configuration: 2x2, ULA low
  Test metrics: 70% throughput

## Slide 7: FR2 PDSCH mapping Type B (2)
Symbol length: 2os
DMRS configuration: Type 1, Single-symbol DM-RS, 0 additional DM-RS
PTRS configuration: Frequency density 2, Time density 1, RE offset 2
MCS: MCS4 from Table 1.
Maximum number of HARQ re-transmission: 1
Number of HARQ process: 4
Overhead for TBS determination: 0

## Slide 8: Pre-emption indication (1)
      Background (Agreed parameters from #94e, 94e-bis, 95e and 96e)
  No URLLC PI performance requirements
  Time frequency set: 14x1
  Number of symbols to be pre-empted: 2
  Starting symbol to be pre-empted: 3
  Pre-emption scheduling: Fixed scheduling
  Test applicability for eMBB UE PI requirements: optional with UE capability signalling
  Antenna Configuration: 2x2 and 2x4, ULA low
  The assumption of UE behaviours for buffer flushing and decoding
    If UE cannot decode the PDCSH correctly, UE feeds back NACK to gNB. Then UE flushes the buffer and waits for the next re-transmission for LLR combing to decode the PDSCH.
  URLLC interference modelling
    SNR: Same as for eMBB transmission
    Structure: Some random data

## Slide 9: Pre-emption indication (2)
      Background (Agreed parameters from #94e, 94e-bis, 95e and 96e)
  Use the following parameters for eMBB PDSCH configuration
Parameter |  | Value
Duplex mode |  | FDD, TDD
Active DL BWP index |  | 1
PDSCH configuration | Mapping type | Type A
 | k0 | 0
 | Starting symbol (S) | 2
 | Length (L) | 12
 | PDSCH aggregation factor | 1
 | PRB bundling type | Static
 | PRB bundling size | 2
 | Resource allocation type | Type 0
 | RBG size | Config2
 | VRB-to-PRB mapping type | Non-interleaved
 | VRB-to-PRB mapping interl bundle size | N/A
PDSCH DMRS configuration | DMRS Type | Type 1
 | Number of additional DMRS | 1
 | Maximum number of OFDM symbols for DL front loaded DMRS | 1
Number of HARQ Processes |  | FDD: 4, TDD: 8
Maximum HARQ transmission |  | 4
The number of slots between PDSCH and corresponding HARQ-ACK information and TDD pattern |  | FDD: 2 TDD: FR1.30-1
CBW/SCS |  | FDD: 10/15, TDD: 40/30
RB allocation |  | Full bandwidth
MIMO layer |  | Rank 1
Propagation condition |  | TDLA30-10

## Slide 10: Pre-emption indication (3)
      Pre-emption probability
  Option 1: 10% within 1 radio frame
  Option 2: 20% within 1 radio frame
      eMBB MCS
  Option 1: MCS13 in Table 1
  Option 2: MCS4 in Table 1
  Option 3: MCS 16 in Table 1
      Test metric
  Option 1: 70% of max T-put
  Other options are not precluded
      Select proper test parameters and test metric to discriminate UE behaviour and ensure proper UE processing i.e. the performance gap > 1dB
      Companies are encouraged to prepare comparison analysis of UE with and without HARQ buffer flushing of pre-empted bits to decide on options above

## Slide 11: Test applicability
      Background (Agreement from 95e and 96e meeting)
  Test applicability for Rel-15 URLLC UE feature:
    The corresponding test applicability rules for the following features needs to be specified:
      PDSCH repetition (pdsch-RepetitionMultiSlots)
      PDSCH mapping type B (pdsch-MappingTypeB)
      PDSCH processing capability 2 (pdsch-ProcessingType2)
      New 64QAM MCS table for PDSCH (dl-64QAM-MCS-TableAlt)
      CQI table with target BLER of 10^-5 (cqi-TableAlt)
  No additional features and capability needed for URLLC Demod and CSI requirements introduced for Rel-15 feature under Rel-16 URLLC WI.
Agreement for 96e meeting
  UE URLLC requirements for Rel-15 features are release independent from Rel-15

## Slide 12: Requirements for Rel-16 URLCC feature
Background (Agreement from 96e meeting)
  Requirements for Multi-TRP URLLC transmission schemes are covered by Rel-16 e-MIMO WI, no discussion in URLLC thread.
Requirements for Rel-16 URLCC features
  No requirements for DCI format 1_2
  Not define PDCCH performance requirements for covering multiple PDCCH monitoring occasions per slot