## Slide 1: WF on power saving demodulation
Agenda Item: 7.6.3
Document for: Approval
Source: CMCC, CATT
3GPP TSG-RAN WG4 #97e R4-2017677
Electronic Meeting, 2-13 Nov., 2020

## Slide 2: Background
Joint PDCCH-WUS and PDCCH test has been discussed in previous RAN4 meetings. The WF R4-2012645 was agreed in RAN4#96-e meeting
Way forward in RAN4#96-e
Test solutions
  Option 1/2 listed in Slides#3 will be used for power saving test.
  Make a decision in next RAN4 meeting.
Test complexity aspects
  DRX cycle
    Use short DRX cycle of 10ms to reduce test time.
    It should be noted that using 10ms is only for test purpose and has no relation to real deployment.
  Number of error samples
    TBD error samples will be used.
Note: Currently RAN5 uses 1000 error samples which is time consuming. Need feedback from TE vendors whether 100 error samples are feasible.

## Slide 3: GTW session agreement (06th Nov. 2020)
Issue 1-1-1: Which test metric do you prefer to be used for PDCCH-WUS/PDCCH test
  Option 1c with Pm-dsg_total=1%
  Issue 1-1-2: In case of Option 2 in Issue 1-1-1, do you think it’s confident to reduce the number of error samples from 1000 to 100?
  No further discussion on this topic.
  Whether to reduce error samples for PDCCH test can be triggered in RAN5 as a general discussion not specific to this WI.

## Slide 4: Way forward
Test parameters for PDCCH
  Reuse the test parameters for PDCCH in DRX-ON in 38.101-4
  For FR1
    For FDD: Test No. 3 in Table 5.3.2.1.1-1 and Test No. 3 in Table 5.3.3.1.1-1
    For TDD: Test No. 2 in Table 5.3.2.2.1-1 and Test No. 2 in Table 5.3.3.2.1-1
For FR2
    For TDD: Test No. 1-2 in Table 7.3.2.2.1-1
  Applicability rule
    Apply the applicability rule that UE already fulfilling PDCCH-WUS performance requirement can skip the corresponding Rel-15 test(s)
The number of search space for PDCCH-WUS
  1 search space for PDCCH-WUS

## Slide 5: Way forward
Simulation assumptions for PDCCH-WUS for FR1-FDD
Parameter | Value | 
 | PDCCH-WUS | PDCCH
Duplex mode | FDD | 
DCI format | 2_6 | 1_1
Bandwidth | 10MHz | 
SCS | 15kHz | 
Number of BS antennas | 1Tx | 
Number of UE antennas | 2Rx, 4Rx | 
DM-RS channel estimation | Realistic | 
Channel model | TDLA30-10 | 
DCI length (excluding 24bits CRS) + Aggregation level | Option1:12 bits , AL=8 Option2: 36 bits , AL=16 | 52 bits + AL=4
CORESET symbol | 2 | 
CORESET bandwidth | 48RB | 
Mapping type | Non-Interleaved | Non-Interleaved
REG bundle size | 6 | 

## Slide 6: Way forward
Simulation assumptions for PDCCH-WUS for FR1-TDD
Parameter | Value | 
 | PDCCH-WUS | PDCCH
Duplex mode | TDD | 
DCI format | 2_6 | 1_1
Bandwidth | 40MHz | 
SCS | 30kHz | 
Number of BS antennas | 1Tx | 
Number of UE antennas | 2Rx, 4Rx | 
DM-RS channel estimation | Realistic | 
Channel model | TDLC300-100 | 
DCI length (excluding 24bits CRS) + Aggregation level | Option1:12 bits + AL=8 Option2: 36 bits + AL=16 | 53 bits + AL=4
CORESET symbol | 1 | 
CORESET bandwidth | 102RB | 
Mapping type | Interleaved(size 3) | Interleaved(size 3)
REG bundle size | 2 | 

## Slide 7: Way forward
Simulation assumptions for PDCCH-WUS for FR2
Parameter | Value | 
 | PDCCH-WUS | PDCCH
Duplex mode | TDD | 
DCI format | 2_6 | 1_1
Bandwidth | 100MHz | 
SCS | 120kHz | 
Number of BS antennas | 1Tx | 
Number of UE antennas | 2Rx | 
DM-RS channel estimation | Realistic | 
Channel model | TDLA30-300 | 
DCI length (excluding 24bits CRS) + Aggregation level | Option1:12 bits + AL=8 Option2: 36 bits + AL=16 | 56 bits + AL=4
CORESET symbol | 1 | 
CORESET bandwidth | 60RB | 
Mapping type | Interleaved(size 2) | Interleaved(size 2)
REG bundle size | 6 | 

## Slide 8: Way forward
Select the test parameters of WUS in next meeting RAN4#98e
  Test parameters for WUS of DCI length and Aggregation level in FR1
  Test parameters for WUS of DCI length and Aggregation level in FR2
Companies provide the ideal and impairment results based on simulation assumption
Companies provide CRs

## Slide 9: References
[1] R4-2014215
[2] R4-2014411
[3] R4-2014412
[4] R4-2014454
[5] R4-2014529
[6] R4-2014540
[7] R4-2014727
[5] R4-2015127
[6] R4-2015595