3GPP TSG-RAN WG4 Meeting # 98-e                                                              R4-2100300

# Electronic Meeting, Jan. 25-Feb. 5, 2021

Source: 	MediaTek Inc.

Title: 	TP for TR 37.717-11-21: to update DC_18_n3-n41 with IMD3 MSD

Agenda item:	9.7.2

Document for:	Approval

# Introduction

In this paper, we found that there is also 2UL IMD3 issue for ENDC bands combination of DC_18_n3-n41. The contribution is to include IMD3 MSD level for victim band of DC_18A_n3A-n41A in TR 37.717-11-21.

# 2. Discussion

## Considerations of IMD3 and MSD for DC_18A_n3A-n41A

Due to frequency of operation, there is 2UL IMD3 issue for DC_18A_n3A-n41A.

- IMD3 of UL n3 and B18: victim frequency range 2590 MHz – 2755 MHz overlaps with n41 RX frequency range 2496 MHz – 2690 MHz.

As for deriving IMD3 MSD of DC_18A_n3A-n41A, the front-end isolation parameters and spur levels are shown in Table 1.

Here, the minimum RX CBW of 10MHz is considered for n41.

Table 1: n41 REFSENS relaxation due to IMD3 of DC_18A_n3A-n41A

| Parameter | Value | Unit |
| --- | --- | --- |
| Antenna isolation | 10 | dB |
| PCB isolation from TX to RX | 65 | dB |
| Primary RX front-end and path loss | 4.5 | dB |
| Diversity RX front-end and path loss | 4 | dB |
| Conductive rejection from n3 PA output to n41 LNA input | 47 | dB |
| SNR requirement for QPSK | -1 | dB |
| Spur level at primary path referred to antenna port | -77.7 | dBm/10MHz |
| Spur level at diversity path referred to antenna port | -77.7 | dBm/10MHz |
| REFSENS relaxation (RX CBW=10MHz) | 16.1 | dB |

When the n41 frequency range is restricted to 2535MHz to 2690MHz, the IMD3 of 2UL B18 and n41 has the frequency as follows

- IMD3 of UL n41 and B18: victim frequency range 875 MHz – 1060 MHz does not overlap with B18 RX frequency range 860 MHz – 875 MHz.

Observation 1: When n41 frequency range is restricted to 2535MHz to 2690MHz, IMD3 frequency range of 2UL B18 and n41 does not overlap with victim B18 RX frequency. IMD3 MSD for B18 can be omitted.

Proposal 1: For n41 RX CBW of 10MHz, the MSD requirement of DC_18A-n3A-n41A due to 2UL IMD3 is provided in Table 2.

Table 2: MSD for DC_18A-n3A-n41A

| DC bands | UL DC | IMD | UL Fc | UL BW (MHz) | UL | DL Fc | DL BW | MSD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (MHz) |  | RB # | (MHz) | (MHz) | (dB) |
| DC_18A_n3A-n41A | 18 | IMD3 | ¦2fn3-fB18 ¦ | 820 | 5 | 25 | 865 | 5 | N/A |
|  | n3 |  |  | 1725 | 5 | 25 | 1820 | 5 |  |
|  | n41 |  |  | 2630 | 10 | 50 | 2630 | 10 | 16.1 |

# 3. Conclusion

Observation 1: When n41 frequency range is restricted to 2535MHz to 2690MHz, IMD3 frequency range of 2UL B18 and n41 does not overlap with victim B18 RX frequency. IMD3 MSD for B18 can be omitted.

Proposal 1: For n41 RX CBW of 10MHz, MSD requirement of DC_18A-n3A-n41A due to 2UL IMD3 is provided in Table 2.

Table 2: MSD for DC_18A-n3A-n41A

| DC bands | UL DC | IMD | UL Fc | UL BW (MHz) | UL | DL Fc | DL BW | MSD |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  | (MHz) |  | RB # | (MHz) | (MHz) | (dB) |
| DC_18A_n3A-n41A | 18 | IMD3 | ¦2fn3-fB18 ¦ | 820 | 5 | 25 | 865 | 5 | N/A |
|  | n3 |  |  | 1725 | 5 | 25 | 1820 | 5 |  |
|  | n41 |  |  | 2630 | 10 | 50 | 2630 | 10 | 16.1 |

# 4. Text Proposal

<Start of Text Proposal>

## 6.x	DC_18_n3-n41

### 6.x.1	Operating bands for DC

Table 6.x.1-1: DC band combination of LTE 1DL/1UL + NR 2DL/1UL

| E-UTRA and NR DC Band | E-UTRA and NR Band | Uplink (UL) band | Downlink (DL) band | Duplex mode |
| --- | --- | --- | --- | --- |
|  |  | BS receive / UE transmit | BS transmit / UE receive |  |
|  |  | FUL_low – FUL_high | FDL_low – FDL_high |  |
| DC_18A_n3A-n41A | 18 | 815 MHz | – | 830 MHz | 860 MHz | – | 875 MHz | FDD |
|  | n3 | 1710 MHz | – | 1785 MHz | 1805 MHz | – | 1880 MHz | FDD |
|  | n41 | 2496 MHz | – | 2690 MHz | 2496 MHz | – | 2690 MHz | TDD |

### 6.x.2	Channel bandwidths per operating band for DC

Table 6.x.2-1: Supported bandwidths per DC band combination of LTE 1DL/1UL + NR 2DL/1UL

|  |  | DC operating / channel bandwidth [MHz] |
| --- | --- | --- |
| E-UTRA and NR DC Configuration | UL Configuration | E-UTRA and NR Band | SCS (kHz) | 5 | 10 | 15 | 20 | 25 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100 | Maximum aggregated bandwidth [MHz] |
| DC_18A_n3A-n41A | DC_18A_n3A DC_18A_n41A | 18 | 15 | Yes | Yes | Yes |  |  |  |  |  |  |  |  |  |  | 155 |
|  |  | n3 | 15 | Yes | Yes | Yes | Yes | Yes | Yes | Yes |  |  |  |  |  |  |  |
|  |  |  | 30 |  | Yes | Yes | Yes | Yes | Yes | Yes |  |  |  |  |  |  |  |
|  |  |  | 60 |  | Yes | Yes | Yes | Yes | Yes | Yes |  |  |  |  |  |  |  |
|  |  | n41 | 15 |  | Yes | Yes | Yes |  | Yes | Yes | Yes |  |  |  |  |  |  |
|  |  |  | 30 |  | Yes | Yes | Yes |  | Yes | Yes | Yes | Yes |  | Yes | Yes | Yes |  |
|  |  |  | 60 |  | Yes | Yes | Yes |  | Yes | Yes | Yes | Yes |  | Yes | Yes | Yes |  |

### 6.x.3	Co-existence studies

Based on the co-existence studies of DC_18A-n3A and DC_18A-n41, impact on own Rx of 3rd band is as follows.

- 2nd and 3rd order IMD generated by dual uplink of Band 18 + Band n3 may also fall into own Rx of band n41.

- 2nd order IMD generated by dual uplink of Band 18 + Band n41 may also fall into own Rx of band n3.

### 6.x.4	∆TIB and ∆RIB values

(TIB,c and (RIB,c values for DC_18A_n3A-n41A are shown in the following tables.

Table 6.x.4-1: ΔTIB,c

| Inter-band DC Configuration | E-UTRA and NR Band | ΔTIB,c [dB] |
| --- | --- | --- |
| DC_18_n3-n41 | 18 | 0.3 |
|  | n3 | 0.5 |
|  | n41 | 0.3 |

Table 6.x.4-2: ΔRIB,c

| Inter-band DC Configuration | E-UTRA and NR Band | ΔRIB,c [dB] |
| --- | --- | --- |
| DC_18_n3-n41 | 18 | 0 |
|  | n3 | 0 |
|  | n41 | 0 |

### 6.x.5	MSD

Table 6.x.5-1 shows the required MSD:

Table 6.x.5-1: MSD exception for Scell due to dual uplink operation for EN-DC_18A_n3A-n41A

| DC bands | UL DC | IMD | UL Fc (MHz) | UL BW (MHz) | UL RB # | DL Fc (MHz) | DL BW (MHz) | MSD (dB) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| DC_18A_n3A-n41A | 18 | IMD2 | ¦fB18 +fn3¦ | 820 | 5 | 25 | 865 | 5 | N/A |
|  | n3 |  |  | 1720 | 5 | 25 | 1815 | 5 |  |
|  | n41 |  |  | 2540 | 10 | 50 | 2540 | 10 | 29.4 |
|  | 18 | IMD2 | ¦fB18 -fn41¦ | 820 | 5 | 25 | 865 | 5 | N/A |
|  | n41 |  |  | 2670 | 10 | 50 | 2670 | 10 |  |
|  | n3 |  |  | 1755 | 5 | 25 | 1850 | 5 | 28.2 |
|  | 18 | IMD3 | ¦2fn3-fB18 ¦ | 820 | 5 | 25 | 865 | 5 | N/A |
|  | n3 |  |  | 1725 | 5 | 25 | 1820 | 5 |  |
|  | n41 |  |  | 2630 | 10 | 50 | 2630 | 10 | 16.1 |

<End of Text Proposal>