## Slide 1
WF on new FR2 bandwidth classes
3GPP TSG-RAN WG4 Meeting # 96-e R4-2103009
Electronic Meeting, 25th January – 5th February, 2021
Agenda Item: 11.3.1
Verizon

## Slide 2: Background New FR2 bandwidth classes
During 1st round of discussion in [138], following proposal was discussed based on [1].
  Issue 1-1-1: New FR2 bandwidth classes
  Proposals
    Option 1: Add 4 new CA BW classes to FBG2 and 8 new CE BW classes to FBG3
    Option 2: Do not add new CA BW classes
    Option 3: Add new CA BW classes but differently as in option 1.
Majority supported option 1 (5 companies) and one companies supported 4 new classes
  A common observation is that the naming convention for the new CA BW classes may need to be reconsidered
A WF is recommended for further discussion

## Slide 3: WF on New FR2 bandwidth classes
Consider a new objective in the scope of Rel-17 FR2 WID
  Support up to 1600MHz downlink aggregated CA BW
  Introduce new CA BW classes in both FBG2 and FBG3 in Table 5.3A.4-1 in 38.101-2
    Allow both new design and backward compatibility
Option 1 shall be defined for FR2 bandwidth classes to FBG2 and FBG3
  For flexibility of both evolving new design and reflecting backward compatibility
Incorporate a the new classes in the Rel-17 FR2 WID
  For FR2 enhancement

## Slide 4: Reference
R4-2100264, Release 17 FR2 bandwidth class, Verizon
R4-2102986, Email discussion summary for [98e][138] [98e][138] FR_RF_FR2_req_enh2_Part_1, (Nokia)