## Slide 1: WF on further RRM enhancement for NR and MR-DC - SRS antenna port switching
Apple, …
R4-2103672
3GPP TSG-RAN4 Meeting #98-e
Online, 25 Jan. – 5 Feb., 2021
Agenda item: 11.4
Document for: Approval
Agreement in 1st round
Agreement in GTW (Jan. 29th)
Agreement in 2nd round

## Slide 2: Sub-topic 1-1: Scope of SRS antenna switching requirement (1/2)
Issue 1-1-1: whether interruption requirement would be defined in RRM for SRS antenna port switching
  Agreement: RAN4 to define interruption requirements for SRS antenna port switching
Issue 1-1-2: whether delay requirement would be defined in RRM for SRS antenna port switching
  Agreements
    RRM delay requirement for SRS antenna port switching is FFS
      Option 1: Do not define SRS antenna port switching delay requirement in RRM.
      Option 2: Define SRS antenna port switching delay requirement same as RF retuning time.
      Option 3: Define SRS antenna port switching delay requirement. FFS for the value. At least RF retuning time shall be included.
Issue 1-1-3: Impact of SRS antenna port switching to other RRM requirements
  Agreements
    Further identify impact of SRS antenna port switching on RRM requirements, e.g.
      Timing measurements and corresponding measurement requirements
      Other RRM requirements

## Slide 3: Sub-topic 1-1: Scope of SRS antenna switching requirement (2/2)
Issue 1-1-4: RAN4 defines the requirement only for SRS antenna port switching in FR1 or in both FR1 and FR2
  Agreements
    Define the RRM requirements for SRS antenna port switching for FR1.
    FFS for FR2 SRS antenna port switching requirements:
      Further identify the applicability of the existing RF transient period for SRS antenna port switching.

## Slide 4: Sub-topic 1-2: Interruption requirement applicability
Issue 1-2-1: Interruption requirement applicability
  FFS:
    Option 1 (MTK, Huawei, OPPO, NEC, Xiaomi): The interruption requirement should base on the band combination capability reporting by UE.
    Option 1a: The interruption requirement should base on the band combination capability (indicated by txSwitchImpactToRx or txSwitchWithAnotherBand) reporting by UE.
    Option 2 (Huawei (observation 1), Nokia (proposal 5), NEC, Apple, vivo, CATT, QC): For the interruption cause by the switching period, whether the victim CCs are same as those indicated by the IEs (txSwitchImpactToRx or txSwitchWithAnotherBand) needs further discussion.
    Option 3 (Ericsson): Needs further checking and discussion.
Issue 1-2-2: Victim cell type impacted by SRS antenna port switching
  Agreement:
    In the R17 FeRRM WI only RRM requirement of NR SRS antenna port switching would be discussed, including following cases (but all the victim CCs shall be determined by the conclusion in issue 1-2-1):
      NR SRS antenna port switching impacting LTE CC
      NR SRS antenna port switching impacting NR CC
Issue 1-2-3: whether same interruption requirement applies to different SRS antenna port switching patterns
  FFS:
    Option 1 (vivo, OPPO, NEC, Apple, Xiaomi, Intel, CATT, QC): use same set of requirements for different SRS antenna switch patterns
    Option 2 (LGE): Depending on UE capability supportedSRS-TxPortSwitch, the interruption requirements should be defined.
    Option 3 (Ericsson, MTK, Nokia): further discussion is needed.

## Slide 5: Sub-topic 1-3: Interruption requirement design (1/5)
Issue 1-3-1: The interruption requirement is defined based on slot level or symbol level
  FFS:
    Option 1 (Apple, QC, MTK, Huawei, OPPO, Xiaomi, vivo, CATT, Intel): based on slot level
    Option 2 (LGE, NEC, Intel, Huawei, Ericsson): based on symbol level
    Option 3 (Nokia, CMCC): FFS
Issue 1-3-2: The components within interruption time of SRS antenna port switching in FR1
  FFS:
    Option 1 (Xiaomi, MTK, vivo, Huawei, OPPO, LG, Intel, CATT): includes antenna switching time and SRS transmission time
    Option 1a (QC, NEC): includes antenna switching time and SRS transmission time; and transient periods before and after SRS transmission slot have to be taken into consideration.
    Option 1b (Ericsson, Xiaomi, NEC): includes antenna switching time and SRS transmission time; and other components can be further discussed.
    Option 2 (Ericsson): FFS on followings
      FFS: time to switch to transmit,
      FFS: time to switch back,
      FFS: guard symbol(s),
      FFS: SRS transmission.
    Option 3 (Apple, Nokia): only antenna switching time
      If the transient period (15us) can be captured within the guard period in FR1, the UL interruption at SRS antenna switching shall be defined based on the minimum guard period specified in RAN1

## Slide 6: Sub-topic 1-3: Interruption requirement design (2/5)
Issue 1-3-3: if option 1 is adopted in issue 1-3-2, details of the interruption time in FR1
  FFS:
    Option 1 (NEC, LG,):
      Interruption time for SRS antenna port switching when the SRS resource transmission in the SRS resource set is in same slot is (nrofSymbols+2+Y) OFDM symbols. Where nrofSymbols is the number of SRS symbols in the SRS transmission during SRS antenna switching and Y is the minimum guard period between two SRS resources of an SRS resource set for antenna switching.
      Interruption time due to SRS antenna port switching when the SRS resources in a resource set are not in same slot are (nrofSymbols +2) OFDM symbols. Where nrofSymbols is the number of SRS symbols in the SRS transmission during SRS antenna switching.
    Option 2 (MTK, OPPO, CATT): The SRS antenna switching interruption time should be
      (A) SRS Transmission time (up to 6 symbols).
      (B) 2 * 15us (The SRS antenna switching time is 15us)
    Option 3 (Xiaomi, Apple, vivo, MTK, Nokia): Wait the conclusion from issue 1-3-2
    Option 4 (QC): SRS transmission time (up to 7 symbols) + 10us*2 transient period
Issue 1-3-4: The components within interruption time of SRS antenna port switching in FR2
  FFS:
    Option 1 (Xiaomi): The total interruption time of SRS antenna switching for MPUE would comprise of panel switching time, panel activation time and SRS transmission time.
    Option 2 (Intel): Clarify that current SRS antenna switching time of 15us is applied for FR2 case where SRS antenna switch in the same panel. For the case that SRS antenna switching happens between different panels for FR2, it needs further discussion whether extra ramp up timing for other antennas are needed.
    Option 3 (MTK (proposal 3)): includes antenna switching time and SRS transmission time.
    Option 4 (OPPO, NEC, Apple, Xiaomi, vivo, Intel, CATT, QC, MTK, Nokia): Wait the conclusion from issue 1-1-4

## Slide 7: Sub-topic 1-3: Interruption requirement design (3/5)
Issue 1-3-5: Would the interruption requirement based on different SCS?
  FFS:
    Option 1 (Apple, Huawei): Interruption requirement is based on the victim CC SCS.
    Option 2 (QC, MTK, vivo, OPPO, LG, Intel, CATT): Interruption requirement is based on the aggressor CC and victim CC SCS.
    Option 3 (Ericsson, Apple, Xiaomi, Nokia, Intel, CATT):
      The interruption requirement depends at least on the SCS of the victim cell.
      FFS: the interruption requirement depends on the SCS of aggressor cell.
    Agreement: Option 3. (moderator: please companies comment if this is agreeable or not)
Issue 1-3-6: Would the interruption requirement differentiate between sync and async cases?
  FFS:
    Option 1 (Apple, QC, MTK, OPPO, Xiaomi): No; based on the async case for the minimum requirement.
    Option 2 (LGE, CATT, Ericsson, Nokia): Yes.
    Option 3 (Huawei, Nokia?): depends on whether to have slot level interruption or symbol level interruption. Need FFS.
Issue 1-3-7: Interruption requirement for UE with or without per-FR MG capability
  FFS:
    Option 1 (Apple):
      For UE capable of per-FR MG, the interruption is only allowed to a victim serving CC if NR SRS antenna port switching happens in the same FR as this victim serving CC.
      For UE not capable of per-FR MG, the interruption is always allowed to a victim serving CC regardless of whether NR SRS antenna port switching happens in the same FR as this victim serving CC.
    Option 2 (MTK, Huawei, Xiaomi, CATT, Apple): No need to define the UE (not) capable of per-FR gaps requirement for SRS antenna port switching in RAN4.
    Option 3 (OPPO, QC, Ericsson, Nokia): FFS after addressing other issues

## Slide 8: Sub-topic 1-3: Interruption requirement design (4/5)
Issue 1-3-8: Interruption requirement proposals
  FFS:
    Option 1 (Apple):
      if NR SRS antenna switching causes interruption to LTE serving CC, the interruption is 2 subframes; while if NR SRS antenna switching causes interruption to NR serving CC, the interruption is 2 slots based on the SCS of the victim CC.
    Option 2 (QC, OPPO):
      SRS antenna switch interruption is specified as the following table for NR SA. In EN-DC, interruption on LTE carrier is the same as victim SCS = 15kHz case in NR SA.
    Option 3 (MTK):
      The SRS antenna switching interruption requirement is shown as follow.
 | Interruption Length (slots) |  | 
Victim SCS (kHz) | 15 | 30 | 60
15 | 2 | 2 | 2
30 | 3 | 2 | 2
60 | 4 | 3 | 2
Victim cell SCS(KHz) | Aggressor Cell SCS (KHz) |  |  | 
 | 15 | 30 | 60 | 120
15 | 2 | 2 | 2 | 2
30 | 2 | 2 | 2 | 2
60 | 3 | 2 | 2 | 2
120 | 5 | 3 | 3 | 2

## Slide 9: Sub-topic 1-3: Interruption requirement design (5/5)
(cont. from last slide) Issue 1-3-8: Interruption requirement proposals
  FFS:
    Option 4 (Intel):
      1 additional OFDM symbol shall be added to the impacted DL interruption. The interruption length is 2 symbols for SCS=15KHz/30KHz/60KHz case and 3 symbols for SCS=120KHz case.
    Option 5 (NEC):
      Interruption time for SRS antenna port switching when the SRS resource transmission in the SRS resource set is in same slot is (nrofSymbols+2+Y) OFDM symbols. Where nrofSymbols is the number of SRS symbols in the SRS transmission during SRS antenna switching and Y is the minimum guard period between two SRS resources of an SRS resource set for antenna switching.
      Interruption time due to SRS antenna port switching when the SRS resources in a resource set are not in same slot are (nrofSymbols +2) OFDM symbols. Where nrofSymbols is the number of SRS symbols in the SRS transmission during SRS antenna switching.
    Option 6 (Apple, Xiaomi, vivo, Intel, CATT, QC, Ericsson, MTK, Nokia, LG): Need to wait for the conclusions from previous issues

## Slide 10: Sub-topic 1-4: LS to RAN1 for clarification
Issue 1-4: LS to RAN1
  FFS:
    Option 1 (Nokia): Send LS to RAN1 clarifying the following questions on the applicability of guard period:
      Does the guard period apply only if the SRS resources of a set are transmitted in the same slot i.e., if it applies if SRS resources of a set are transmitted in different slots?
      Does the guard period apply in the case of non-consecutive SRS switching i.e. if the SRS resources of a set are separated by more than one OFDM symbols in FR1?