## Slide 1: GTW topics for the study on enhanced test methods for FR2
Apple
3GPP TSG-RAN WG4 Meeting #98-e
Electronic Meeting, 25 January – 5 February, 2021
Agenda Item: 12.1.1
Draft R4-21xxxxx

## Slide 2: Key topics to conclude during RAN4 #98
High DL power / low UL power: applicability of the DNF system
ETC impact on test system
Test time reduction: prioritization of candidate solutions
Check status of TPs
Remaining issues with the TPMI method
Band n262 testability

## Slide 3: High DL power / low UL power: applicability of the DNF system
Summary of options to conclude the applicability of the DNF system:
  Option 1: With the considered UE models (arrays on a phone size ground plane), figure of merits such as EIRP, TRP, and Spherical Coverage are not influenced dramatically from range length especially if the dynamic beam scenarios is considered
  Option 2: DNF method may be possible for single panel UE (single panel per band) with the antenna panel offset declaration. For multi-panel UE (multi-panel per band), it seems complicated manufacture declaration is needed for path loss compensation
  Option 3: DNF is not suitable for spherical coverage and beam peak searches (for more information, see applicability discussion above). We should instead focus on CFFNF and CFFDNF instead
  Option 4:
    Beam peak searches and spherical coverage test cases are not applicable regardless of black-box or black&white-box approach. Performing these tests with the NF measurement probe would require the extensive black&white-box approach which is not deemed a feasible enhancement of the methodology.
    The low UL power/high DL power EIRP/EIS test cases in the known FF BP direction as well as spherical coverage and beam peak search are not applicable to the black box approach.
    The applicability of the low UL power/high DL power EIRP/EIS test cases in the known BP direction and with the black&white-box approach is FFS.
  Option 5:
    Beam peak searches and spherical coverage test cases are not applicable to black-box. For black&white-box approach, performing these tests with DNF would require the antenna array panel offset to be declared. This could be seen complex in case of multi-panel UE (multi-panel per band)
    The low UL power/high DL power EIRP/EIS test cases in the known FF BP direction as well as spherical coverage and beam peak search are not applicable to the black box approach.
    The applicability of the low UL power/high DL power EIRP/EIS test cases in the known BP direction and with the black&white-box approach is FFS.
  Option 6:
    Capture DNF for Beam peak searches and spherical coverage test cases in TR, meanwhile such method is not RAN4 recommendation
Proposal:
  Option 4 is agreed with a view toward resolving the FFS by the next meeting
  Adopt option 4 as RAN4 conclusion meanwhile capture DNF for Beam peak searches and spherical coverage test cases into TR
Notes: MVG : We proposed option 5, based on the evaluations, we understand DNF need to work with manufacture declaration. Even it’s difficult, but still a technical feasible solution.
Keysight: For beam peak search and spherical coverage, DNF required complexed solution. Too many limitation for the usage of such methodology, we would like to have a common acceptable methodology with reasonable performance.
R&S: Share similar view as Keysight.
Apple: Document the extensive declaration approach, and how DNF workable.

## Slide 4: ETC impact on test system
EIRP/EIS beam peak searching procedure under ETC:
  Option 1: perform 3D scan
  Note : option 2 is not roubust enough for UE which with multi-panels
  Option 2: beam peak search within a certain cone of directions around peak position under NTC (by declaration or NTC peak searching results)
  -> If UE support the declaration of option 2, then option 2 can apply for such UE; otherwise option 1 will be applied for testing.
  -> By default, option 1 applied; if declaration present from UE vendor, then option 2 applied.
  Note: option1 is needed for UE with best antenna pannel switch based on temperature and/or UE without declaration present (Further work on the texts into TR if needed)
RAN4 agrees to define a temperature tolerance for FR2 ETC system. Several aspects need to consider:
  an accuracy of temperature control by an air conditioner
  accuracy of a thermocouple to measure a temperature in the ETC enclosure
  temperature deviation at the center of the QZ
The value of temperature tolerance is FFS.
  [+/- 4] degrees Celsius tolerance is the starting point
  Test only can be executed under target temperature within the tolerance
  Test equipment vendors are encouraged to share thermal regulation schemes and anticipated thermal regulation capabilities. Examples:
    How much heat can be extracted at each temperature (W)
    How to ensure heat transfer coefficient of DUT is high enough in all orientations
    Treatment to accommodate non hand-held form factors
Notes: Keysight: Option 1 should be baseline.
QC: Same view as Keysight. Option2 should be declaration basis.
vivo: Prefer option 2 as baseline to save test time.
Samsung: Similar view as vivo. The derivation between ETC and NTC should be within a small value.
Apple: The MU and the beam peak difference should be clarified first.
Anristu: We think either option 1 or option2 fine for us.
QC: option 2 only robust for single panel UE, for multi-panel UE, that’s questionable.
Keysight: ETC test is black box testing, MU not a issue in our view.
If UE declaration for option 2, then test with option 2 , otherwise option 1 applied.

## Slide 5: Test time reduction: prioritization of candidate solutions
Background
  6 test time reduction options were documented at the outcome of RAN4 #97 [R4-2017597]
  4 new options were proposed in the first round of RAN4 #98 discussions [R4-2103769]
  WF discussions during the second round organized the options as follows:
    1-MG
    2-RSRP
    3-Single Pollink
    4-Others
Proposal:
  Options 1-MG, 2-RSRP, and 3-Single Pollink are prioritized in the study, and their completion can conclude the test time reduction objective
  Work on 4-Others, including potential new options, is not precluded

## Slide 6: Check status of TPs
[R4-2103966] Low UL Power/High DL Power Test Cases (Keysight, R&S)
  Trending toward agreeable? Key issues?
[R4-2103967] polarization basis mismatch (vivo)
  Trending toward agreeable? Key issues?
[R4-2103968] TP to TR 38.884 on Inter-band DL CA in FR2 (Anritsu)
  Trending toward agreeable? Key issues?

## Slide 7: Remaining issues with the TPMI method
Detailed TPMI method enhancement coverage is FFS
  if TPMI method is applicable for clause 6.2 of TS38.101-2, then 2 port SRS (nrofSRS-Ports = 2) shall be configured
Which TPMI index per test AoA shall be sent by TE is FFS
  Option1: Fixed TPMI index
  Option2: Optimal TPMI index
    Option2-A: TE to configure the UE with SRS resources at each grid point
    Option2-B: TE simply try out all TPMIs and choose best one
  UE vendors are encouraged to study the UE EIRP performance delta between Option1 and Option2
  TE vendors are encouraged to study the feasibility/pros/cons of Option2-A/B compared to Option1
TPMI method enhancement coverage | clause 6.2 of TS38.101-2 (Transmitter power) | Clause 6.1, 6.3 to 6.6 of TS38.101-2 (other Transmitter characteristics)
Rel-15 nonCoherent UEs | No | No
Rel-15 coherent UEs | [Yes] | [Yes]
Rel-16 nonCoherent UEs | No | No
Rel-16 coherent UEs | [Yes] | [Yes]
Rel-16 nonCoherent UEs which support uplink full power transmission | [Yes] | [Yes]

## Slide 8: Band n262 testability
Quality of quiet zone MU at 49 GHz
  Option 1: The QoQZ MUs at 49 GHz are within the example MU value defined in RAN5
    No increase in QoQZ MU is expected necessary for 49 GHz
  Option 2: Make the following changes to the “Multiple antenna” MU element:
    MU element description
    The applicability
    Potentially the MU element sample value
Proposal:
  The two options are not mutually exclusive and can be agreed Companeis are encouraged to bring analysis for band n262 testability.